MODEL CA1020 SERIES

PARTS CATALOG

Aug. 2006

Vehicle Specifications

| Production name | CA1020VR Series FAW MINI TRUCK |
| --- | --- |
| DIMENSIONS |
| Exterior dimensions(L×W×H) mm | 3998×1475×1890 |
| Wheel base mm | 2550 |
| Treads(F/R) mm | 1280/1290 |
| Ground clearance mm | 156(rear axle shaft tube) |
| Seating capacity persons | 2 |
| Max. Speed Km/h | 100(970cc) |
| Max. gradability % | 29 |
| Angles(Approach/Departure) | 27.°/ 29° |
| Brake distance at 80 Km/h m | <57.2 |
| Turning circles semi-meters m | 5 |
| Fuel consumption at L/100Km | 6.0(50Km/h) |
| MODEL | CA1020VR |
| WEIGHT |
| Curb vehicle weight Kg | 970 |
| Gross vehicle weight Kg | 1795 |
| Weight distribution(loaded) Kg | 665kg/1130kg |
| Weight distribution (unloaded) Kg | 495kg/475Kg |
| ENGINE |  |
| Model,Cylinders | JB465QE1,L4,OHC，EFI |
| Displacement ml/fuel | 970/Gasoline |
| Bore×Stroke mm×mm | 65.5×72 |
| Compression ratio | 8.8 |
| Max.Power W(r/min) | 35.5（5200） |
| Max.torque N.m(r/min) | 74（3000-3500） |
| TRANSIMISSION |
| Type | 5MT,synchromesh |
| Gear tatio 1st | 3.505 |
| 2nd | 2.043 |
| 3rd | 1.383 |
| 4th | 1 |
| 5th | 0.806 |
| Reverse | 3.536 |
| Final gear ratio | 5.125 |
| Clutch system | Single-plate,Diaphragm spring clutch |
| CHASSIS |
| Steering | Rack & pinion |
| Braking system | Dual hydraulic brake system,Disc brake(F),Drum brake(R) |
| Suspension | Front | Strut & Coil spring |
|  | Rear | Semi-oval leaf spring |
| Drive train | 4×2MR 5.125 |
| Tires size | 165/70 R13 |
| CAPACITY |
| Fuel tank capacity litre | 40 |

Recommedation Class

In this catalogue, the pattern of consumption and replacement of spare parts are different by items

| Class No. | Definition |
| --- | --- |
| A | Inspection or replacement pediodically or compulsory maintenance parts |
| B | Collision trim parts,Lamp, Mirror,glass, etc. |
| C | Fast moving parts,Bearing,bulb,seal, decrations |
| D | Body Welded parts,bolt,other parts not in common use |

General  Index

Engine Mechanical

| Section name | Section No. | Page |  | Section name | Section No. | Page |
| --- | --- | --- | --- | --- | --- | --- |
| Engine Assembly | 01-1000 | 1-2 |  | Generator | 01-1015 | 33-34 |
| PCV Value | 01-1001 | 3-4 |  | Starter | 01-1016 | 35-36 |
| Engine Front , Rear supporting bracket | 01-1002 | 5-6 |  | Fuel and Engine Control |
| Engine Front , Rear Mounting Cushion | 01-1002 | 7-8 |  |  |
| Piston and Crankshaft | 01-1003 | 9-10 |  |  |
| Engine Oil Filter and Oil Pump | 01-1004 | 11-12 |  | Section name | Section No. | Page |
| Oil pan | 01-1005 | 13-14 |  | Fuel filter and interrelated hoses | 01-1105 | 37-38 |
| Intake manifold | 01-1006 | 15-16 |  | Fuel tank and fuel pump | 01-1106 | 39-40 |
| Thermostat and interrelated hoses | 01-1007 | 17-18 |  | Carbon canister | 01-1130 | 41-42 |
| Exhaust manifold | 01-1008 | 19-20 |  | Air filter | 01-1109 | 43-44 |
| Cylinder head | 01-1009 | 21-22 |  | Cooling & Exhaust |
| Cylinder block | 01-1010 | 23-24 |  |  |
| Water pump and fan | 01-1011 | 25-26 |  |  |
| Camshaft throttle and bock arm | 01-1012 | 27-28 |  | Section name | Section No. | Page |
| Timing belt and front and rear cover of engine | 01-1013 | 29-30 |  | Muffler welding assembly and catalytic converter | 01-1201 | 45-46 |
|  |  |  |  | Radiator assy | 01-1301 | 47-48 |
| Engine Electrical |  |  |  |  |
| Section name | Section No. | Page |  |  |  |  |
| Engine fuel injection hardness, sensors and throttle body | 01-1014 | 31-32 |  |  |  |  |

Power Train

| Section name | Section No. | Page |  | Section name | Section No. | Page |
| --- | --- | --- | --- | --- | --- | --- |
| Throttle cable and clutch cable | 02-1108 | 49-50 |  | Steering Wheel | 03-3402 | 91-92 |
| Brake clutch and accelerator pedal | 02-1602 | 51-52 |  | Steering shaft | 03-3404 | 93-94 |
| Transmission assembly | 02-1700 | 53-54 |  | Section name | Section No. | Page |
| Transmission case and cover | 02-1701 | 55-56 |  | Brake |
| Transmission Gear | 02-1701-1 | 57-58 |  |  |
| Transmission Gear | 02-1701-2 | 59-60 |  |  |
| Shifting Mechanism(lever & fork) | 02-1702 | 61-62 |  | Front Brake Disc | 04-3501 | 95-96 |
| Clutch cover, Disc & Release parts | 02-1602 | 63-64 |  | Rear brake Drum | 04-3502 | 97-98 |
| Transmission shift lever & control linkage | 02-1703-1 | 65-66 |  | Brake piping and control | 04-3506 | 99-100 |
| Transmission shift lever & control linkage | 02-1703-2 | 67-68 |  | Brake master cylinder,vacuum booster | 04-3506 | 101-102 |
| Propeller Shaft | 02-2201 | 69-70 |  | Parking brake control | 04-3508 | 103-104 |
| Front shock absorber with coil spring assembly | 02-2901 | 71-72 |  | Section name | Section No. | Page |
|  |  |  |  | Body Electrical |
| Middle arm welding assembly,front suspension | 02-2904-1 02-2904-2 | 73-74 75-76 |  |  |
| Rear Axle Housing And Half Axle | 02-2401 | 77-78 |  | Lamps,speaker,battery & relay | 05-3711-1 05-3711-2 | 105-106 107-108 |
| Final drive assembly | 02-2402-1 02-2402-2 | 79-80 81-82 |  | Windshield Wiper | 05-5205 | 109-110 |
|  |  |  |  | Wiring harness | 05-3724 | 111-112 |
| Rear leaf spring assembly | 02-2912 | 83-84 |  | Heater Unit | 05-8101 | 113-114 |
| Wheel and Tyre | 02-3101 | 85-86 |  | Nozzle&Duct-Ventilation,defroster | 05-8102 | 115-116 |
| Spare wheel bracket -hanger | 02-3105 | 87-88 |  |  |  | 117-118 119-120 |
| Section name | Section No. | Page |  |  |  |  |
| Steering |  | Switch unit, A/c & heater | 05-8112 | 121-122 |
| Steering Gear Box | 03-3401 | 89-90 |  |  |  |  |

Body

| Section name | Section No. | Page |  | Section name | Section No. | Page |
| --- | --- | --- | --- | --- | --- | --- |
| Instrument Panel, Pad,fitting | 06-5310 | 123-124 |  | Middle chassis Frame-CA1020V | 06-2801 | 173-174 |
| Vice Instrument Panel | 06-5305 | 125-126 |  | Middle chassis Frame-CA1020VR | 06-2801 | 175-176 |
| Front Door welded Panel & fitting | 06-6100-1 06-6100-2 | 127-128 129-130 |  | Cover-Frame-CA1020V | 06-2801 | 177-178 |
|  |  |  |  | Cover-Frame-CA1020VR(L) | 06-2801 | 179-180 |
| Front Door Glass Lifter | 06-6104 | 131-132 |  | Rear welding floor –Frame-CA1020V | 06-5101 | 181-182 |
| Front door lock | 06-6105 | 133-134 |  | Rear welding floor–Frame-CA1020VR(L) | 06-5101 | 183-184 |
| Front door gemel | 06-6200 | 135-136 |  | Front welded panel parts-Frame | 06-5301 | 185-186 |
|  |  |  |  | Side panel welded parts | 06-5401-1 | 187-194 |
| Rear door | 06-6203 | 137-138 |  | Front welded floor parts-Frame | 06-5101 | 195-196 |
| Rear Door Lifter | 06-6203 | 139-140 |  |  |  |  |
| Rear Door Lock Mechanism | 06-6300 | 141-142 |  | Truck bed | 06-5101 | 197-202 |
|  |  |  |  | Section name | Section No. | Page |
| Driver’s Seat | 06-6800 | 147-148 |  | Miscellaneous |
| Rear Seat | 06-7200 | 149-150 |  |  |
| Driver seat belt | 06-8212 | 151-152 |  |  |
| Front & Rear Bumper | 06-2803 | 153-154 |  | Brand & Logo | 07-3921 | 203-204 |
| Heat insulating lining, engine house | 06-5107 | 155-156 |  | Key Set & Blank Key | 07-3704 | 205-206 |
| Battery cover Carpet | 06-5107 06-5109 | 157-158 159-160 |  | Tool Kit | 07-3919 | 207-208 |
| Front windshield | 06-5206 | 161-162 |  |  |  |  |
| Top cover | 06-5702 | 163-164 |  |  |  |  |
| Rear chassis Frame-1020V | 06-2801 | 165-166 |  |  |  |  |
| Rear chassis Frame-1020VR | 06-2801 | 167-168 |  |  |
| Rear chassis Frame-1020VRL | 06-2801 | 169-170 |  |  |
| Front chassis Frame | 06-2801 | 171-172 |  |  |  |  |

| ENGINE MECHANICAL—ENGINE ASSEMBLY | SECTION. NO.:01-1000 | PAGE:1 |
| --- | --- | --- |
| ENGINE MECHANICAL—ENGINE ASSEMBLY | SECTION. NO.:01-1000 | PAGE:2 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 01 | 1000940D2E2 | 发动机带变速箱总成，1051cc, | Engine and transmission assy 1051cc | 1 |  | D |  | LIUJI |
| 1 |  |  |  |  | 1 |  | D |  | LIUJI |
| 2 | 01 | JB465Q-1AE1 | 发动机总成，1051cc, | Engine assy. (1051cc) | 1 | Двигатель в сборе | D |  | LIUJI |
| ENGINE MECHANICAL—PCV VALUE | SECTION. NO.:01-1001 | PAGE:3 |
| ENGINE MECHANICAL—PCV VALUE | SECTION. NO.:01-1001 | PAGE:4 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O2 | K-1000016J | 曲轴箱通风管 | Crankcase ventilation hose,pipe to air clear | 1 |  | C | JB465Q-1AE1,only | 10510cc |
| 2 | O1 | J-1003067A | 曲轴箱通风管Ι | Crankcase ventilation hose,pipe to cylinder head | 1 |  | C | For all |  |
| 3 | O1 | ZBT32005.1-88（ф22） | 环箍（ф22） | CLAMP RINGф22-HOSE | 4 |  | C | For all |  |
| 4 | O1 | B-1-1003065DJ | 三通管 | THREE WAY PIPE | 1 |  | D | For all |  |
| 5 | O1 | A-1003068D | PCV 阀通气管 | PCV VALVE PIPE | 1 |  | C | For all |  |
| 6 | O1 | B-1-1000074DB | 环箍（ф16） | CLAMPф16 | 2 |  | C | For all |  |
| 7 | O1 | B-1-1008041D | PCV 阀 | PCV VALVE | 1 | Датчик температуры | C | For all |  |
| ENGINE MECHANICAL—Engine Front , Rear supporting bracket | SECTION. NO.:01-1002A | PAGE:5 |
| ENGINE MECHANICAL—Engine Front , Rear supporting bracket | SECTION. NO.:01-1002A | PAGE:6 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 1001011-2E2 | 发动机左支架 | Left Supporting Bracket -Engnine | 1 |  | D |  |  |
| 2 |  | Q151C1030 | 螺栓 | Bolt | 3 |  | D |  |  |
| 3 |  | Q40310 | 弹簧垫圈 | Spring Waeher | 3 |  | C |  |  |
| 4 |  | Q40110 | 平垫圈 | Flat Washer | 3 |  | D |  |  |
| 5 |  | 1001020-2E2 | 发动机右支架总成 | Right Supporting Bracket- Engnine | 1 |  | D |  |  |
| 6 |  | Q151C1030 | 螺栓 | Bolt | 3 |  | D |  |  |
| 7 |  | Q40310 | 弹簧垫圈 | Spring Waeher | 3 |  | D |  |  |
| 8 |  | Q40110 | 平垫圈 | Flat Washer | 3 |  | C |  |  |
| 9 |  | Q151C1090 | 螺栓 | Bolt | 2 |  | D |  |  |
| 10 |  | Q361C10 | 螺母 | Nut | 2 |  | D |  |  |
| 11 |  | Q40310 | 弹簧垫圈 | Spring Waeher | 2 |  | D |  |  |
| 12 |  | Q40110 | 平垫圈 | Flat Washer | 4 |  | D |  |  |
| 13 |  | 1001031-2E2 | 发动机后支架 | Rear Supporting Bracket Engnine | 1 |  | D |  |  |
| 14 |  | Q1460825 | 组合螺栓 | Combined Bolt | 2 |  | D |  |  |
| 15 |  | Q151C1090 | 螺栓 | Bolt | 1 |  | D |  |  |
| 16 |  | Q361C10 | 螺母 | Nut | 1 |  | D |  |  |
| 17 |  | Q40310 | 弹簧垫圈 | Spring Waeher | 1 |  | D |  |  |
| 18 |  | Q40110 | 平垫圈 | Flat Washer | 2 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—Engine Front , Rear Mounting Cushion | SECTION. NO.:01-1002B | PAGE:7 |
| ENGINE MECHANICAL—Engine Front , Rear Mounting Cushion | SECTION. NO.:01-1002B | PAGE:8 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 0 |  | L-1001011J | 悬挂挡板 | Shield Plate, Mounting | 2 |  | D |  |  |
| 1 |  | M-1001027 | 左悬挂架总成 | Mounting Bracket Assy, Lh | 1 | Кронштейн двигателя с подушкой левый | C |  |  |
| 2 |  | M-1001010 | 右悬挂架总成 | Mounting Bracket Assy, Rh | 1 | Кронштейн двигателя с подушкой левый | C |  |  |
| 3 | 1 | N-1001039 | 后悬挂组件 | Rear Hanger | 1 | Кронштейн с подушкой двигателя задний | C |  |  |
| 4 |  | M8*30(GB9074.17-88) | 组合螺栓 | Combined Bolt | 1 |  | D |  |  |
| 5 |  | M8*25(GB9074.17-88) | 组合螺栓 | Combined Bolt | 3 |  | D |  |  |
| 6 |  | M8*20(GB9074.17-88) | 组合螺栓 | Combined Bolt | 4 |  | D |  |  |
| 7 |  | L-1001021J | 发动机前悬挂软垫 | Engine Front Mounting Cushion Assembly | 3 | Подушка кронштейнов двигателя | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—Piston and Crankshaft | SECTION. NO.:01-1003 | PAGE: 9 |
| ENGINE MECHANICAL—Piston and Crankshaft | SECTION. NO.:01-1003 | PAGE:10 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O2 | J-1004027 | 活塞环组件 | THE 1ST PISTON RING | 4set | Кольцо поршневое 1поршень | C | all engine |  |
|  | O3 | H-1004028 | 活塞 | PISTON | 4 | поршень | C | 1051cc engine |  |
| 3 | O2 | J-1004021 | 活塞销 | PISTON PIN | 4 | Палец поршневой | D | all engine |  |
| 4 | O1 | B-1-1004022D | 活塞销卡环 | CLAMP RING, PISTON PIN | 8 | Кольцо стопорное поршневого пальца | D | all engine |  |
| 5 | O2 | H-1004011 | 连杆总成 | CONNECTING ROD ASSY | 4 | Шатун в сборе 1 шатун | C | 1051cc engine |  |
| 6,7 | O1 | B-1-1004015\12D | 连杆螺栓\螺母 | BOLT /NUT | 8set |  | D | all engine |  |
| 8 | O1 | B-1-1004014D | 连杆瓦 | BEARING，CONNECTING ROD | 4set | Вкладыши шатунные 1 шейка | C | all engine |  |
| 9 | O2 | H-1005022 | 曲轴 | CRANKSHAFT | 1 | Вал коленчатый | D | 1051cc engine |  |
| 10 | O1 | B-1-1002021D | 主轴瓦 | MAIN BEARING | 4 set | Вкладыши коренные | C | all engine |  |
| 11 | O1 | B-1-1000047DA | 曲轴止推片 | THRUST PLATE, CRANKSHAFT | 2 | Полукольцо осевого смещения (2шт) | C | all engine |  |
| 12 | O1 | B-1-1011016D | 曲轴前油封 | CRANKSHAFT, FRONT OIL SEAL ASSY | 1 | Сальник коленвала передний | C | all engine |  |
| 13 | O2 | J-1000024 | 曲轴正时皮带轮挡片 | SHIELD SLICE | 1 |  | D | all engine |  |
| 14 | O1 | J-1000048 | 曲轴正时皮带轮 | TIMING GEAR ，CRANKSHAFT | 1 | Шестерня коленвала | D | all engine |  |
| 15 | O1 | GB1099-79（5X19） | 半圆键 | KEY 5*19 | 1 |  | D | all engine |  |
| 16 | O1 | J-1000049J | 主动皮带轮 | PULLEY | 1 | Шкив коленвала | D | all engine |  |
| 18 | O1 | B-1-1002022D | 曲轴后油封 | REAR OIL SEAL ASSY ，CRANKSHAFT | 1 | Сальник коленвала задний | C | all engine |  |
| 19 | O1 | B-1-1002030D | 曲轴后端盖密封垫 | WASHER | 1 | Прокладка задней крышки коленвала | C | all engine |  |
| 20 | O1 | B-1-1002020D | 曲轴后端盖 | REAR COVER,CRANKSHAFT | 1 | Крышка коленвала задняя | D | all engine |  |
| 21 | O1 | B-1-1000082D | 曲轴后端盖螺栓 | BOLT | 2 |  | D | all engine |  |
| 22 | O1 | B-1-1000081D | 曲轴后端盖螺栓 | SEAL GASKET | 4 |  | D | all engine |  |
| 23 | O1 | B-1-1000014D | 定位套 | LOCATION SLEEVE | 2 |  | D | all engine |  |
| 24 | O1 | B-1-1004018DA | 活塞销衬套 | PISTON PIN SLEEVE | 4 |  | C | all engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—Engine Oil Filter and Oil Pump | SECTION. NO.: 01-1004 | PAGE:11 |
| ENGINE MECHANICAL—Engine Oil Filter and Oil Pump | SECTION. NO.:01-1004 | PAGE:12 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | B-1-1012010DB | 机油滤清器 | ENGINE OIL FILTER ASSY | 1 | Фильтр маслянный | A | All |  |
| 2 |  | B-1-1000084D | 螺栓（M6X35） | BOLT | 5 |  | D | All |  |
| 3 |  | B-1-1000085D | 螺栓（M6X40） | BOLT | 2 |  | D | All |  |
| 4 |  | B-1-1000083D | 螺栓（M6X3） | BOLT | 1 |  | D | All |  |
| 5 |  | B-1-1000014D | 机油泵定位套 | LOCATION SLEEVE | 2 |  | D | All |  |
| 6 |  | B-1-1011010D | 机油泵 | OIL PUMP | 1 | Насос маслянный | D | All |  |
| 7 |  | B-1-1000051DA | 机油泵垫 | GASKET, OIL PUMP | 1 | Прокладка маслянного насоса | C | All |  |
| 8 |  | B-1-1012031D | 机油滤清器连接管 | CONNECTING PIPE | 1 | Штуцер маслянного фильтра | D | All |  |
| 9 |  | B-1-3810010D | 机油压力传感器 | OIL PRESSURE SENSOR | 1 | Датчик маслянный | C | All |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—OIL PAN | SECTION. NO.:01-1005 | PAGE:13 |
| ENGINE MECHANICAL—OIL PAN | SECTION. NO.:01-1005 | PAGE:14 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 02 | H-1009010J | 机油盘 | OIL PAN ASSY | 1 | Картер маслянный | D | 1051cc engine |  |
| 2 | 01 | B-1-1000064D | 机油盘密封垫 | GASKET，OIL PAN | 1 | Прокладка поддона | B | all engine |  |
| 4 | 01 | B-1-1009018D | 机油盘放油锣塞 | SCREW PLUG, OIL DRAIN | 1 | Пробка сливная | D | all engine |  |
| 5 | 01 | B-1-1009017DB | 放油锣塞密封垫 | SEAL WASHER， SCREW PLUG | 1 |  | B | all engine |  |
| 6 | 01 | B-1-1010010D | 机油集滤器 | OIL PICK-UP TUBR | 1 | маслоприемник | D | all engine |  |
| 7 | 01 | B-1-1002031 | “O”型密封圈 | O-SHAPE SEAL RING | 1 | Кольцо уплотнительное маслоприемника | C | all engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—INTAKE MANIFOLD | SECTION. NO.:01-1006 | PAGE:15 |
| ENGINE MECHANICAL—INTAKE MANIFOLD | SECTION. NO.:01-1006 | PAGE:16 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | Remark |
| 1 | 01 | A-1008045DJ | 进气压力传感器支架 | BRACKET,INTAKE PRESSURE SENSOR | 1 |  | D | All engine |  |
| 2 | 02 | K-1008044 | 进气歧管支架 | BRACKET,INTAKE MANIFOLD | 1 |  | D | 1051cc engine |  |
| 5 | 01 | K-1000022 | 节流阀体密封垫 | SEAL WASHER, THROTTLE CHAMBER | 1 |  | Ｃ | All engine |  |
| 6 | 01 | A-1008047DJ | 碳罐电磁开关通气管 | Ventilated pipe , in touch with electromagnetism switch of carbon tank | 1 |  | C | All engine |  |
| 7 | 01 | B-1-1000074DB | 管夹子 | CLIP | 2 |  | C | All engine |  |
| 8 | 01 | B-1-1000080D | 螺栓 | BOLT | 1 |  | D | All engine |  |
| 9 | 01 | A-1008046DA | 碳罐清洗电磁开关支架 | BRAKET | 1 |  | D | All engine |  |
| 10 | 01 | 276Q-23501A | 真空连接管 | VACUUM CONNECT ING PIPE | 1 |  | C | All engine |  |
| 11 | 01 | B-1-1000091D | 进气歧管连接螺栓 | BOLT | 3 |  | D | All engine |  |
| 12 | 01 | B-1-1000091D | 油轨固定螺栓 | BOLT | 2 |  | D | All engine |  |
| 13 | 01 | GB6170-86/GB93-87（M8） | 螺母/螺栓（M8） | NUT/BOLT | 1set |  | D | All engine |  |
| 14 | 01 | A-1000027DA | 发动机吊钩 | HOOK | 1 |  | D | All engine |  |
| 15 | 01 | B-1-1000093D | 双头螺栓 | STUD | 5 |  | D | All engine |  |
| 16 | 01 | A-1000063D | 进气歧管密封垫 | SEALED GASKET，INTAKE MANIFOLD | 2 | Прокладка впускного коллектора | C | All engine |  |
| 17 | 01 | A-1008027D1 | 进气歧管 | INTAKE MANIFOLD | 1 | Коллектор впускной | D | All engine |  |
| 19 | 01 | A-1000027DA | 吊钩 | HOOK,ENGINE | 1 |  | Ｄ | All engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—Thermostat and interrelated hoses | SECTION. NO.:01-1007 | PAGE:17 |
| ENGINE MECHANICAL—Thermostat and interrelated hoses | SECTION. NO.:01-1007 | PAGE:18 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | Remark |
| 2 | O1 | J-1008029JA | 节温器盖 | THERMOSTAT COVER | 1 |  | D | Крышка термостата |  |
| 3 | O1 | B-1-1008031D | 节温器盖密封垫 | SEALED GASKET, THERMOSTAT COVER | 1 | Прокладка крышки термостата | C |  |  |
| 4 | O1 | B-1-1306010D | 节温器 | THERMOSTAT | 1 | термостат | C |  |  |
| 5 | O1 | A-1008048DA | 回水胶管2 | WATER RETURN SOFT HOSE | 1 |  | C |  |  |
| 6 | O1 | B-1-1000044DA | 回水胶管管夹 | CLIP,WATER RETURN SOFT HOSE | 4 |  | C |  |  |
| 9 | O1 | B-1-1303010D | 进水管总成 | WATER INLET HOSE ASSY | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—EXHAUST MANIFOLD | SECTION. NO.:01-1008 | PAGE:19 |
| ENGINE MECHANICAL—EXHAUST MANIFOLD | SECTION. NO.:01-1008 | PAGE:20 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | A-1008010DJ | 排气歧管总成 | Exhaust Manifold Pipe | 1 | Коллектор выпускной | D |  |  |
| 2 | O1 | A-1008015D | 排气歧管外隔热垫 | Outer Heat Insulating Cover Assembly – Exhaust Manifold | 1 |  | D |  |  |
| 3 | O1 | A-1008012D | 排气歧管内隔热垫 | Inner Heat Insulating Cover Assembly – Exhaust Manifold | 1 |  | D |  |  |
| 4 | O1 | B-1-1008017DJ | 双头螺栓 | Stud | 3 |  | D |  |  |
| 5 | O1 | B-1-1000080D | 螺栓 | Blot | 2 |  | D |  |  |
| 6 | O1 | A-1008054D | 排气歧管隔热垫 | Heat Insulating Cover Assembly – Exhaust Manifold | 1 | Прокладка выпускного коллектор | D |  |  |
| 7 | O1 | B-1-1008016D | 双头螺栓 | Stud | 6 |  | D |  |  |
| 9 | O1 | GB6170-86（M6） | 螺母（M6） | Nut | 6 |  | D |  |  |
| 10 | O1 | B-1-1000094D | 排气歧管固定双头螺栓（M8X25） | Stud, Exhaust Pipe | 8 | Шпилька крепления выпускного коллектора | D |  |  |
| 11 | O1 | GB6170-86 | 螺母（M8） | Nut | 8 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |
| ENGINE MECHANICAL—CYLINDER HEAD | SECTION. NO.:01-1009 | PAGE:21 |
| ENGINE MECHANICAL—CYLINDER HEAD | SECTION. NO.:01-1009 | PAGE:22 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 0 | 02 | H-1003010 | 气缸盖总成 | CYLINDER HEAD ASSY | 1 | Голвка блока ???? | D | 1051cc engine |  |
| 3 | 01 | B-1-1000121D | 油孔螺钉 | SCREW | 1 |  | D | all engine |  |
| 4 | 01 | B-1-1003016D | 汽缸盖碗型堵塞 | BOWL PLUG, CYLINDER HEAD | 6 |  | D | all engine |  |
| 5 | 01 | J-1003070 | 汽缸垫 | GASKET， CYLINDER HEAD | 1 | Прокладка головки блока | C | all engine |  |
| 6 | 01 | B-1-1000028D | 汽缸盖定位销 | PIN, CYLINDER HEAD | 4 |  | D | all engine |  |
| 7 | 01 | B-1-1000031D | 汽缸盖连接螺栓 | BOLT ,CYLINDER HEAD | 10 | Болт крепления головки блока | C | all engine |  |
| 8 | 01 | B-1-1003050D | 汽缸盖罩总成 | COVER ASSY，CYLINDER HEAD | 1 | Крышка клапанная | D | all engine |  |
| 9 | 01 | B-1-1003064DA | 汽缸盖罩密封垫 | RUBBER SEAL, CYLINDER HEAD COVER | 1 | Прокладка клапанной крышки | C | all engine |  |
| 10 | 01 | B-1-1000061D | 汽缸盖罩螺栓垫圈 | WASHER ASSY | 4 | Шайба болта клапанной крышки | D | all engine |  |
| 11 | 01 | B-1-1000059D | 汽缸盖罩螺栓 | BOLT , CYLINDER HEAD COVER | 4 | Болт крепления клапанной крышки | D | all engine |  |
| 12 | 01 | B-1-1003052DA | 加油口盖 | COVER ASSY，FILLING OIL | 1 | Крышка маслозаливная | D | all engine |  |
| 13 | 01 | A-3707100D | 火花塞 | SPARK PLUG | 4 | Свеча зажигания | C | all engine |  |
| 14 | 01 | A-1000038D | 汽缸盖后端盖 | DISTRIBUTOR SEAT | 1 | Крышка задняя ГБЦ | D | all engine |  |
| 15 | 01 | B-1-1000035D | 汽缸盖后端密封垫 | GASKET, DISTRIBUTOR SEAT | 1 | Прокладка задней крышки ГБЦ | C | all engine |  |
| 16 | 01 | GB907.15-88-M8X25 | 螺栓 | BOLT | 1 |  | D | all engine |  |
| 17 | 01 | GB907.15-88-M8X35 | 螺栓 | BOLT | 2 |  | D | all engine |  |
| 18 | 01 | B-1-1000128D | 汽缸盖前端盖 | FRONT COVER, CYLINDER HEAD | 1 | Крышка передняя ГБЦ | D | all engine |  |
| 19 | 01 | B-1-1000091D | 进气歧管带肩螺栓 | BOLT | 8 |  | D | all engine |  |
| 20 | 01 | B-1-1000123D | 密封垫 | GASKET, FRONT COVER | 1 | Прокладка передней крышки ГБЦ | C | all engine |  |
| 23 | 01 | B-1-1000131D （M8X16） | 螺栓 | BOLT | 2 |  | D | all engine |  |
| 24 | 01 | B-1-1000122D | 定位销 | PIN, FRONT COVER | 3 |  | D | all engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE MECHANICAL—CYLINDER BLOCK | SECTION. NO.:01-1010 | PAGE:23 |
| --- | --- | --- |
| ENGINE MECHANICAL—CYLINDER BLOCK | SECTION. NO.:01-1010 | PAGE:24 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O2 | H-1002010 | 汽缸体组件 | CYLINDER BLOCK | 1 | Блок цилиндров | D | 1051cc engine |  |
| 2 | O1 | B-1-1002012D | 碗型堵塞Ⅰ | BOWL PLUG | 3 |  | D | all engine |  |
| 3 | O1 | B-1-1003016D | 碗型堵塞Ⅱ | BOWL PLUG | 2 |  | D | all engine |  |
| 4 | O1 | B-1-1011011D | NPT 1/4 锥型锣塞 | SCREW PLUG， NPT 1/4 CONE | 3 |  | D | all engine |  |
| 5 | O1 | B-1-1002032D | NPT 1/8锥型锣塞 | NPT1/8 CONE SCREW PLUG | 1 |  | D | all engine |  |
| 6 | O1 | B-1-1002019D | 曲轴主轴承盖连接螺栓 | BOLT , MAIN BEARING | 10 |  | D | all engine |  |
| 7 | O1 | B-1-1000026D | 油位计固定卡 | CLIP， DIPSTICK | 1 |  | D | all engine |  |
| 8 | O1 | B-1-1002027D1 | 封水端盖 | END COVER | 1 |  | D | all engine |  |
| 9 | O1 | B-1-1002028D1 | 封水端盖密封垫 | SEAL WASHER, END COVER | 1 |  | B | all engine |  |
| 10 | O1 | B-1-1000080D | 封水端盖固定螺栓 | BOLT , END COVER | 4 |  | D | all engine |  |
| 11 | O1 | B-1-1000097D | 隔板 | SPACER | 1 |  | D | all engine |  |
| 13 | O1 | B-1-1002050D | 油位计 | DIPSTICK | 1 | Щуп маслянный | D | all engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE MECHANICAL—WATER PUMP AND FAN | SECTION. NO.:01-1011 | PAGE:25 |
| --- | --- | --- |
| ENGINE MECHANICAL—WATER PUMP AND FAN | SECTION. NO.:01-1011 | PAGE:26 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | B-1-1000083D | 水泵固定螺栓 | BOLT,WATER PUMP | 2 |  | D |  |  |
| 2 | O1 | J-1307010 | 水泵 | WATER PUMP ASSY | 1 | Насос водяной | C |  |  |
| 3 | O1 | B-1-1000052D | 水泵密封垫 | SEAL WASHER WATER PUMP | 1 | Прокладка водяного насоса | C |  |  |
| 4 | O1 | B-1-1000092D | 水泵固定双头螺栓 | STUD,WATER PUMP | 2 |  | D |  |  |
| 5 | O1 | GB6170-86（M6） | 螺母（M6） | NUT | 2 |  | D |  |  |
| 6 | O1 | J-1000077 | 风扇皮带 | BELT, FAN | 1 | Ремень вентилятора | C |  |  |
| 7 | O1 | J-1000018 | 风扇垫块 | HUB, FAN | 1 | Проставка крыльчатки вентилятора | D |  |  |
| 8 | O1 | J-1000017J | 风扇皮带轮 | PULLEY, PUMP | 1 | Шкив водяного насоса | D |  |  |
| 10 | O1 | J-1308010J | 风扇 | FAN ASSY | 1 | Крыльчатка вентилятора | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE MECHANICAL—CAMSHAFT THROTTLE VALUE AND ROCK ARM | SECTION. NO.:01-1012 | PAGE:27 |
| --- | --- | --- |
| ENGINE MECHANICAL—CAMSHAFT THROTTLE VALUE AND ROCK ARM | SECTION. NO.:01-1012 | PAGE:28 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O2 | K-1006013 | 凸轮轴 | CAMSHAFT | 1 | Вал распределительный | C | 1051cc engine |  |
| 2 | O1 | B-1-1000124D | 凸轮轴前油封 | FRONT OIL SEAL ，CAMSHAFT | 1 | Сальник распределительного вала | C | all engine |  |
| 3 | O1 | B-1-1000129D | 凸轮轴止推板 | THRUST PLATE, CAMSHAFT | 1 | Пластина распредвала | D | all engine |  |
| 4 | O1 | GB819-8（M6X16） | 沉头螺钉 | SCREW | 2 |  | D | all engine |  |
| 5 | O1 | B-1-1007045D | 摇臂轴 | ROCK ARM SHAFT | 2 | Ось коромысел | D | all engine |  |
| 6 | O1 | B-1-1007047D | 沉头螺钉（M6X12） | SCREW | 10 |  | D | all engine |  |
| 7 | O1 | B-1-1007026D | 摇臂 | ROCK ARM | 8 | Коромысло клапана | D | all engine |  |
| 8 | O1 | B-1-1007035D | 摇臂轴弹簧 | SPRING，ROCK ARM SHAFT | 8 | Пружина оси коромысел | C | all engine |  |
| 9,10 | O1 | B-1-1007027/46D | 摇臂调整螺钉/母 | ADJUSTING SCREW/NUT | 8set |  | C | all engine |  |
| 11 | O1 | B-1-1007033DA | 进气门 | INLET VALVE | 4 | Клапан выпускной | C | all engine |  |
| 12 | O1 | B-1-1007032DA | 排气门 | EXHAUST VALVE | 4 | Клапан впускной | C | all engine |  |
| 13 | O1 | B-1-1007030D | 气门弹簧 | SPRING， VALVE | 8 | Пружина клапана | C | all engine |  |
| 14 | O1 | B-1-1007029D | 气门弹簧座 | SPRING SEAT，VALVE | 8 | Шайба пружины клапана | C | all engine |  |
| 15 | O1 | B-1-1007028DA | 气门锥型锁块 | VALVE KEEPER | 8set | Сухари клапана | C | all engine |  |
| 16 | O1 | B-1-1007021D | 气门弹簧座 | SPRING SEAT，VALVE | 8 | Седло пружины клапана | C | all engine |  |
| 17 | O1 | B-1-1007022D | 气门油封 | OIL SEAL ASSY，VALVE | 8 | Колпачек маслосъемный | C | all engine |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE MECHANICAL—TIMING BELT AND FRONT AND REAR COVER OF ENGINE | SECTION. NO.:01-1013 | PAGE:29 |
| --- | --- | --- |
| ENGINE MECHANICAL—TIMING BELT AND FRONT AND REAR COVER OF ENGINE | SECTION. NO.:01-1013 | PAGE:30 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O2 | H-1022015 | 后罩壳焊接总成 | REAR HOUSING WELDING ASSY | 1 |  | D | 1051cc engine |  |
| 2 | O2 | H-1023011 | 前罩壳焊接总成 | FRONT HOUSING | 1 |  | D | 1051cc engine |  |
| 3 | O2 | H-1000029 | 前后罩壳密封垫 | RUBBER SEAL，FRONT REAR HOUSING | 1 |  | C | 1051cc engine |  |
| 4 | O1 | B-1-1022012D | 后罩盖橡胶垫 | BUSHING | 2 |  | C | all engine |  |
| 5 | O1 | B-1-1022014D | 后罩盖橡胶垫 | REAR HOUSING, RUBBER WASHER | 2 |  | C | all engine |  |
| 6 | O1 | B-1-1022013D | 后罩盖衬套 | RUBBER GASKET | 4 |  | D | all engine |  |
| 8 | O1 | B-1-1000080D | 前后罩盖连接螺栓 | BOLT, CYLINDER HEAD COVER | 6 |  | D | all engine |  |
| 9 | O1 | B-1-1000011D | 支撑片 | REINFORCEMENT SLICE | 1 |  | D | all engine |  |
| 10 | O1 | B-1-1023013D | 前罩盖挡圈 | SHIELD WASHER，FRONT HOUSING | 1 |  | D | all engine |  |
| 11 | O3 | H-1000101 | 凸轮轴正时皮带轮 | TIMING BELT WHEEL，CAMSHAFT | 1 |  | D | 1051cc engine |  |
| 12 | O1 | GB1099-79（5X19） | 半圆键 | KEY 5*19 | 1 |  | D | all engine |  |
| 14 | O3 | H-1000053 | 正时皮带 | TIMING BELT | 1 |  | C | 1051cc engine |  |
| 15 | O1 | B-1-1021010D | 张紧轮 | TENSION PULLEY ASSY | 1 |  | C | all engine |  |
| 16 | O1 | B-1-1000088D | 张紧轮固定螺栓 | BOLT ,TENSION PULLEY | 1 |  | D | all engine |  |
| 17 | O1 | B-1-1000065D | 扭簧 | SPRING | 1 |  | C | all engine |  |
| 18 | O1 | B-1-1000067D | 扭簧衬套 | BUSHING ，SPRING | 1 |  | D | all engine |  |
| 19 | O1 | B-1-1000073D | 张紧轮固定螺栓 | BOLT ,TENSION PULLEY | 1 |  | D | all engine |  |

| ENGINE ELECTRICAL—Engine fuel injection hardness, sensors and throttle body | SECTION. NO.:02-1014 | PAGE:31 |
| --- | --- | --- |
| ENGINE ELECTRICAL—Engine fuel injection hardness, sensors and throttle body | SECTION. NO.:02-1014 | PAGE:32 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3602010-V09 | 进气温度传感器总成 | Air Inlet Pressure Sensor | 1 |  | C |  |  |
| 2 |  | 3602020-2E2 | 氧传感器总成 | Oxygen Sensor | 1 |  | C |  |  |
| 3 |  | 3602030-V03 | 曲轴位置传感器总成 | Crankshaft Position Sensor | 1 |  | C |  |  |
| 4 |  | 3602040-V03 | 冷却液温度传感器总成 | Coolant Teperature Sensor | 1 |  | C |  |  |
| 5 |  | 3602050-V03 | 进气压力传感器总成 | Air Inlet Pressure Sensor | 1 |  | C |  |  |
| 6 |  | 3603010-V03 | 节流阀体总成 | Throttle Body Assy | 1 |  | C |  |  |
| 7 |  | 3603020-V03 | 燃油导轨总成 | Fuel Rail Assy | 1 |  | C |  |  |
| 9 |  | 3603030-V03 | 碳罐电磁阀 | Canister Electromagnetic Valve | 1 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE ELECTRICAL—Generator | SECTION. NO.:02-1015 | PAGE:33 |
| --- | --- | --- |
| ENGINE ELECTRICAL—Generator | SECTION. NO.:02-1015 | PAGE:34 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | Remark |
| 3 | 01 | B-1-1000021D | 发电机上支架 | upper bracket, generator | 1 | Планка натяжная генератора | D |  |  |
|  | 02 | L-1000021J | 发电机上支架 | upper bracket, generator |  |  | D |  |  |
| 4 | 01 | L-3701010JA | 发电机 | Generator assembly | 1 | генератор | C |  |  |
| 5 | 01 | B-1-1000089D | . 螺栓（M8X30） | bolt | 2 |  | D |  |  |
| 7 | 01 | B-1-1000102DA | 发电机下支架 | lower bracket, generator | 1 | Кронштейн крепления генератора | D |  |  |
|  | 02 | L-1000102J | 发电机下支架 | lower bracket, generator | 1 |  | D | For compressor, A/C |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| ENGINE ELECTRICAL—Starter | SECTION. NO.:02-1016 | PAGE:35 |
| --- | --- | --- |
| ENGINE ELECTRICAL—Starter | SECTION. NO.:02-1016 | PAGE:36 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | Remark |
| 1 | 01 | B-1-3708010DW | 起动机 | starter | 1 | стартер | C |  |  |
| 2 | 01 | B-1-1000069D | 起动机固定螺栓I | bolt, starter | 1 |  | D |  |  |
| 3 | 01 | B-1-1000068D | 起动机固定螺栓II | bolt, starter | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| FUEL AND ENGINE CONTROL—Fuel filter and interrelated hoses | SECTION. NO.:01-1104 | PAGE:37 |
| --- | --- | --- |
| FUEL AND ENGINE CONTROL—Fuel filter and interrelated hoses | SECTION. NO.:01-1104 | PAGE:38 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | Remark |
| 1 |  | 1105010-V09 | 汽油滤清器 | fuel filter | 1 | Фильтр топливный 1010 | A |  |  |
| 2 |  | 1105011-V01 | 燃油滤清器支架（1） | bracket,fuel filter | 1 |  | D |  |  |
| 3 |  | Q68308F4 | 中间固定式双管夹片 | pipe clip | 1 |  | D |  |  |
| 4 |  | CQ1460620 | 组合螺栓 | combined bolt | 1 |  | Ｄ |  |  |
| 5 |  | 1104011-V09 | 胶管-油泵到燃油滤 | Rubber hose,fuel pump to fuel filter | 1 |  | Ｃ |  |  |
| 6 |  | 1104012-V09 | 胶管-油滤到进油管 | Rubber hose,fuel filter to fuel inlet pipe | 1 |  | Ｃ |  |  |
| 7 |  | 1104014-2E2 | 进油管 | Fuel inlet pipe | 1 |  | Ｄ |  |  |
| 8 |  | 1104016-6J6 | 胶管-油轨进口到进油管 | Rubber hose,connect to fuel rails | 1 |  | Ｃ |  |  |
| 9 |  | 1104013-6J6 | 胶管-油轨出口到回油管 | Rubber hose,from fuel rails to fuel return pipe | 1 |  | Ｃ |  |  |
| 10 |  | 1104019-2E2 | 回油管 | Fuel return pipe | 1 |  | Ｄ |  |  |
| 11 |  | 1104021-V09 | 胶管-回油管到油泵回油口 | Rubber hose,fuel return pipe to fuel tank(fuel pump) | 1 |  | Ｃ |  |  |
| 12 |  | 015.3-706 | 夹子 | grommet | 8 |  | Ｃ |  |  |
| 13 |  | Q68108F4 | 单管夹片 | Single pipe clip | 2 |  | Ｄ |  |  |
| 14 |  | Q2716313 | 十字槽自攻螺钉 | screw | 3 |  | Ｄ |  |  |
| 15 |  | 018.5-706 | 夹子 | grommet | 2 |  | Ｃ |  |  |

| FUEL AND ENGINE CONTROL—Fuel pump and fuel tank | SECTION. NO.:01-1106 | PAGE:39 |
| --- | --- | --- |
| FUEL AND ENGINE CONTROL—fuel pump and fuel tank | SECTION. NO.:01-1106 | PAGE:40 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 1103010-V01 | 汽油箱盖总成 | GASOLINE TANK CAP ASSEMBLY | 1 |  | D |  |  |
| 2 |  | 1101063-6J6 | 加油口颈衬垫 | FUEL ADDING LINING GASKET | 1 |  | D |  |  |
| 3 |  | 1101080-6J6 | 加油口颈总成 | FUEL ADDING NECK ASSEMBLY | 1 |  | D |  |  |
| 4 |  | Q1840512 | 六角法兰面螺栓 | BOLT | 4 |  | D |  |  |
| 5 |  | CQ1460620 | 组合螺栓 | COMBINED BOLT | 1 |  | D |  |  |
| 6 |  | Q673B15 | 钢丝型弹性环箍 | STEEL GROMMET | 4 |  | C |  |  |
| 7 |  | 1101064-6J6 | 连通管胶管Ⅱ | CONNECTING HOSE II | 1 |  | C |  |  |
| 8 |  | Q68112F4 | 单管夹片 | CLAMP | 1 |  | D |  |  |
| 9 |  | CQ2716313 | 自攻螺钉 | SELF-TAPPING SCREW | 1 |  | D |  |  |
| 10 |  | 1101062-V01 | 连通钢管 | CONNECTING STEEL TUBE | 1 |  | D |  |  |
| 11 |  | 1101056-6J6 | 胶套-连通钢管 | RUBBER BUSHING | 1 |  | C |  |  |
| 12 |  | CQ67660B | 蜗杆传动式软管夹箍 | GROMMET | 2 |  | C |  |  |
| 13 |  | 1101066-6J6 | 加油胶管 | FUEL ADDING HOSE | 1 |  | C |  |  |
| 14 |  | 1101058-6J6 | 连通管胶管Ⅰ | CONNECTING HOSE I | 1 |  | C |  |  |
| 15 |  | 1101074-V09 | 弹簧胀圈 | SPRING WASHER | 1 |  | C |  |  |
| 16 |  | 1106010-V09 | 汽油泵总成 | FUEL PUMP ASSEMBLY | 1 |  | C |  |  |
| 17 |  | 1106040-V09 | 油量传感器浮子及连杆 | FUEL LEVEL SENSOR ASSY | 1 |  | C | ***note*** |  |
| 18 |  | 1101073-V09 | O型密封圈 | SEALING RING "o" | 1 |  | C |  |  |
| 19 |  | 1101010-V09 | 燃油箱 | FUEL TANK ASSY | 1 |  | D |  |  |
| 20 |  | CQ1460820 | 组合螺栓 | COMBINED BOLT | 4 |  | D |  |  |
|  |  | NOTE: WE HAVE THREE SUPPLIERS OF FUEL PUMP, ONLY THE ONE MADED BY QIXING COMPANY CAN BE UNASSEMBLED ,AND THE FUEL LEVEL SENSOR ASSY CAN BE REPAIRED |  |  |  |  |  |

| FUEL AND ENGINE CONTROL—Carbon canister | SECTION. NO.:01-1130 | PAGE:41 |
| --- | --- | --- |
| FUEL AND ENGINE CONTROL—Carbon canister | SECTION. NO.:01-1130 | PAGE:42 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 1130010-V09 | 碳罐 | CARBON CANISTER | 1 | Адсорбер 1010 | Ｃ |  |  |
| 2 |  | 012.8-706 | 夹子 | CLAMP | 2 |  | Ｃ |  |  |
| 3 |  | ZD150*8 | 扎带 | PLASTIC CLIP | 2 |  | Ｃ |  |  |
| 4 |  | 1130011-V03 | 胶管-碳罐到电磁阀 | RUBBER HOSE,CARBON CANISTER TO ELECTROMAGNETION VALVE | 1 |  | Ｃ |  |  |
| 5 |  | Q673B10 | 夹子 | CLAMP | 2 |  | Ｃ |  |  |
| 6 |  | 1101052-V01 | 胶管-油泵到碳罐 | RUBBER HOSE,FUEL PUMP TO CARBON CANISTER | 1 |  | Ｃ |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| FUEL AND ENGINE CONTROL—Air filter | SECTION. NO.:01-1109 | PAGE:43 |
| --- | --- | --- |
| FUEL AND ENGINE CONTROL—Air filter | SECTION. NO.:01-1109 | PAGE:44 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 0１ | 1109041-2E2 | 管夹子 | CLAMP | 2 |  | Ｃ |  |  |
| 2 | 0１ | 1109032-2E2 | 空滤出气管 | OUTLET PIPE,AIR FILTER | 1 | Шланг корпуса воздушного фильтра (болишой) | Ｃ |  |  |
| 3 | 0１ | Q1460825 | 六角头螺栓、弹簧垫圈、平垫圈组合件 | COMBINED BOLT | 2 |  | Ｄ |  |  |
| 4 | 0１ | 1109010-2E2 | 空滤器总成 | AIR FILTER ASSY | 1 | Корпус воздушного фильтра в сборе | Ｃ |  |  |
| 5 | 0１ | 1109023-2E2 | 滤芯总成 | ELEMENT， AIR FILTER | 1 | Фильтр воздушный(элемент) 1010 | Ａ |  |  |
| 6 | 0１ | 1109031-2E2 | 空滤进气管 | INLET PIPE,AIR FILTER | 1 | Шланг воздушного фильтра (малый) | Ｃ |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| COOLING & EXHAUST- Muffler welding assembly and catalytic converter | SECTION. NO.:01-1201 | PAGE:45 |
| --- | --- | --- |
| COOLING & EXHAUST- Muffler welding assembly and catalytic converter | SECTION. NO.:01-1201 | PAGE:46 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 1205010-V09 | 三元催化器焊接总成 | Catalytic Converter Assembly | 1 | Катализатор нов 1010 | C |  |  |
| 2 |  | 1205030-V06 | 密封垫片总成 | Asbestos Cushion | 1 | Прокладка катализатора новая | C |  |  |
| 3 |  | GB /T 854 10 | 单耳止动垫圈 | Washer | 3 |  | D |  |  |
| 4 |  | Q361C10 | 螺母 | Nut | 3 |  | C |  |  |
| 5 |  | 1201098-V01 | 密封圈 | Seal | 1 | Прокладка между глушителем и катализатором 1010 | D |  |  |
| 6 |  | 1201096-6J6 | 消声器法兰螺栓 | Muffler Flange Bolt | 2 |  | C |  |  |
| 7 |  | 1201097-6J6 | 弹簧 | Spring | 2 |  | C |  |  |
| 8 |  | 1201010-4E2 | 消声器焊接总成 | Muffler Welding Assembly | 1 | Глушитель в сборе | C |  |  |
| 9 |  | 1201090-6J6 | 连接胶块 | Connecting Rubber Pad | 3 | Подушка подвески глушителя | D |  |  |

| COOLING & EXHAUST-Radiator assy | SECTION. NO.:01-1301 | PAGE:47 |
| --- | --- | --- |
| COOLING & EXHAUST-Radiator assy | SECTION. NO.:01-1301 | PAGE:48 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | Q1460830 | 组合螺栓 | COMBINED BOLT | 2 |  | Ｄ |  |  |
| 2 |  | 1302011-2E2 | 散热器支架 | BRACKET,RADIATOR | 2 |  | Ｄ |  |  |
| 3 |  | 1302013-1J0 | 橡胶衬套 | RUBBER BUSHING | 4 |  | Ｃ |  |  |
| 4 |  | 1301010-2E2 | 散热器总成 | RADIATOR ASSY | 1 | Радиатор в сборе | Ｃ |  |  |
| 5 |  | CQ1460620 | 组合螺栓 | COMBINED BOLT | 2 |  | Ｄ |  |  |
| 6 |  | 1309010-2E2 | 散热器护风罩及电子扇总成 | RADIATOR COVER AND ELECTRIC FAN | 1 | Рамка радиатора с электромотором??? | Ｃ |  |  |
| 7 |  | 1311010-V01 | 膨胀箱总成 | COMPENSATION WATER TANK | 1 | Бачек расширительный ???? | Ｃ |  |  |
| 8 |  | 1303012-2E2 | 发动机出水软管 | RUBBER HOSE,ENGINE WATER OUTLET | 1 |  | Ｃ |  |  |
| 9 |  | 1303011-2E2 | 发动机进水软管 | RUBBER HOSE,ENGINE WATER INLET | 1 |  | Ｃ |  |  |
| 11 |  | Q67632 | B型蜗杆传动式软管环箍 | GROMMET | 8 |  | Ｃ |  |  |
| 12 |  | 1303014-2E2 | 散热器出水软管 | WATER OUTLET PIPE,RADIATOR | 1 | Шланг радиатора нижний | Ｃ |  |  |
| 13 |  | 1303013-2E2 | 散热器进水软管 | WATER OUTLET PIPE,RADIATOR | 1 | Шланг радиатора верхний | Ｃ |  |  |
| 14 |  | CQ1460616 | 组合螺栓 | COMBINED BOLT | 4 |  | Ｄ |  |  |
| 15 |  | 1303020-2E2 | 水管焊接总成 | WATER PIPE WELDING ASSY | 1 |  | Ｄ |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Throttle cable assembly and clutch cable | SECTION. NO.:02-1108 | PAGE:49 |
| --- | --- | --- |
| POWER TRAIN—Throttle cable assembly and clutch cable | SECTION. NO.:02-1108 | PAGE:50 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 01 | 1108100—2E2 | 油门拉线总成 | Throttle cable assembly | 1 | Трос газа | C |  |  |
| 2 | 01 | 1602060-2E2 | 离合器拉线总成 | Clutch cable assembly | 1 | Трос сцепления | C |  |  |
| 3 | 01 | 1602072-V0l | 扎带 | plastic clip | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Brake pedal, clutch pedal and accelerator pedal | SECTION. NO.:02-1602 | PAGE:51 |
| --- | --- | --- |
| POWER TRAIN—Brake pedal, clutch pedal and accelerator pedal | SECTION. NO.:02-1602 | PAGE:52 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 1602021-2E2 | 衬套－离合踏板 | Bushing , clutch pedal | 4 |  | C |  |  |
| 3 |  | 3504101-2E2 | 制动踏板回位弹簧 | Retract spring , brake pedal | 2 |  | C |  |  |
| 5 |  | Q1840835 | 六角法兰面螺栓 | Hex washer head bolt | 1 |  | D |  |  |
| 6 |  | Q33008 | 全金属六角法兰面锁紧螺母 | lock nut | 1 |  | D |  |  |
| 7 |  | 3504020-2E2 | 踏板支架焊接总成 | Pedal bracket welding assy | 1 |  | D |  |  |
| 8 |  | Q1420816 | 六角头螺栓和弹簧垫圈组合件 | combined hex bolt with spring washer | 2 |  | D |  |  |
| 9 |  | 1602025-2E2 | 离合器踏板臂焊接总成 | clutch pedal arm welding assy | 1 |  | D |  |  |
| 10 |  | 3504080-2E2 | 制动踏板臂焊接总成 | brake pedal arm welding assy | 1 |  | D |  |  |
| 11 |  | 3504102-V01 | 踏板胶套 | Rubber cover , pedal | 2 |  | C |  |  |
| 12 |  | 1108300-2E2 | 油门踏板总成 | Accelerator Pedal | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Transmission assembly | SECTION. NO.:02-1700 | PAGE:53 |
| --- | --- | --- |
| Note: Key No.2 Gasket and seal kit-transmission Seal –oil front cover Gasket- front cover Gasket –case front Seal-oil rear extension Gasket- rear extension Gasket-shift housing |
| POWER TRAIN—Transmission assembly | SECTION. NO.:02-1700 | PAGE:54 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | G-1700000J | 变速箱总成 | Transmission assembly | 1 | Коробка передач в сборе | C |  | 5 MT |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Transmission case and cover | SECTION. NO.:02-1701 | PAGE:55 |
| --- | --- | --- |
| POWER TRAIN—Transmission case and cover | SECTION. NO.:02-1701 | PAGE:56 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 6 | O1 | 462-3729010 | 倒车开关 | reverse switch | 1 | Датчик заднего хода | C |  |  |
| 7 | O1 | 465-1701010E1 | 变速箱壳体 | gear box cover(upper and lower | 1 | Картер КПП передний в сборе | D |  |  |
| 8 | O1 | 462-1702211 | 上箱孔罩 | upper box plug cover | 1 |  | D |  |  |
| 10 | O1 | GB900-88 （AYM8*30-8.8） | 双头螺栓 | bolt（AYM8*30-8.8） | 6 |  | D |  |  |
| 12 | O1 | 465-1701504 | 延伸箱后油封 | rear oil seal | 1 | Сальник вторичного вала | C |  |  |
| 17 | O1 | 465-1701500 | 延伸箱 | rear housing,rear extension | 1 | Картер КПП задний | D |  |  |
| 18 | O1 | 465-1701013 | 上下箱定位销 | location pin | 1 |  | D |  |  |
| 20 | O1 | 465-1702037 | 工艺孔堵 | seal plug | 1 |  | C |  |  |
| 21 | O1 | 465-1701120 | 输入轴档板 | front cover,housing | 1 | Крышка первичного вала | D |  |  |

| POWER TRAIN—Transmission Gear | SECTION. NO.:02-1701-1 | PAGE:57 |
| --- | --- | --- |
| POWER TRAIN—Transmission Gear | SECTION. NO.:02-1701-1 | PAGE:58 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 465-1701122 | 输入轴油封 | OIL SEAL ，INPUT SHAFT | 1 | Сальник первичного вала | C |  |  |
| 2 | O1 | 465-1701115 | 输入轴轴承档圈 | THRUST RING，BEARING | 1 | Колцо стопорное внутреннее подшипника первичного вала | C |  |  |
| 3 | O1 | 465-1701113 | 输入轴轴承 | BEARING, INPUT SHAFT | 1 | Подшипник первичного вала | C |  |  |
| 4 | O1 | 465-1701110 | 输入轴 | INPUT SHAFT | 1 | Вал первичный(голый) | D |  |  |
| 5 | O1 | 465-1701110-00 | 输入轴滚针轴承 | NEEDLE BEARING，INPUT SHAFT | 1 | Подшипник игольчатый первичного вала | C |  |  |
| 6 | O1 | 465-1701114 | 输入轴轴承档圈 | THRUST RING, BEARING | 1 | Кольцо стопорное внешнее подшипника первичного вала | D |  |  |
| 7 | O1 | 465-1701115 | 输入轴轴承档圈 | THRUST WASHER，BEARING | 1 |  | D |  |  |
| 8 | O1 | 465-1701208 | 3/4/5档同步器齿环 | GEAR RING, 3RD/4TH/5TH GEAR SYNCHRONIZE | 4 | Кольцо блокирующее синхронизатора 3,4,5 передачи | D |  |  |
| 9 | O1 | 465-1701204 | 高速同步器组件 | 3RD/4TH GEAR SYNCHRONIZER | 1 | Муфта со ступицей 3,4 передачи в сборе | C |  |  |
| 11 | O1 | 465-1701202-00 | 三档齿轮滚针轴承 | NEEDLE BEARING，3rd SPEED GEAR | 1 | Подшипник игольчатый шестерни з передачи | C |  |  |
| 12 | O1 | 465-1701202 | 三档齿轮 | 3RD SPEED GEAR | 1 | Шестерня 3 передачи | D |  |  |
| 13 | O1 | 465-1701201 | 输出轴 | OUTPUT SHAFT | 1 | Вал вторичный (голый) | D |  |  |
| 14 | O1 | 465-1701223 | 输出轴倒档齿轮 | REVERSE GEAR, OUTPUT SHAFT | 1 | Шестерня задней передачи | D |  |  |
| 15 | O1 | 465-1701224-00 | 5 档齿轮滚针轴承 | NEEDLE BEARING，5TH GEAR | 1 | Подшипник игольчатый шестерни 5 передачи (или задней?????) | C |  |  |
| 16 | O1 | 465-1701215 | 倒档齿轮轴套 | SHAFT SLEEVE, RELEASE GEAR | 1 |  | D |  |  |
| 18 | O1 | GB/T276-94(465A/6206N/C3) | 输出轴前轴承 | FRONT BEARING, OUTPUT SHAFT | 1 | Подшипник вторичного вала передний | C |  |  |
| 19 | O1 | 465-1701232 | 主轴承前档圈 | THRUST RING, BEARING | 1 |  | D |  |  |
| 21 | O1 | 1701211-465A | 一档齿轮 | 1ST GEAR | 1 | Шестерня 1 передачи | D |  |  |
| 22 | O1 | 465-1701212-00 | 一档齿轮滚针轴承 | NEEDLE BEARING,1ST GEAR | 1 | Подшипник игольчатый шестерни 1 передачи | C |  |  |
| 23 | O1 | 465-1701215 | 倒档齿轮轴套 | AXLE SLEEVE，RELEASE GEAR | 1 |  | D |  |  |
| 24 | O1 | 465-1701221 | 低速同步器齿环组件 | GEAR RING,1ST/2ND SPEEDSYNCHRONIZER | 2 | Кольцо блокирующее шестерни 1,2 передачи | C |  |  |
| 25 | O1 | 465-1701217 | 低速同步器组件 | 1ST/2ND GEAR SYNCHRONIZER | 1 | Муфта синхронизатора со ступицей 1,2 передачи в сборе | C |  |  |
| 27 | O1 | 465-1701209 | 2 档齿轮 | GEAR ASSY- 2ND | 1 | Шестерня 2 передачи | D |  |  |

| POWER TRAIN—Transmission Gear | SECTION. NO.: 02-1701-2 | PAGE:59 |
| --- | --- | --- |
| POWER TRAIN—Transmission Gear | SECTION. NO.: 02-1701-2 | PAGE:60 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 29 | O1 | 465-1701226 | 5 档同步器组件 | HUB-SYNCHRONIZER,5TH GEAR | 1 | Муфта синхронизатора 5 передачи | C |  |  |
| 31 | O1 | 465-1701115 | 输入轴轴承档圈 | THRUST WASHER，INPUT SHAFT BEARING | 1 |  | D |  |  |
| 32 | O1 | 465-1701224-00 | 5 档齿轮滚针轴承 | NEEDLE BEARING，5TH GEAR | 1 | Подшипник игольчатый шестерни 5 передачи | D |  |  |
| 33 | O1 | 465-1701224 | 5 档齿轮 | 5TH GEAR ASSY | 1 | Шестерня 5 передачи | D |  |  |
| 34 | O1 | 465-1701225 | 主轴后轴承档圈 | THRUST WASHER，MAIN SHAFT BEARING | 1 |  | C |  |  |
| 35 | O1 | GB/T276-84 (465A/6305/C3) | 输出轴后轴承 | REAR BEARING, OUTPUT SHAFT | 1 | Подшипник вторичного вала задний | D |  |  |
| 36，38 | O1 | 465-1701234 | 主轴后轴承卡圈 | RING SNAP,MAIN SHAFT BEARING | 3 | Кольцо стопорное заднего подшшипника втор вала и шестерни привода спидометра | D |  |  |
| 39 | O1 | 465-1701230 | 涡轮 | DRIVE GEAR, ODOMETER | 1 | Шестерня привода спидометра втор вала | D |  |  |
| 41 | O1 | 465-1701405 | 倒档齿轮垫圈 | WASHER，RELEASE GEAR | 1 |  | D |  |  |
| 42 | O1 | 465-1701402 | 倒档齿轮 | RELEASE GEAR | 1 |  | D |  |  |
| 43 | O1 | 465-1701404 | 倒档齿轮轴 | IDLE GEAR SHAFT, REVERSE | 1 | ОСЬ ШЕСТЕРНИ ЗАДНЕЙ ПЕРЕДАЧИ (ПАРАЗИТКИ | D |  |  |
| 44 | O1 | 465-1701406 | 倒档齿轮止推环 | THRUST RING ，RELEASE GEAR | 1 |  | D |  |  |
| 45 | O1 | GB-3452.1-92(21X1.2) | 涡轮轴套密封圈 | O-SHAPE SEAL RING(21X1.2)， ODOMETER GEAR SHAFT | 1 |  | C |  |  |
| 46 | O1 | GB-3452.1-92(19X1.9) | 涡轮轴套密封圈 | O-SHAPE SEAL RING (19*1.9)，ODOMETER GEAR SHAFT | 1 |  | C |  |  |
| 48 | O1 | 465-1701507 | 涡轮轴套 | SHAFT SLEEVE, ODOMETER GEAR | 1 | МУФТА ШЕСТЕРНИ ПРИВОДА СПИДОМЕТРА | C |  |  |
| 49 | O1 | 465-1701506 | 涡杆 | DRIVEN GEAR, ODOMETER | 1 | ШЕСТЕРНЯ ПРИВОДА СПИДОМЕТРА В КАРТЕР | C |  |  |
| 50 | O1 | 465-1701115 | 输入轴轴承卡圈 | RING SNAP,INPUT SHAFT BEARING | 1 |  | D |  |  |
| 51 | O1 | 465-1701304 | 中间轴前轴承 | FRONT BEARING, MIDDLE SHAFT | 1 |  | C |  |  |
| 52 | O1 | 465-1701301 | 中间轴 | MIDDLE SHAFT | 1 |  | D |  |  |
| 53 | O1 | 465-1701305 | 中间轴中轴承 | BEARING, MIDDLE SHAFT | 1 |  | C |  |  |
| 54 | O1 | 465-1701303 | 5档传动齿轮 | 5TH OVERDRIVE GEAR | 1 |  | D |  |  |
| 55 | O1 | 465-1701302 | 倒档传动齿轮 | RELEASE GEAR, MIDDLE SHAFT | 1 |  | D |  |  |
| 56 | O1 | 465-1701306 | 中间轴后轴承 | REAR BEARING, MIDDLE SHAFT | 1 |  | C |  |  |

| POWER TRAIN—Shifting Mechanism(lever & fork) | SECTION. NO.:02-1702 | PAGE:61 |
| --- | --- | --- |
| POWER TRAIN—Shifting Mechanism(lever & fork) | SECTION. NO.:02-1702 | PAGE:62 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 2 | O1 | GB119-86 （ A6*12） | 定位销 | location pin | 1 |  | D |  |  |
| 5 | O1 | 465-1702013 | 换档轴总成 | Gear shifting shaft assembly | 1 |  | D |  |  |
| 6 | O1 | 465-1702022 | 换档箱密封圈 | seal ring,shift housing | 1 |  | C |  |  |
| 7--13 | O1 | 462-1702097 | 换位轴总成 | gear position shifting combined parts | 1 |  | D |  |  |
| 14 | O1 | 465-1702017 | 换档摆杆 | guide block | 1 |  | D |  |  |
| 15 | O1 | 465-1702021 | 换档杆1#回位簧 | 1# return spring | 1 |  | C |  |  |
| 16 | O1 | 465-1702020 | 垫圈 | washer | 1 |  | D |  |  |
| 17 | O1 | 462-1702115 | 换档杆2#回位簧 | 2# return spring |  |  | C |  |  |
| 18 | O1 | 465-1702025 | 螺栓 | bolt | 1 |  | D |  |  |
| 19 | O1 | 465-1702034 | 1/2档拨叉 | fork, first and second speed gear | 1 | Вилка включения 1,2 передачи | C |  |  |
| 20 | O1 | 465-1702035 | 3/4档拨叉 | fork, third and fourth speed gear | 1 | Вилка включения 3,4 передачи | C |  |  |
| 21 | O1 | 465-1702036 | 5/倒档拨叉 | fork, fifth speed gear reverse speed gear | 1 | Вилка включения 5,и заднего хода | C |  |  |
| 22 | O1 | 465-1702031 | 1/2 档换档杆 | fork shaft, first and second speed gear | 1 | Шток включения 1,2передачи | D |  |  |
| 23 | O1 | 465-1702032 | 3/4档换档杆 | fork shaft, third and fourth speed gear | 1 | Шток включения 3,4 передачи | D |  |  |
| 24 | O1 | 465-1702033 | 5/倒档换档杆 | Transmission fork shaft, reverse and fifth speed gear | 1 | Шток включения 5 пер,и заднего хода | D |  |  |
| 26 | O1 | Q/TZ0903 5*22 | 圆柱销 | column pin,fork | 3 | Фиксатор вилок КПП | C |  |  |
| 27 | O1 | 465-1702038 | 换档锁紧簧 | spring | 3 | Фиксатор штоков КПП | C |  |  |
| 28 | O1 | GB308-89 D9.525 | 拨叉轴互锁钢球 | steel ball,fork shaft | 3 | Шарик штоков КПП | D |  |  |
| 29 | O1 |  | 垫圈 | washer | 1 |  | D |  |  |
| 30 | O1 | 465-1702000 | 换档箱总成 | shift housing assy | 1 | Крышка кпп верхняя в сборе | D |  |  |

| POWER TRAIN—Clutch cover,Disc & Release parts | SECTION. NO.:02-1602 | PAGE:63 |
| --- | --- | --- |
| POWER TRAIN—Clutch cover,Disc & Release parts | SECTION. NO.:02-1602 | PAGE:64 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | B-1-1000135D | 飞轮定位销 | PIN, FLYWHEEL | 1 |  | D |  |  |
| 2 | O1 | G-1005012 | 飞轮 | FLYWHEEL | 1 |  | C |  |  |
| 3 | O1 | B-1-1005014D | 飞轮固定螺栓 | BOLT，FLYWHEEL | 6 |  | D |  |  |
| 4 | O1 | B-1-1602000D | 摩擦片 | DISC ASSY-CLUTCH | 1 | Диск сцепления ведомый | C |  |  |
| 5 | O1 | H-1601000 | 离合器压盘 | COVER ASSY-CLUTCH | 1 | Корзина сцепления | C |  |  |
|  |  | B-1-1005024D |  | BOLT（M8X20） | 2 |  | D |  |  |
| 7 | O1 | 465-1601206 | 分离轴承 | RELEASE BEARING，CULTCH | 1 | Подшипник выжимной | C |  |  |
| 8 | O1 | 462-1702214 | 拨叉轴套 | AXLE SLEEVE,FORK SHIFT | 2 | Втулка вилки подшипника сцепления | C |  |  |
| 9 | O1 | 465-1601200 | 离合器拨叉轴 | FORK SHAFT ASSY, CLUTCH | 1 | Вилка подшипника сцепления | C |  |  |
| 10 | O1 | 465-1601205 | 拨叉轴回位簧 | SPRING，FORK SHAFT | 2 |  | C |  |  |
| 11 | O1 | GB6170-86（M8） | 螺母（M8） | NUT(M8) | 1 |  | D |  |  |
| 13 | O1 | GB5782-86（M8） | 螺栓（M8） | BOLT(M8) | 1 |  | D |  |  |
| 14 | O1 | 465-1601204 | 离合器转臂 | TURNING ARM，FORK SHAFT | 1 | Рычаг вилки сцепления | D |  |  |
| 15 | O1 | GB/T276-94 | 飞轮球轴承 | BALL BEARING，FLYWHEEL | 1 |  | C |  |  |
| 16 | O1 | J-1005013 | 离合器齿圈 | GEAR RING，FLYWHEEL | 1 |  | C |  |  |
| 17 | O1 | G-1005011 | 飞轮齿圈总成 | FLYING WHEEL AND GEAR RING ASSY | 1 | Маховик в сборе | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Transmission shift lever and control linkage | SECTION. NO.:02-1703-1 | PAGE:65 |
| --- | --- | --- |
| POWER TRAIN—Transmission shift lever and control linkage | SECTION. NO.:02-1703-1 | PAGE:66 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 1703060-2E2 | 变速手柄总成 | knob-hand lever | 1 | Рукоятка КПП | D |  |  |
| 2 | O1 | 1703013-2E2 | 防尘罩 | rubber dust cover | 1 | Чехол рычага КПП | C |  |  |
| 3 | O1 | 1703020-V01 | 变速操纵支架总成 | Bracket, gear shifting control | 1 |  | D |  |  |
| 4 | O1 | 1703030-V01 | 变速操纵杆总成 | lever assy-control | 1 |  | D |  |  |
| 5 | O1 | 1703040-V01 | 选速臂总成 | Gear selecting arm | 1 | Маятник троса КПП | D |  |  |
| 6 | O1 | 1703051-V01 | 球头座 | Ball head seat | 1 |  | D |  |  |
| 7 | O1 | 1703052-V01 | 衬套 | bushing | 2 |  | D |  |  |
| 8 | O1 | 1703053-V01 | 选速回位弹簧 | Return spring, gear selecting | 1 |  | C |  |  |
| 9 | O1 | Q40012 | 小垫圈 | small washer | 1 |  | D |  |  |
| 10 | O1 | Q43690 | 开口挡圈 | Cotter washer | 1 |  | C |  |  |
| 11 | O1 | 1703057-V01 | 连接接头 | Connector | 1 |  | D |  |  |
| 12 | O1 | 1703054-V01 | 接头衬套 | Bushing, connector | 1 |  | D |  |  |
| 13 | O1 | 1703056-V01 | 鞍形弹性垫圈 | Lock washer | 1 |  | C |  |  |
| 14 | O1 | Q40108 | 垫圈 | Washer | 1 |  | D |  |  |
| 15 | O1 | Q5003220 | 开口销 | Cotter pin | 1 |  | D |  |  |
| 16 | O1 | CQ1420512 | 组合螺栓 | combined bolt | 4 |  | D |  |  |
| 19 | O1 | CQ1420625 | 组合螺栓 | combined bolt | 1 |  | D |  |  |
| 20 | O1 | 1703070-2E2 | 变速软杆总成 | Gear shifting soft lever assembly | 1 | Трос КПП два оверствия | B |  |  |
| 21 | O1 | 1703080-2E2 | 选速软杆总成 | Gear selecting soft lever assembly | 1 | Трос КПП одно отверствие | B |  |  |
| 22 | O1 | CQ36006 | 六角厚螺母 | Thick nut | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Transmission shift lever and control linkage | SECTION. NO.:02-1703-2 | PAGE:67 |
| --- | --- | --- |
| POWER TRAIN—Transmission shift lever and control linkage | SECTION. NO.:02-1703-2 | PAGE:68 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 23 | O1 | CQ36006 | 六角厚螺母 | Thick nut | 1 |  | D |  |  |
| 24 | O1 | Q40108 | 垫圈 | Washer | 1 |  | D |  |  |
| 25 | O1 | Q5002520 | 开口销 | Lock pin | 3 |  | C |  |  |
| 26 | O1 | 1703093-V01 | 软杆孔堵 | Plug, soft lever hole | 1 |  | D |  |  |
| 27 | O1 | 1703092-V01 | 防尘堵压板 | Compress plate, dust plug | 1 | Фиксатор тросов КПП на два троса | D |  |  |
| 28 | O1 | CQ2716316 | 自攻螺钉 | Self-tapping screw | 2 |  | D |  |  |
| 29 | O1 | 1703100-6J6 | 选换档软轴支架焊接总成 | welding supporting bracket, shifting soft lever | 1 |  | D |  |  |
| 30 | O1 | ZDG100×8 | 扎带 | strap | 1 |  | B |  |  |
| 31 | O1 | Q40108 | 垫圈 | washer | 2 |  | D |  |  |
| 32 | O1 | 1703091-V01 | 软杆固定卡片 | Clip plate, soft lever | 2 | Фиксатор тросов КПП | B |  |  |
| 33 | O1 | Q50108 | 锁销 | lock pin | 2 |  | B |  |  |
| 34 | O1 | 1703010-2E2 | 变速操纵总成 | Gear shifting lever and control linkage assembly | 1 | Рычаг КПП в сборе | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN— Propeller Shaft | SECTION. NO.:02-2201 | PAGE:69 |
| --- | --- | --- |
| POWER TRAIN—Propeller Shaft | SECTION. NO.:02-2201 | PAGE:70 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 2201010-4E2 | 传动轴总成 | Propeller shaft | 1 | Вал карданный в сборе | D |  |  |
| 2 | O1 | 2201020-v01 | 万向节花键轴叉总成 | Spline yoke assembly, u-joints | 1 |  | C |  |  |
| 3 | O1 | 2201059-v01 | 万向节法兰盘 | Flange, u-joints | 1 |  | C |  |  |
| 4 | O1 | 2201030-v01 | 万向节总成 | U-joints assembly | 2 | Крестовина карданного вала в сборе | C |  |  |
| 5 | O1 | 2201096-v01 | 孔用弹性挡圈 | Elastic retaining washer | 8 |  | C |  |  |
| 6 | O1 | 2201014-v01 | 传动轴螺栓 | Bolt, propeller shaft | 4 | Болт карданного вала | D |  |  |
| 7_1 | O1 | CQ34008 | 六角螺母 | Nut | 4 | Гайка болта карданного вала | D |  |  |
| 7_2 | O1 | Q40308 | 弹簧垫圈 | Sping washer | 4 | Шайба болта карданного вала | C |  |  |
|  |  |  |  |  |  |  |  | 1020v ，1020vr |  |

| POWER TRAIN—Front shock absorber with coil spring assembly | SECTION. NO.:02-2901 | PAGE:71 |
| --- | --- | --- |
| POWER TRAIN—Front shock absorber with coil spring assembly | SECTION. NO.:02-2901 | PAGE:72 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2901015-4E2 | 前支柱总成（左） | Front shock absorber with coil spring assembly , LH | 1 | Стойка передней подвески левая | C |  |  |
| 2 |  | 2901020-4E2 | 前支柱总成（右） | Front shock absorber with coil spring assembly , RH | 1 | Стойка передней подвески правая | C |  |  |
| 3 |  | 2901011-2E2 | 六角法兰面螺栓 | bolt | 4 |  | D |  |  |
| 4--1 |  | CQ34112 | 六角螺母 | nut | 4 |  | D |  |  |
| 4--2 |  | Q40312 | 弹簧垫圈 | spring washer | 4 |  | C |  |  |
| 5 |  | 3001011-2E2 | 左转向节 | left steering knuckle | 1 | Кулак поворотный левый | D |  |  |
| 6 |  | 3001012-2E2 | 右转向节 | right steering knuckle | 1 | Кулак поворотный правый | D |  |  |
| 7 |  | 3103018-2E2 | 车轮固定螺栓 | bolt for fixing wheel | 8 | Болт колеса | D |  |  |
| 8 |  | 3103015-2E2 | 前轮毂总成 | front wheel hub | 2 | Ступица передняяв сборе | C |  |  |
| 9 |  | 3103017-V01 | 车轮固定螺母 | Nut ,wheel | 8 | Гайка колеса | D |  |  |
| 10 |  | 3103023-2E2 | 锁紧螺母 | lock nut | 2 | Гайка поворотного кулака | D |  |  |
| 11 |  | 3103021-2E2 | 防尘罩 | dust cover | 2 | Колпак передней ступицы | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Middle arm welding assembly,front suspension | SECTION. NO.:02-2904-1 | PAGE:73 |
| --- | --- | --- |
| POWER TRAIN—Middle arm welding assembly ,front suspension | SECTION. NO.:02-2904-1 | PAGE:74 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2904010-2E2 | 前悬挂架本体总成 | Middle arm welding assembly,front suspension | 1 |  | D |  |  |
| 2 |  | Q40112 | 平垫圈 | plate washer | 4 |  | D |  |  |
| 3 |  | Q40312 | 弹簧垫圈 | spring washer | 4 |  | C |  |  |
| 4 |  | Q151B1230 | 六角头螺栓 | hex bolt | 4 |  | D |  |  |
| 5 |  | CQ1601075 | 六角头螺栓 | hex bolt | 2 |  | D |  |  |
| 7 |  | Q40310 | 弹簧垫圈 | spring washer | 2 |  | C |  |  |
| 8 |  | CQ34010 | 六角螺母 | nut | 2 |  | D |  |  |
| 9 |  | 2909055-2E2 | 加强杆支承座总成（左） | seat assy-LH | 1 |  | D |  |  |
| 10 |  | 2909060-2E2 | 加强杆支承座总成（右） | seat assy-RH | 1 |  | D |  |  |
| 11 |  | Q40310 | 弹簧垫圈 | spring washer | 8 |  | C |  |  |
| 12 |  | Q151C1030 | 六角头螺栓 | bolt | 8 |  | D |  |  |
| 13 |  | Q40110 | 平垫圈 | plate washer | 8 |  | D |  |  |
| 14 |  | 2904065-2E2 | 支臂衬套总成 | Bushing assembly | 2 | Втулка нижнего рычага | C |  |  |
| 15 |  | Q151C1050 | 六角头螺栓 | hex bolt | 2 |  | D |  |  |
| 16 |  | Q341C10 | 螺母 | nut | 2 |  | D |  |  |
| 17 |  | Q40310 | 弹簧垫圈 | spring washer | 2 |  | C |  |  |
| 18 |  | CQ34112 | 六角螺母 | hex nut | 4 |  | D |  |  |
| 19 |  | Q40312 | 弹簧垫圈 | spring washer | 4 |  | C |  |  |
| 20 |  | 2904045-2E2 | 前轴支臂焊接总成（左） | cantilever welding assy-lower,LH | 1 | Рычаг передней подвески левый в сборе | C |  |  |
| 21 |  | 2904050-2E2 | 前轴支臂焊接总成（右） | cantilever welding assy-lower,RH | 1 | Рычаг передней подвески правый в сборе | C |  |  |
| 22 |  | Q5003025 | 开口销 | Cotter pin | 2 |  | C |  |  |
| 23 |  | Q387B12 | 六角开槽薄螺母 | nut | 2 |  | D |  |  |
| 24 |  | 2909035-2E2 | 加强杆焊接总成（左） | rod-tension welding assembly,LH | 1 | Растяжка передней подвески левая | D |  |  |
| 25 |  | 2909040-2E2 | 加强杆焊接总成（右） | rod-tension welding assembly,RH | 1 | Растяжка передней подвески правая | D |  |  |

| POWER TRAIN—Middle arm welding assembly ,front suspension | SECTION. NO.:02-2904-2 | PAGE:75 |
| --- | --- | --- |
| POWER TRAIN—Middle arm welding assembly,front suspension | SECTION. NO.:02-2904-2 | PAGE:76 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 26 |  | 2909023-2E2 | 加强杆垫圈Ⅱ | washer-thrust,tension rod | 2 |  | D |  |  |
| 27 |  | 2909021-2E2 | 加强杆衬套 | bushing mounting-tension rod | 4 |  | C |  |  |
| 28 |  | 2909022-2E2 | 加强杆垫圈Ⅰ | washer-thrust,tension rod | 2 |  | C |  |  |
| 29 |  | Q33812 | 非金属嵌件六角法兰面锁紧螺母 | locknut | 2 |  | C |  |  |
| 30 |  | 2906011-2E2 | 前稳定杆 | front stable pulling rod | 1 |  | D |  |  |
| 31 |  | 2906021-2E2 | 稳定杆安装支架 | bracket,stable pulling rod | 2 | Скоба подушки стабилизатора | D |  |  |
| 32 |  | 2906022-2E2 | 稳定杆安装衬套 | rubber bushing, stable pulling rod | 2 | Подушка стабилизатора | C |  |  |
| 33 |  | Q1460825 | 六角头螺栓弹簧垫圈和平垫圈组合件 | combined bolt | 2 |  | D |  |  |
| 34 |  | 2906030-2E2 | 连接杆总成 | joint lever | 2 | Стойка стабилизатора | C |  |  |
| 35 |  | 2906041-2E2 | 软垫 | rubber gasket | 4 |  | C |  |  |
| 36 |  | Q33008 | 全金属六角法兰面锁紧螺母 | locknut | 2 |  | D |  |  |
| 37 |  | Q32810 | 1型非金属嵌件六角锁紧螺母 | locknut | 2 |  | D |  |  |
| 38 |  | 2906042-2E2 | 垫圈 | washer | 4 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| POWER TRAIN—Rear Axle Housing And Half Axle | SECTION. NO.:02-2401 | PAGE:77 |
| --- | --- | --- |
| POWER TRAIN—Rear Axle Housing And Half Axle | SECTION. NO.:02-2401 | PAGE:78 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 1 | 2401010VC | 后桥壳总成 | Rear axle shaft tube | 1 | Картер заднего моста | D | CA1020VR |  |
| 2 |  | LZ111-2400107 | 通气塞 | Cap plug | 1 | Сапун заднего моста | D |  |  |
| 3 |  | SC1010-2401043B | 塑料垫圈 | Plastic seal | 1 |  | D |  |  |
| 4 |  | SC1012-2401108 | 加油螺塞 | Oil inlet plug | 1 | Пробка заливная заднего моста | D |  |  |
| 5 |  | LZ111-2400103 | 铜垫圈 | copper seal | 1 |  | D |  |  |
| 6 |  | JA1020-2400030 | 放油螺塞总成 | Oil outlet plug | 1 | Пробка сливная заднего моста | C |  |  |
| 7 |  | LZ111-2400015 | 特种螺栓 | bolt | 8 |  | D |  |  |
| 8 |  | JA1020-2400101-01 | 胶木垫 | Rubber pad | 1 | Прокладка редуктора заднего моста | C |  |  |
| 10 |  | JA1020-2403201 | 后桥半轴 | Half axle | 2 | Полуось заднего моста | D |  |  |
| 11 |  | SC6350-2403202 | 半轴垫圈 | Washer , half axle | 2 | Кольцо подшпника полуоси | D |  |  |
| 12 |  | GB/T276-94 | 滚动轴承6207-RS/P6 | Ball bearing, half axle | 2 | Подшипник полуоси | D |  |  |
| 13 |  | JA1020-2403203 | 半轴挡圈 | Thrust ring, half axle | 2 | Втулка подшипника полуоси | C |  |  |
| 14 |  | SC1012-2400020 | 半轴油封 | Oil seal ring assembly ,half axle | 2 | Сальник полуоси | D |  |  |
| 15 |  | SC6350-2400102B | 油封座 | Oil retainer plate , half axle | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  | 1020，1020 |  |

| POWER TRAIN—Final drive assembly | SECTION. NO.:02-2402-1 | PAGE:79 |
| --- | --- | --- |
| POWER TRAIN—Final drive assembly | SECTION. NO.:02-2402-1 | PAGE:80 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 0 |  |  | 主减速器及差速器总成 | Final drive assy | 1 | Редуктор заднего моста в сборе | C |  |  |
| 1 |  | JA1020-2402300 | 凸缘总成 | Flange assembly, driving gear | 1 | Фланец редуктора заднего моста | D |  |  |
| 2-1 |  | JA1020-2402105 | 主动锥齿轮 | Driving bevel gear | 1 |  | C |  |  |
| 2-2 |  | JA1020-2402106 | 从动锥齿轮 | driven bevel gear | 1 |  | D |  |  |
| 3 |  | JA1020-2402401--423 | 调整垫片 | Adjusting shim, driving bevel gear t=0.10 | 按需 |  | C |  |  |
| 4 |  | 30306X2B/P6X | 滚动轴承 | Taper Roller Bearing | 1 | Подшипник ведомой шестерни внутренний | C |  |  |
| 5 |  | LZ111-2402107 | 隔 套 | Wave Elastic bushing | 1 | Втулка ведомой шестерни РЗМ | C |  |  |
| 6 |  | LZ111-2402108 | 调整垫片(三) | Adjusting shim, driving bevel gear t=1.00 | 1 |  | C |  |  |
| 7 |  | 30305X2B/P6X | 滚动轴承 | Taper Roller Bearing | 1 | Подшипник ведомой шестерни наружний | C |  |  |
| 8 |  | LZ111-2402020 | 油 封 | Oil seal | 1 | Сальник хвостовика | C |  |  |
| 9 |  | JA1020-2402101 | 主减速器壳体 | Reducer housing and differential bearing cover | 1 |  | C |  |  |
| 10 |  | LZ111-2402112 | 垫 圈 | washer | 1 |  | C |  |  |
| 11 |  | LZ111-2402111-2 | 主动伞齿轮锁紧螺母 | Lock nut | 1 |  | D |  |  |
| 12 |  | LZ111-2403108 | 行星齿轮轴 | Shaft, planet pinion | 1 |  | D |  |  |
| 13 |  | JA1020-2403104 | 行星齿轮 | Planet pinion | 2 |  | D |  |  |
| 14 |  | LZ111-2403106 | 球面垫片 | Shim | 2 |  | D |  |  |
| 15 |  | JA1020-2403103 | 半轴齿轮 | Half axle gear | 2 |  | C |  |  |
| 16 |  | LZW6370A-L01-2403102 | 调整垫片 | Adjusting shim | 按需 |  | D |  |  |
| 17 |  | JA1020-2403101 | 差速器壳 | Differential housing | 1 |  | D |  |  |
| 18 |  | GB/T119.2-2000 | 销5×25 | pin | 1 |  | D |  |  |
| 19 |  | JA1020-2403111 | 螺 栓 | bolt | 10 |  | D |  |  |
| 20 |  | 32008×1WC | 滚动轴承 | Taper Roller Bearing | 2 | Подшипник дифференциала | D |  |  |
| 21 |  | JA1020-2402501～545 | 调整垫片 | Adjusting shim | 按需 |  | C |  |  |
| 22 |  |  | 差速器总成 | Differential assy | 1 | Дифференциал в сборе | C |  |  |
| 24 |  | GB/T5782-2000 | 螺栓 M10X50 | bolt | 4 |  | C |  |  |
| 26 |  | GB/T6170-2000 | 螺母M8 | nut | 8 |  | D |  |  |
|  |  |  |  |  |  |  |  | 1020，1020 |  |

| POWER TRAIN—Rear leaf spring assembly | SECTION. NO.:02-2912 | PAGE:83 |
| --- | --- | --- |
| POWER TRAIN—Rear leaf spring assembly | SECTION. NO.:02-2912 | PAGE:84 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2912010-4E2 | 后钢板弹簧总成 | Rear leaf spring assembly | 2 | Рессора задняя | D |  |  |
| 2 |  | 2912030-4E2 | 后钢板弹簧缓冲块总成 | Cushion block assembly , rear leaf spring | 2 | Подушка задней рессоры | D |  |  |
| 3 |  | 2912041-4E2 | 后板簧U型螺栓 | U-bolt , rear leaf spring | 4 | Стремянка задней рессоры | D |  |  |
| 4 |  | 2912042-4E2 | 垫片 | washer | 2 | Прокладка стремя нок задней рессоры | D |  |  |
| 5 |  | Q40312 | 弹簧垫圈 | Lock washer | 8 | Шайба стремянки задней ресссоры | C |  |  |
| 6 |  | Q341B12 | 六角螺母 | nut | 8 | Гайка стремянки задней рессоры | D |  |  |
| 7 |  | CQ1611290 | 六角头螺栓 | bolt | 2 | Палец задней рессоры | C |  |  |
| 8 |  | Q40312 | 弹簧垫圈 | Lock washer | 2 | Шайба пальца рессоры | C |  |  |
| 9 |  | CQ34112 | 六角头螺母 | nut | 2 | Гайка пальца ресссоры | D |  |  |
| 10 |  | 2912060-4E2 | 外侧板总成 | Side outer plate | 2 | Серьга рессоры с болтами | C |  |  |
| 11 |  | 2912064-4E2 | 后钢板弹簧吊耳上衬套 | Rubber bushing-rear leaf spring | 4 | Втулка серьги рессоры | D |  |  |
| 12 |  | 2912062-4E2 | 吊耳内侧板 | Side inner plate | 2 | Серьга рессоры под болты | D |  |  |
| 13 |  | Q40310 | 弹簧垫圈 | Lock washer | 4 |  | D |  |  |
| 14 |  | CQ34110 | 六角头螺母 | nut | 2 |  | C |  |  |
| 15 |  | Q151B1255 | 六角头螺栓 | bolt | 2 | Палец амортизатора | D |  |  |
| 16 |  | Q40312 | 弹簧垫圈 | Lock washer | 2 | Шайба пальца амортизатора | C |  |  |
| 17 |  | Q341B12 | 六角螺母 | nut | 2 | Гайка пальца амортизатора | D |  |  |
| 18 |  | 2915010-4E2 | 后减振器总成 | Rear shock absorber assembly | 2 | Амортизатор задий | C |  |  |
| 19 |  | Q40110 | 平垫圈 | washer | 2 |  | C |  |  |
| 20 |  | Q40310 | 弹簧垫圈 | Lock washer | 2 |  | D |  |  |
| 21 |  | CQ34010 | 六角螺母 | nut | 2 |  | D |  |  |

| POWER TRAIN—Wheel and Tyre | SECTION. NO.:02-3101 | PAGE:85 |
| --- | --- | --- |
| POWER TRAIN—Wheel and Tyre | SECTION. NO.:02-3101 | PAGE:86 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 3101015-2E2 | 5.00B×13车轮总成 | 13 x 5.00b wheel assembly | 5 | Диск колеса(металл) | D | standard |  |
| 2 | O1 | 3103017-V01 | 车轮螺母 | Nut , wheel | 20 |  | D | standard |  |
| 3 | O1 | 3106010-4E2 | 轮胎总成165/70R13 | 165/70 r13 tyre assembly | 5 | Шина | C | standard |  |
| 4 | O1 | 3106015-V01 | 气门嘴总成（Z2-01-2） | Value （Z2-01-2） | 5 |  | C | standard |  |
| 5 | O1 | 3101020-V01 | 车轮平衡重 | Wheel balancing fixture | 1 |  | D | standard |  |

| POWER TRAIN—Spare wheel bracket -hanger | SECTION. NO.:02-3105 | PAGE:87 |
| --- | --- | --- |
| POWER TRAIN—Spare wheel bracket-hanger | SECTION. NO.:02-3105 | PAGE:88 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3105010A4E2 | 备胎架焊接总成 | Spare wheel bracket - hanger | 1 | Полка крепления запасного колеса | D |  |  |
| 2 |  | 3105021-4E2 | 备胎架吊杆 | Spare wheel bracket Rod | 1 | Фикатор полки запасного колеса | D |  |  |
| 3 |  | Q33012 | 全金属六角法兰面锁紧螺母 | Nut | 2 | Гайка фиксатора запасного колеса | D |  |  |
| 4 |  | CQ1500616 | 六角头导颈螺栓 | Combined bolt | 2 |  | D |  |  |

| STEERING- Steering Gear Box | SECTION. NO.:03-3401 | PAGE:89 |
| --- | --- | --- |
| STEERING- Steering Gear Box | SECTION. NO.:02-3401 | PAGE:90 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 1 | 3401010-2E2 | 转向器带拉杆总成 | Steering gear box with ball pin assembly | 1 | Рейка рулевая в сборе | D |  |  |
| 1 | 2 | 3401020-2E2 | 转向器总成 | Steering gear box assembly | 1 |  | D |  |  |
| 2 |  | Q32712 | 六角尼龙圈锁紧薄螺母 | Lock Nut | 2 |  | C |  |  |
| 3 |  | 3003040-2E2 | 右球销总成 | Right ball pin | 1 | Тяга рулевой рейки правая | C |  |  |
| 4 |  | 3003012-2E2 | 右防护套 | Right protect rubber bushing | 1 | Пыльник рулевой рейки правый | C |  |  |
| 5 |  | 3400021-2E2 | 转向器支架Ⅱ | Bracket II, Steering gear box | 1 |  | D |  |  |
| 6 |  | Q1420830 | 六角头螺栓和弹簧垫圈组合件 | combined Bolt | 4 |  | D |  |  |
| 7 |  | 3400011-2E2 | 转向器支架Ⅰ | Bracket I, Steering gear box | 1 |  | D |  |  |
| 8 |  | 3401011-2E2 | 齿轮轴防尘罩 | Dust cover, Gear shaft | 1 |  | C |  |  |
| 9 |  | 3003011-2E2 | 左防护套 | Left protect rubber bushing | 1 | Пыльник рулевой рейки левый | C |  |  |
| 10 |  | 3003035-2E2 | 左球销总成 | Left ball pin | 1 | Тяга рулевой рейки левая | C |  |  |
| 11 |  | Q1460835 | 六角头螺栓弹簧垫圈和平垫圈组合件 | combined Bolt | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| STEERING-Steering Wheel | SECTION. NO.:03-3402 | PAGE:91 |
| --- | --- | --- |
| STEERING-Steering Wheel | SECTION. NO.:03-3402 | PAGE:92 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 3402010A1J0 | 转向盘总成 | Steering wheel assembly | 1 | Колесо рулевое в сборе | D |  |  |
| 2 | O1 | Q40312 | 弹簧垫圈 | Spring washer | 1 |  | C |  |  |
| 3 | O1 | CQ34012 | 螺母 | Nut | 1 |  | D |  |  |
| 4 | O1 | 3402020A1J0 | 上盖总成 | Upper cover ,steering wheel | 1 |  | C |  |  |
| 5 | O1 | 3735021-2E2 | 组合开关上壳体 | Upper plastic cover, Combined switch | 1 | Накладка подрулевых переключателей верхняя | D |  |  |
| 6 | O1 | Q2204213 | 十字槽盘头组合自攻螺钉 | Screw | 2 |  | D |  |  |
| 7 | O1 | 3735031-1J0 | 转向柱护罩 | Cover, Steering shaft | 1 | Накладка рулевой колонки нижняя | D |  |  |
| 8 | O1 | 3735023-1J0 | 组合开关下壳体 | Lower plastic cover, Combined switch | 1 | Накладка подрулевых переключателей нижняя | D |  |  |
| 9 | O1 | Q2204819 | 十字槽盘头组合自攻螺钉 | Screw | 2 |  | D |  |  |
| 10 | O1 | Q2360520 | 十字槽盘头组合螺钉 | Screw | 4 |  | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| STEERING-Steering shaft | SECTION. NO.:03-3404 | PAGE:93 |
| --- | --- | --- |
| STEERING-Steering shaft | SECTION. NO.:03-3404 | PAGE:94 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3404020-2E2 | 转向轴(上)总成 | Steering shaft(upper) | 1 | Вал рулевой верхняя часть в сбор | D |  |  |
| 2 |  | 3404050-2E2 | 转向轴(下)总成 | Steering shaft(lower) | 1 | Вал карданный рулевой нижняя часть в сборе | D |  |  |
| 3 |  | Q1460830 | 六角头螺栓、弹簧垫圈和平垫圈组合件 | Combined Bolt | 2 |  | D |  |  |
| 4 |  | Q32008 | 六角法兰面螺母 | Hex Nut | 2 |  | D |  |  |
| 5 |  | Q1420830 | 六角头螺栓和弹簧垫圈组合件 | combined Bolt | 2 |  | D |  |  |
| 6 |  | 3404011-2E2 | 转向轴防尘罩 | Rubber dust cover, steering shaft | 1 | Пыльник рулевой колонки | C |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BRAKE-Front Brake Disc | SECTION. NO.:04-3501 | PAGE:95 |
| --- | --- | --- |
| BRAKE- Front Brake Disc | SECTION. NO.:04-3501 | PAGE:96 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3501015-2E2 | 前左制动钳总成 | Brake clamp assembly (left) | 1 | Скоба переднего тормоза левая в сборе | C |  |  |
| 2 |  | 3501020-2E2 | 前右制动钳总成 | Front brake assembly(right) | 1 | Скоба переднего тормоза правая в сборе | C |  |  |
| 3 |  | 3501050-2E2 | 内侧制动块 | Inner side brake block assembly | 2 | Колодка тормознаяпередняя внутренняя | B |  |  |
| 4 |  | 3501060-2E2 | 外侧制动块 | Outer side brake block assembly | 2 | Колодка тормозная передняя наружняя | B |  |  |
| 5 |  | 3501106-2E2 | 制动盘 | Braking plate | 2 | Диск переднего тормоза | C |  |  |
| 6 |  | 3501100-2E2 | 前右制动盘防尘罩总成 | Dust cover(right) | 1 | Щит переднего тормоза правый | D |  |  |
| 7 |  | 3501095-2E2 | 前左制动盘防尘罩总成 | Dust cover(left) | 1 | Щит переднего тормоза левый | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BRAKE-Rear brake Drum | SECTION. NO.:04-3502 | PAGE:97 |
| --- | --- | --- |
| BRAKE-Rear Brake Drum | SECTION. NO.:04-3502 | PAGE:98 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 0 | O1 | 3502015-4E2 | 后左制动器总成 | Brake assembly, RL | 1 | Щит заднего тормоза левый в сборе | D |  |  |
|  | O2 | 3502020-4E2 | 后右制动器总成 | Brake assembly, RR | 1 | Щит заднего тормоза правый в сборе | D |  |  |
| 1 | O1 | 3502025-VOl | 后左制动底板总成 | Brake plate assembly, RL | 1 | Щит заднего тормоза левый (голый) | D |  |  |
|  | O1 | 3502030-V01 | 后右制动底板总成 | Brake plate assembly, RR | 1 | Щит заднего тормоза правый (голый) | D |  |  |
| 2 | O1 | Q1860612 | 螺栓 | bolt | 4 |  | D |  |  |
| 3 | O1 | CQ34008/Q40308 | 螺母/弹簧垫圈 | NUT/WASHER | 8set |  | D/C |  |  |
| 4 | O1 | 3502117—VOl | 定位簧销钉 | PIN,Returning spring | 4 |  | D |  |  |
| 5 | O1 | 3502050-V01 | 制动蹄总成 | BRAKE SHOE ASSY | 4 | Колодка задняя тормозная | B |  |  |
| 6 | O1 | 3502114-V01 | 制动蹄下端拉簧 | LOWER SPRING，BRAKE SHOE | 2 | Пружина стяжная задних тормозных колодок нижняя | C |  |  |
| 7 | O1 | 3502116—VOl | 制动蹄定位簧 | BRAKE SHOE LOWER SPRING | 4 |  | D |  |  |
| 8 | O1 | 3502100—VOl | 后右制动间隙自调机构总成 | Brake clearance self-adjusting mechanism,RR | 2 | Рычаг разводной тормозных колодок | D |  |  |
|  | O2 | 3502095—VOl | 后左制动间隙自调机构总成 | Brake clearance self-adjusting mechanism,RL | 2 |  | D |  |  |
| 9 | O1 | 3502113—VOl | 制动蹄回位弹簧 | BRAKE SHOE RETURNING SPRING | 4 | Пружина стяжная тормозных колодок верхняя левая | C |  |  |
| 10 | O1 | 3502111-V01 | 后制动蹄与推板拉簧 | REAR BRAKE SHOE AND PULL SPRING | 2 | Пружина стяжная тормозных колодок верхняя правая | C |  |  |
| 11 | O1 | Q43660 | 开口挡圈 | COTTER RATAIN WASHER | 2 |  | C |  |  |
| 12 | O1 | 3502092—VOl | 后右驻车制动拉臂 | BRAKE PULL ARM，RR,REAR BRAKE DRUM | 1 |  | D |  |  |
|  | O2 | 3502091-V01 | 后左驻车制动拉臂 | BRAKE PULL ARM，RL,REAR BRAKE DRUM | 1 |  | D |  |  |
| 13 | O1 | 3502093-V01 | 拉臂销轴 | PULL ARM PIN SHAFT | 2 |  | D |  |  |
| 14 | O1 | 3502065-2E2 | 后左制动分泵总成 | Brake slave cylinder assembly,RL | 1 | Цилиндр задний тормозной левый | C |  |  |
|  | O2 | 3502070—2E2 | 后右制动分泵总成 | Brake slave cylinder assembly,RR | 1 | Цилиндр задний тормозной правый | C |  |  |
| 15 | O1 | CQ1460820 | 底板固定螺栓 | BOLT | 8 |  | D |  |  |

| BRAKE-brake piping and control | SECTION. NO.:04-3506 | PAGE:99 |
| --- | --- | --- |
| BRAKE- brake piping and control | SECTION. NO.:04-3506 | PAGE:100 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3506115-2E2 | 油管总成-总泵第二腔至三路接头 | TUBE ASSY-BRAKE | 1 |  | D |  |  |
| 2 |  | 3506110-2E2 | 油管总成-总泵第一腔至三路接头 | TUBE ASSY-BRAKE | 1 |  | D |  |  |
| 3 |  | 3506140-2E2 | 油管总成-六通接头至右前制动软管 | TUBE ASSY-BRAKE | 1 | Трубка тормозная к правому тормозному шлангу | D |  |  |
| 4 |  | 3506135-2E2 | 油管总成-六通接头至左前制动软管 | TUBE ASSY-BRAKE | 1 | Трубка тормозная к левому тормозному шлангу | D |  |  |
| 5 |  | 3506120-2E2 | 油管总成-三路接头前左口至六通接头前左口 | TUBE ASSY-BRAKE | 1 |  | D |  |  |
| 6 |  | 3506125-2E2 | 油管总成-三路接头前右口至六通接头前右口 | TUBE ASSY-BRAKE | 1 |  | D |  |  |
| 7 | 1 | 3506145-4E2 | 油管总成-六通接头至感载比例阀Ⅰ | TUBE ASSY-BRAKE | 1 |  | D |  |  |
| 8 | 1 | 3506150-4E2 | 油管总成-六通接头至感载比例阀Ⅱ | TUBE ASSY-BRAKE | 1 | Шланг переднего тормоза (к суппорту) | D |  |  |
| 9 |  | 3506070-2E2 | 前制动软管总成 | HOSE ASSY-FRONT BRAKE | 2 | Тройник тормозной??? | C |  |  |
| 10 |  | 3506190-1J0 | 三路接头总成 | THREE WAY CONNECTOR-BRAKE TUBE | 1 | Тройник тормозной | D |  |  |
| 11 |  | 3506076-2E2 | 六通接头 | SIX WAY CONNECTOR | 1 |  | D |  |  |
| 12 |  | 3506197-1J0 | 三路接头衬垫 | LINER, THREE WAY CONNECTOR | 1 |  | C |  |  |
| 13 |  | 3506219-2E2 | 制动油管夹子Ⅳ | CLIP-TUBE,BRAKE Ⅳ | 2 |  | D |  |  |
| 14 |  | 3506218-2E2 | 制动油管夹子Ⅲ | CLIP-TUBE,BRAKE Ⅲ | 1 |  | D |  |  |
| 15 |  | 3506217-2E2 | 制动油管夹子Ⅱ | CLIP-TUBE,BRAKE Ⅱ | 7 |  | D |  |  |
| 16 |  | 3506091-V01 | L型弹簧卡片 | SPRING CLIP-BRAKE HOSE | 6 |  | C |  |  |
| 17 |  | Q1840825 | 六角法兰面螺栓 | HEX BOLT | 2 |  | D |  |  |
| 18 |  | Q32006 | 六角法兰面螺母 | NUT | 2 |  | D |  |  |
| 19 |  | 3506155-4E2 | 油管总成-感载比例阀至后制动软管 | TUBE ASSY-BRAKE | 1 | Трубка тормозная к правому заднему колесу | D |  |  |
| 20 |  | 3506160-4E2 | 油管总成-后制动软管至后右制动器 | TUBE ASSY-BRAKE | 1 | Трубка тормозная к левому заднему колесу | D |  |  |
| 21 |  | 3506165-4E2 | 油管总成-后右制动器至后左制动器 | TUBE ASSY-BRAKE | 1 | Шланг тормозной распределителя тормозных сил | D |  |  |
| 22 |  | 3506095-4E2 | 后制动软管总成 | HOSE ASSY-REAR BRAKE | 1 | Распределитель тормозных сил | C |  |  |
| 23 |  | 3527010-4E2 | 液压感载比例阀总成 | LOADING LEVEL VALUE ASSY | 1 |  | D |  |  |
| 24 |  | Q68506F4 | 一端固定式双管夹片 | CLIP-TUBE,BRAKE | 1 |  | D |  |  |
| 25 |  | Q68606F4 | 单管夹片 | CLIP-TUBE,BRAKE | 4 |  | D |  |  |
| 26 |  | Q2716313 | 十字槽盘头自攻螺钉 | SCREW | 5 |  | D |  |  |
| 27 |  | CQ1460820 | 组合螺栓 | BOLT | 2 |  | D |  |  |
| 28 |  | Q32008 | 六角法兰面螺母 | NUT | 1 |  | D |  |  |

| BRAKE-Brake master cylinder,vacuum booster | SECTION. NO.:04-3506 | PAGE:101 |
| --- | --- | --- |
| BRAKE-Brake master cylinder,vacuum booster | SECTION. NO.:04-3506 | PAGE:102 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3506015-2E2 | 制动储液罐总成 | BRAKE OIL TANK | 1 | Бачек тормозного цилиндра | C |  |  |
| 2 |  | 3506020-2E2 | 制动储液罐支架焊接总成 | BRACKET-BRAKE OIL TANK | 1 |  | D |  |  |
| 3 |  | Q32006 | 六角兰面螺母 | NUT | 4 |  | D |  |  |
| 4 |  | CQ34006 | 六角螺母 | NUT | 1 |  | D |  |  |
| 5 |  | 3506031-2E2 | 橡胶套 | GLUE SLEEVE | 1 |  | C |  |  |
| 6 |  | 3506026-2E2 | 输油胶管Ⅰ | OIL PIPE I | 1 | Шланг главного цилиндра задний | C |  |  |
| 7 |  | 3506027-2E2 | 输油胶管Ⅱ | OIL PIPE II | 1 | Шланг главног цилиндра сцепления передний | C |  |  |
| 8 |  | CQ67516 | 蜗杆传动式软管夹箍 | Clip | 4 |  | C |  |  |
| 9 |  | 3506044-2E2 | 真空制动软管Ⅳ | VACUUM SOFT PIPE IV | 1 | Шланг вакуумного усилителя | C |  |  |
| 10 |  | 3506043-2E2 | 真空制动软管Ⅲ | VACUUM SOFT PIPE III | 1 |  | C |  |  |
| 11 |  | 3506042-2E2 | 真空制动软管Ⅱ | VACUUM SOFT PIPE II | 1 |  | C |  |  |
| 12 |  | 3506041-2E2 | 真空制动软管Ⅰ | VACUUM SOFT PIPE I | 1 |  | C |  |  |
| 13 |  | 3506050-2E2 | 真空管Ⅱ总成 | VACUUM PIPE I | 1 |  | D |  |  |
| 14 |  | 3506045-2E2 | 真空管Ⅰ总成 | VACUUM PIPE I | 1 |  | D |  |  |
| 15 |  | 3506052-2E2 | 真空管支架 | BRACKET-VACUUM PIPE | 1 |  | D |  |  |
| 16 |  | Q673B17 | 钢带弹性环箍 | CLIP | 8 |  | C |  |  |
| 17 |  | Q2360616 | 十字槽平圆头组合螺钉 | SCREW | 1 |  | D |  |  |
| 18 |  | 3505010-2E2 | 制动总泵总成 | BRAKE MASTER CYLINDER ASSY | 1 | Цилиндр главный тормозной | C |  |  |
| 19 |  | CQ34008 | 螺母 | NUT | 2 |  | D |  |  |
| 20 |  | 3510010-2E2 | 真空助力器总成 | VACUUM BOOSTER ASSY | 1 | Вакуумный усилитель | C |  |  |
| 21--1 |  | Q5101022 | 平头销 | PIN | 1 |  | D |  |  |
| 21--2 |  | Q5003025 | 开口销 | PIN | 1 |  | C |  |  |
| 22 |  | 3506190-1J0 | 三路接头总成 | THREE WAY CONNECTOR | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BRAKE-Parking brake control | SECTION. NO.:04-3508 | PAGE:103 |
| --- | --- | --- |
| BRAKE- Parking brake control | SECTION. NO.:04-3508 | PAGE:104 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3508010-2E2 | 驻车制动操纵手柄总成 | PARKING BRAKE HANDLE | 1 | Рычаг стояночного тормоза в сборе | C |  |  |
| 2 |  | 3818010-2E2 | 手制动灯开关总成 | HAND BRAKE SWITCH ASSY | 1 |  | Ｃ |  |  |
| 3 |  | CQ1460820 | 组合螺栓 | BOLT | 2 |  | Ｄ |  |  |
| 4 |  | 3508110-4E2 | 前驻车制动拉索总成 | CABLE ASSY,PARKING BRAKE | 1 | Трос стояночного тормоза передний | Ｃ |  |  |
| 5 | 1 | 3508140-4E2 | 后右驻车制动拉索带夹子总成 | CABLE ASSY,PARKING BRAKE,REAR, RH | 1 | Трос стояночного тормоза правый | Ｃ |  |  |
| 6 | 1 | 3508135-4E2 | 后左驻车制动拉索带夹子总成 | CABLE ASSY,PARKING BRAKE,REAR, LH | 1 | Трос стояночного тормоза левый | Ｃ |  |  |
| 7 |  | 3508171-V01 | 卡簧 | PLATE-CABLE LOCK,PARKING BRAKE | 2 |  | Ｃ |  |  |
| 8 |  | 3508161-2E2 | 回位弹簧-驻车拉索 | Returning spring, parking brake | 1 | Пружина стяжная тросов стояночного тормоза | Ｃ |  |  |
| 9 |  | CQ1460612 | 六角头螺栓弹簧垫圈和平垫圈组合件 | Combined bolt | 4 |  | Ｄ |  |  |
| 10 |  | Q33006 | 全金属六角法兰面螺母 | Lock nut | 1 |  | Ｃ |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BODY ELECTRICAL-Lamps,speaker,battery & relay | SECTION. NO.:05-3711-1 | PAGE:105 |
| --- | --- | --- |
| BODY ELECTRICAL-Lamps,speaker,battery & relay | SECTION. NO:05-3711-1 | PAGE:106 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3711015-2E2 | 左组合前灯总成 | left front combined light assy | 1 | Фара передняя левая | B |  |  |
|  |  | 3711020-2E2 | 右组合前灯总成 | right front combined light assy | 1 | Фара передняя правая | B |  |  |
| 2 |  | 7901030-V01 | 扬声器总成 | speaker | 2 |  | C |  |  |
| 3 |  | 3721010-2E2 | 电喇叭总成 | horn assy | 1 | Сигнал звуковой | C |  |  |
| 4 |  | 3720010-6J6 | 制动灯开关总成 | brake light switch assy | 1 |  | C |  |  |
| 5 |  | 3722111-2E2 | 中央配电盒 | center match electricity box | 1 |  | C |  |  |
| 6 |  | 7903010-1J0 | 天线总成 | antenna assy | 1 |  | C |  |  |
| 8 |  | 3751080C2E2 | 继电器盒总成 | relay cover assy | 1 |  | C |  |  |
| 9 |  | 7901010AVO1 | 收放机总成 | radio/cassette | 1 | магнитола | C |  |  |
| 10 |  | 3820010-8J0 | 组合仪表总成 | instrument cluster assy | 1 | Комбинация приборов | C |  |  |
| 11 |  | 3732220-2E2 | 后雾灯开关总成 | rear frog light switch assy | 1 |  | C |  |  |
| 13 |  | 3726015-2E2 | 左侧转向灯总成 | side turning light assy,lh | 1 | Повторитель поворотов боковой | B |  |  |
|  |  | 3726020-2E2 | 右侧转向灯总成 | side turning light assy,rh | 1 |  | B |  |  |
| 14 |  | 3714010-2E2 | 前室内灯总成 | front chamber light assy | 1 |  | C |  |  |
| 15 |  | 3818010-2E2 | 手制动开关总成 | hand brake swtich assy | 1 |  | C |  |  |
| 16 |  | 3808010-V09 | 水温传感器 | water temperature transducer assy | 1 |  | C |  |  |
| 17 |  | 3735010-2J0 | 组合开关总成 | combined switch assy | 1 | Переключатель подрулевой | C |  |  |
| 18 |  | 3703010-V01B1` | 蓄电池总成 | battery assy | 1 |  | C |  |  |
| 19 |  | 3820015-V06 | 车速里程表电子传感器 | electric sensor assy,speed | 1 |  | C |  |  |
| 20 |  | 3732105-4E2 | 左后雾灯总成 | left rear frog light assy | 1 | Фонарь задний габаритный задний левый | B |  |  |
|  |  | 3732110-4E2 | 右后雾灯总成 | right rear frog light assy | 1 | Фонарь задний габаритный правый | B |  |  |
| 21 |  | 3717010-6J6 | 牌照灯总成 | license plate assy | 2 | Фонарь освещения номерного знака 6350 | B |  |  |
| 22 |  | 3773015-4E2 | 左组合后灯总成 | left rear combined light assy | 1 | Фонарь задний левый 1021VR | B | CA1020VR |  |
| 23 |  | 3773020-4E2 | 右组合后灯总成 | right rear combined light assy | 1 | Фонарь задний правый 1021VR | B | CA1020VR |  |

| BODY ELECTRICAL-Windshield Wiper | SECTION. NO.:05-5205 | PAGE:109 |
| --- | --- | --- |
| BODY ELECTRICAL- Windshield Wiper | SECTION. NO-05-5205 | PAGE:110 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 5205030-2E2 | 刮水器传动杆总成 | Transmission rod assembly , wiper | 1 | C | Трапеция стеклоочистителя | standard |  |
| 2 | O1 | Q32006 | 六角法蓝面螺母 | Nut | 4 | D |  | standard |  |
| 3 | O1 | 5205045-2E2 | 左雨刷摆臂总成 | left wiper arm assy | 1 | C | Рычаг стеклоочистителя левый со щеткой в сборе | standard |  |
| 4 | O1 | 5205050-2E2 | 右雨刷摆臂总成 | right wiper arm assy | 1 | C | Рычаг стеклоочистителя правый со щеткой в сборе | standard |  |
| 5 | O1 | 5205091-2E2 | 卡帽 | cap | 2 | C |  | standard |  |
| 6 | O1 | 5205092-2E2 | 固定螺母 | nut | 2 | D |  | standard |  |
| 7 | O1 | 5205130-2E2 | 刮水电机及固定板总成 | Motor and fixed board assembly , wiper | 1 | C | Мотор стеклоочистителя | standard |  |
| 8 | O1 | Q174B0616 | 十字槽凹穴六角头螺栓 | bolt | 3 | D |  | standard |  |
| 9 | O1 | 5207051-2E2 | 右输水管 | right water pipe | 1 | C |  | standard |  |
| 10 | O1 | 5207055-2E2 | 输水单向阀总成 | transport wate unilateralism assy | 2 | C |  | standard |  |
| 11 | O1 | 5207060-2E2 | 喷嘴总成 | Nozzle assy | 2 | C | Форсунка стеклоочистителя | standard |  |
| 12 | O1 | 5207067-2E2 | 喷嘴连接胶管 | nozzle connect rubber pipe | 2 | C |  | standard |  |
| 13 | O1 | 5207046-2E2 | 左输水管 | left water pipe | 1 | C |  | standard |  |
| 14 | O1 | 5207041-2E2 | 水管三通接头 | water pipe three-connector | 1 | C |  | standard |  |
| 15 | O1 | 5207042-2E2 | 洗涤器前输水管 | syringe front water pipe | 1 | C |  | standard |  |
| 16 | O1 | 5207010-2E2 | 洗涤器水盒总成 | syringe water cover assy | 1 | C | Бачек стеклоочистителя | standard |  |
| 17 | O1 |  | 喷水电机 | spray engine | 1 | C | Мотор бочка стеклоочистителя | standard |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY ELECTRICAL-Wiring harness | SECTION. NO.:05-3724 | PAGE:111 |
| --- | --- | --- |
| BODY ELECTRICAL- Wiring harness | SECTION. NO-05-3724 | PAGE:112 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3724060-4E2 | 前舱电线束总成 | front cabin wire assy | 1 |  | C |  |  |
| 2 |  | 3724021-2E2 | 橡胶护套 | rubber jacket | 1 |  | C |  |  |
| 3 |  | 3724020-4E2 | 车身电线束总成 | wire assembly , cab | 1 | Жгут проводов панели приборов | C |  |  |
| 4 |  | 3724070－4E2 | 左前门电线束总成 | wire assy,left front door | 1 |  | C |  |  |
| 5 |  | 3724080－4E2 | 右前门电线束总成 | wire assy,right front door | 1 |  | C |  |  |
| 6 |  | 3724090-4E2 | 室内灯电线束总成 | wire assembly , license light | 1 |  | C |  |  |
| 7 |  | 3724030-4E2 | 底盘电线束总成 | wire assembly , chassis | 1 |  | C | CA1020VR |  |
|  |  | 3724030-3E2 | 底盘电线束总成 | wire assembly , chassis | 1 |  | C | CA1020V |  |
| 8 |  | 3724017-8J0 | 发电机导线-接蓄电池正极 | wire | 1 |  | C |  |  |
| 9 |  | 3724070-6J6 | 搭铁线总成 | wire assy | 1 |  | C |  |  |
| 10 |  | 3724040-4E2 | 电线总成-接蓄电池正极 | Wire Assembly, Battery Positive Pole | 1 |  | C | CA1020VR |  |
|  |  | 3724040-3E2 | 电线总成-接蓄电池正极 | Wire Assembly, Battery Positive Pole |  |  |  | CA1020V |  |
| 11 |  | 3724035-2E2 | 易熔线 | fuse wire | 2 |  | C |  |  |
| 12 |  | 3724050-4E2 | 电线总成-接蓄电池负极 | Wire Assembly, Battery Negative Pole | 1 |  | C | CA1020VR |  |
|  |  | 3724050-3E2 | 电线总成-接蓄电池负极 | Wire Assembly, Battery Negative Pole | 1 |  | C | CA1020V |  |

| BODY ELECTRICAL-Heater Unit | SECTION. NO.:05-8101 | PAGE:113 |
| --- | --- | --- |
| BODY ELECTRICAL-Heater Unit | SECTION. NO.:05-8101 | PAGE:114 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 8101015-2E2 | 水箱总成 | Water tank assy, heater | 1 | Радиатор отопителя | C |  |  |
| 2 |  | 8101035-2E2 | 电机总成 | Motor assy, heater | 1 | Мотор отопителя | C |  |  |
| 3 |  | 8101050-2E2 | 暖风机叶轮 | impeller fan w/o motor,heater | 1 | Крыльчатка мотора отопителя | C |  |  |
| 4 |  | 8101055-2E2 | 暖风机调速电阻总成 | Resistance assy,heater | 1 | Реастат отопителя | C |  |  |
| 5 |  | 8101061-2E2 | 暖风机左壳体 | Left body cover,Heater | 1 | Кожуж отопителя левый | C |  |  |
| 6 |  | 8101062-2E2 | 暖风机右壳体 | Right body cover,heater | 1 | Кожух отопителя правый | C |  |  |
| 7 |  | 8101063-2E2 | 拉线卡子 | Clamp.heater | 3 |  | C |  |  |
| 8 |  | 8101071-2E2 | 状态摆动杆 | Swing pole,heater | 1 |  | D |  |  |
| 9 |  | 8101076-2E2 | 冷暖风门摇臂 | Rocker,cool to heat | 1 |  | D |  |  |
| 10 |  | VOl-350 | 弹簧夹子 | Spring clamp | 6 | Зажим крепежный кожухов отопителя | C |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BODY ELECTRICAL-Nozzle & Duct–Ventilation,defroster | SECTION. NO.:05-8102 | PAGE:115 |
| --- | --- | --- |
| BODY ELECTRICAL-Nozzle & Duct - Ventilation,defroster | SECTION.NO.:05-8102 | PAGE:116 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | Q2714216 | 十字槽盘头自攻螺钉 | Screw-tapping | 4 |  | D | standard |  |
| 2 | O1 | 8112010-2E2 | 操纵机构总成 | Control assy,heater | 1 |  | C | for heater |  |
|  | O2 | 8112901-2E2 | 操纵机构总成及电器开关合件 | Control assy and a/c switch assy | 1 |  | C | w/collor |  |
| 3 | O1 | 8101010-2E2 | 暖风机总成 | Heater unit assy | 1 |  | C | standard |  |
| 4 | O1 | 8101045-2E2 | 风箱连接管总成 | air Connect hose assy,heater | 1 |  | C | for heater |  |
| 5 | O1 | Q174B0620 | 十字槽凹穴六角头螺栓 | Bolt | 1 |  | D | standard |  |
| 6 | O1 | Q40206 | 大垫圈 | Washer | 1 |  | D | standard |  |
| 7 | O1 | 8101240-2E2 | 换气箱总成 | Exchange air box assy | 1 |  | C | standard |  |
| 8 | O1 | 8101122-2E2 | 暖风出水胶管 | Hose,water outlet,heater | 1 |  | C | standard |  |
| 9 | O1 | 8101117-2E2 | 暖风进水胶管2 | Hose 2,water inlet,heater | 1 |  | C | standard |  |
| 10 | O1 | Q673B17 | 弹性环箍 | Spring clamp | 6 |  | C | standard |  |
| 11 | O1 | 8101116-2E2 | 暖风进水胶管1 | Hose 1-water inlet | 1 |  | C | standard |  |
| 12 | O1 | 8102036-2E2 | 左侧窗除霜风道 | Nozzle-side demister,LH | 1 |  | C | standard |  |
| 13 | O1 | 8102030-2E2 | 前风窗除霜风道总成 | Nozzle-demister-front window | 1 |  | C | standard |  |
| 14 | O1 | 8102041-2E2 | 右侧窗除霜风道 | Nozzle-side demister,RH | 1 |  | C | standard |  |
| 15 | O1 | Q2204813 | 十字槽盘头自攻螺钉和平垫圈组合 | Combined screw and washer-tapping | 12 |  | D | standard |  |
| 16 | O1 | 8102056-2E2 | 左风道 | Duct-demister,LH | 1 |  | C | standard |  |
| 17 | O1 | 8102050-2E2 | 中央风道总成 | Duct-central ventilator | 1 |  | C | standard |  |
| 18 | O1 | 8102061-2E2 | 右风道 | Duct-demister,RH | 1 |  | C | standard |  |
| 19 | O1 | 8101221-V01 | 进水胶管护套 | Bushing, water inlet hose | 1 |  | C | standard |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY ELECTRICAL-Switch unit, A/c & heater | SECTION. NO.:05-8112 | PAGE:121 |
| --- | --- | --- |
| BODY ELECTRICAL- Switch unit, A/c & heater | SECTION. NO-05-8112 | PAGE:122 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 8112016-2E2 | 暖风旋钮 | Knob-Heater motor assembly | 2 |  | C | standard |  |
| 2 | O1 | 8112017-2E2 | 伞齿轮 | Gear,Knob-Heater motor assembly | 2 |  | C | standard |  |
| 3 | O1 | 8112018-2E2 | 轴 | Axes,Knob-Heater motor assembly | 2 |  | C | standard |  |
| 4 | O1 | 8112019-2E2 | 风速开关总成 | Switch assy,wind speed,heater | 1 |  | C | standard |  |
| 5 | O1 | 8112021-2E2 | 内外气杠杆 | Lever,heater cable | 1 |  | C | standard |  |
| 6 | O1 | 8112022-2E2 | 钮套 | Knob cover,Knob-Heater motor assembly | 3 |  | C | standard |  |
| 7 | O1 | 8112023-2E2 | 灯泡 | Bulb,Knob-Heater motor assembly | 2 |  | C | standard |  |
| 8 | O1 | 8112024-2E2 | 内外气钮 | Knob,Knob-Heater motor assembly | 1 |  | C | standard |  |
| 9 | O1 | 8112026-2E2 | 开关旋钮 | Switch knob,Knob-Heater motor assembly | 1 |  | C | standard |  |
| 10 | O1 | 8112027-2E2 | 控制器座 | Control seat,Knob-Heater motor assembly | 1 |  | C | standard |  |
| 11 | O1 | 8112028-2E2 | 内外气导光板 | Plate,Knob-Heater motor assembly | 1 |  | C | standard |  |
| 12 | O1 | 3745010-2E2 | AC开关总成 | A/C switch assy | 1 |  | C | for cooler |  |
|  | O2 | 8112036-2E2 | A/C假钮 | Switch ,heater | 1 |  | C | standard |  |
| 13 | O1 | 8112010-2E2 | 控制器面板 | Pannel, heater | 1 |  | C | standard |  |
| 14 | O1 |  | 拉线 | Cable, heater | 1 |  | C | standard |  |
| 15 | O1 |  | 拉线 | Cable, heater | 1 |  | C | standard |  |
| 16 | O1 |  | 拉线 | Cable, heater | 1 |  | C | standard |  |
| 17 | 01 | 8112010-2E2 | 操纵机构 | A/C or Heater control panel | 1 |  | C | standard |  |
| 18 | 01 | 8112901-2E2 | 操纵机构总成和电器开关 | A/C or Heater control panel with switch assy | 1 | Механизм управления отопителем | C | With a/c |  |

｛｛｝｝

| BODY-Instrument Panel, Pad,fitting | SECTION. NO.:06-5310 | PAGE:123 |
| --- | --- | --- |
| BODY-Instrument Panel, Pad,fitting | SECTION. NO-06-5310 | PAGE:124 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 5301310-2E2 | 前围横梁焊接总成 | Front beam welding assy,instrument panel | 1 |  | D |  |  |
| 2 | O1 | Q2204813 | 十字槽盘头自攻螺钉和平垫圈组合件 | Screw | 3 |  | D |  |  |
| 3 | O1 | 5310010-2E2 | 仪表板总成 | Instrument panel assy （4-14） | 1 | Панель приборов (голая) | C |  |  |
| 4 | O1 | 5303010-2E2 | 杂物箱总成 | Glove box assy | 1 | Крышка бардачка | C |  |  |
| 5 | O1 | 5310051-2E2 | 中间装饰罩 | Middle decorating cover,instrument panel | 1 | Накладка центральная панели приборов | C |  |  |
| 6 | O1 | 5310041-2E2 | 仪表装饰罩 | lid- instrument,instrument panel | 1 | Окантовка комбинации приборов | C |  |  |
| 7 | O1 | 5310171-2E2 | 熔断器盖 | Fuse cover | 1 | Крышка передней панели левая нижняя | C |  |  |
| 8 | O1 | 5310173-2E2 | 开关面罩 | Switch cover | 1 |  | C |  |  |
| 9 | O1 | 5310031-2E2 | 仪表板左侧堵盖 | lid-instrument panel,LH | 1 |  | C |  |  |
| 10 | O1 | 5310032-2E2 | 仪表板右侧堵盖 | lid-instrument panel,RH | 1 |  | C |  |  |
| 11 | O1 | 5310020-2E2 | 侧出风口总成 | Grille-side ventilator | 2 | Воздуховод панели приборов правый,левый | C |  |  |
| 12 | O1 | 5310060-2E2 | 中间出风口总成 | Grille-central ventilator | 1 | Воздуховод центральный | C |  |  |
| 13 | O1 | Q2300616 | 十字槽螺钉和垫圈组合件 | Screw | 1 |  | D |  |  |
| 14 | O1 | 5310033-2E2 | 仪表板中堵盖 | middle lid-instrument panel, | 1 |  | C |  |  |
| 15 | O1 | 5310181-2E2 | 收录机托架 | Bracket,radio | 1 |  | D |  |  |
| 16 | O1 | 3722013-2E2 | 保险片插拔器 | Fuse seat | 1 |  | C |  |  |
| 17 | O1 | 8203010-2E2 | 烟灰盒总成 | Front ash tray | 1 | пепельница | C |  |  |
| 18 | O1 | Q2204813 | 自攻钉和垫圈组合件 | Screw-tapping | 1 |  | D |  |  |
| 19 | O1 | Q2300616 | 十字槽盘头螺钉和平垫圈组合件 | Screw-tapping | 2 |  | D |  |  |
| 20 | O1 | Q2300616 | 十字槽盘头螺钉和平垫圈组合件 | Screw-tapping | 3 |  | D |  |  |
| 21 | O1 | 5301420-2E2 | 六角头螺栓和平垫圈组合件 | combined Bolt | 4 |  | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BODY-Vice Instrument Panel | SECTION. NO.:06-5305 | PAGE:125 |
| --- | --- | --- |
| BODY- Vice Instrument Panel | SECTION. NO-06-5305 | PAGE:126 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 5305011-2E2 | 副仪表板 | Vice-Instrument panel | 1 | Консоль передняя (с подстаканником) | C |  |  |
| 2 | O1 | Q2360616 | 十字槽盘头螺钉、弹簧垫圈和平垫圈组合件 | Screw | 2 |  | D |  |  |
| 3 | O1 | CQ2204816（A） | 十字槽盘头凸缘自攻螺钉 | Screw | 2 |  | D |  |  |
| 4 | O1 | 5107240-2E2 | 中盖板装饰罩 | Decorating cover,Vice-Instrument panel | 1 | Консоль рычага КПП | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY-Front Door Panel & fitting | SECTION. NO.:06-6100-1 | PAGE:127 |
| --- | --- | --- |
| BODY- Front Door Panel & fitting | SECTION. NO.:06-6100-1 | PAGE:128 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 6100015C4E2 | 左前车门总成 | Front left door welding assy | 1 | Дверь передняя левая | D | molded inner decoration panel |  |
| 2 | O1 | 6100020C4E2 | 右前车门总成 | Front right door welding assy | 1 | Дверь передняя правая | D | molded inner decoration panel |  |
| 3 | O1 | 6102025C2E2 | 左前门内饰板本体总成 | Front left door inner decoration panel assy | 1 |  | C | molded inner decoration panel |  |
| 4 | O1 | 6102030C2E2 | 右前门内饰板本体总成 | Front right door inner decoration panel assy | 1 |  | C | molded inner decoration panel |  |
| 5 | O1 | 6102061-2E2 | 左前门密封膜 | Left front door sealing film | 1 |  | B | standard |  |
| 6 | O1 | 6102062-2E2 | 右前门密封膜 | Right front door sealing film | 1 |  | B | standard |  |
| 7 | O1 | 6103075-2E2 | 左前门玻璃后导槽总成 | Glass rear rail , left front door | 1 |  | D | standard |  |
| 8 | O1 | 6103080-2E2 | 右前门玻璃后导槽总成 | Glass rear rail , right front door | 1 |  | D | standard |  |
| 9 | O1 | Q1800612 | 六角法兰面承面带齿螺栓 | Bolt | 2 |  | D | standard |  |
| 10 | O1 | Q2204216 | 十字槽盘头自攻螺钉 | Screw | 2 |  | D | standard |  |
| 11 | O1 | 6102206-V06 | 前门内拉手 | Inside handle assembly, front door | 2 |  | C | standard |  |
| 12 | O1 | 6102106-V06 | 卡扣 | plastic clamp | 12 |  | B | standard |  |
| 13 | O1 | 6107021-2E2 | 左前门密封条 | rubber Sealing strap, left front door | 1 | Уплотнитель передней левой двери | C | standard |  |
| 14 | O1 | 6107022-2E2 | 右前门密封条 | rubber Sealing strap,right front door | 1 | Уплотнитель передней правой двери | C | standard |  |
| 15 | O1 | 6107041-2E2 | 左前门玻璃密封条 | glass run rubber strap,left front door glass | 1 | Утлотнитель проема передней двери????? | C | standard |  |

| BODY-Front Door Panel & fitting | SECTION. NO.:06-6100-2 | PAGE:129 |
| --- | --- | --- |
| BODY- Front Door Panel & fitting | SECTION. NO.:06-6100-2 | PAGE:130 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 16 | O1 | 6107042-2E2 | 右前门玻璃密封条 | glass run rubber strap,right front door glass | 1 | Уплотнитель проема передней двери????? | C | standard |  |
| 17 | O1 | 6107061A2E2 | 左前门玻璃内挡水条 | Inside sealing strap, left front door glass | 1 | Накладка пер двери опускного стекла внутренняя левая(бархотка) | C | standard |  |
| 18 | O1 | 6107062-2E2 | 右前门玻璃内挡水条 | Inside sealing strap, right front door glass | 1 | Накладка пер двери опускного стекла внутренняя правая(бархотка) | C | standard |  |
| 19 | O1 | 6107051-2E2 | 前门玻璃外挡水条 | Outer sealing strap,front door glass | 2 | Накладка передней двери опускного стекла наружняя правая,левая (бархотка) | C | standard |  |
| 20 | O1 | 6107091-2E2 | 前车门上防撞块 | Bump block, front door | 2 |  | C | standard |  |
| 21 | O1 | 6101034-V01 | 塑料螺母 | plastic nut | 6 |  | C | standard |  |
| 22 | O1 | 6107097-2E2 | 前车门线束密封胶堵 | Sealing plug,front door wiring harness | 2 |  | C | standard |  |
| 23 | O1 | 6102041-2E2 | 左前门上内护板 | inner upper cover,left front door | 1 | Заглушка зеркала заднего вида внутренняя левая | C | standard |  |
| 24 | O1 | 6102042-2E2 | 右前门上内护板 | inner upper cover,right front door | 1 | Заглушка зеркала заднего вида внутренняя левая | C | standard |  |
| 25 | O1 | 6102045-2E2 | 左前门内拉手盒支架总成 | Bracket-Inner handle box, left front door | 1 |  | D | standard |  |
| 26 | O1 | 6102050-2E2 | 右前门内拉手盒支架总成 | Bracket-Inner handle box, right front door | 1 |  | D | standard |  |
| 27 | O1 | Q2714816 | 十字槽盘头自攻螺钉 | Screw-tapping | 4 |  | D | standard |  |
| 28 | O1 | 6105158-V06 | 车门自锁手柄套 | Door self-lock handle bushing | 2 |  | C | standard |  |
| 29 | O1 | 5702012AV01 | 卡扣 | Clamp | 4 |  | C | standard |  |
| 30 | O1 | 6107093-2E2 | 前车门缓冲胶垫 | Rubber Cushion,front door | 2 |  | C | standard |  |

| BODY-Front Door Glass Lifter | SECTION. NO.:06-6104 | PAGE:131 |
| --- | --- | --- |
| BODY- Front Door Glass Lifter | SECTION. NO.:06-6104 | PAGE:132 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 6104015-2E2 | 左前门玻璃升降器总成 | Front door glass lifter assembly, manual ,LH | 1 | Стеклоподъемник передний левый | C | standard |  |
| 2 | O1 | 6104020-2E2 | 右前门玻璃升降器总成 | Front door glass lifter assembly,manual, RH | 1 | Стеклоподъемник передний правый | C | standard |  |
| 3 | O1 | 6103015-2E2 | 左前门玻璃总成 | Front left door glass assy | 1 | Обшивка передней двери левая | B | standard |  |
| 4 | O1 | 6103020-2E2 | 右前门玻璃总成 | Front right door glass assy | 1 | Обшивка передней двери правая | B | standard |  |
| 5 | O1 | 6104105-2E2 | 玻璃升降器摇柄总成 | Rock handle assembly, glass lifter,manual | 2 | Ручка стеклоподъемника | B | standard |  |
| 6 | O1 | Q2360610 | 组合螺钉 | Combined bolt | 4 |  | D | standard |  |
| 7 | O1 | Q2360616 | 组合螺钉 | Combined bolt | 8 |  | D | standard |  |
| 8 | O1 | Q2360612 | 组合螺钉 | Combined bolt | 4 |  | D | standard |  |

| BODY-Front door lock | SECTION. NO.:06-6105 | PAGE:133 |
| --- | --- | --- |
| BODY-Front door Lock | SECTION. NO:06-6105 | PAGE:134 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | O1 | 6105015-2E2 | 左前门锁总成 | Front door lock body assembly, L.H. | 1 | Замок передней двер левый | C |  |  |
| 2 | O1 | 6105020-2E2 | 右前门锁总成 | Front door lock body assembly, R.H. | 1 | Замок передней двери правый | C |  |  |
| 3 | O1 | 6105157-V06 | 车门锁止按钮 | Door self lock handle | 2 | Фиксатор замков передних дверей | C |  |  |
| 4 | O1 | 6105050-2E2 | 前车门锁环总成 | Front door lock ring assembly | 2 | Фиксатор передних дверей (на кузове) | D |  |  |
| 5 | O1 | Q2420820 | 组合螺钉 | Combined bolt | 4 |  | D |  |  |
| 6 | O1 | 6105075-2E2 | 左前门内手柄总成 | Inside handle assembly, left front door | 1 |  | C |  |  |
| 7 | O1 | 6105080-2E2 | 右前门内手柄总成 | Inside handle assembly, right front door | 1 |  | C |  |  |
| 8 | O1 | Q2640516 | 十字槽半沉头自攻锁紧螺钉 | Screw-tapping | 2 |  | D |  |  |
| 9 | O1 | 6105405-V01 | 左前车门外抠手总成 | Outside handle assembly, left front door | 1 |  | C |  |  |
| 10 | O1 | 6105410-V01 | 右前车门外抠手总成 | Outside handle assembly, right front door | 1 |  | C |  |  |
| 11 | O1 | Q2420620 | 组合螺钉 | Combined bolt | 6 |  | D |  |  |
| 12 | O1 | 6105215-2E2 | 左前门锁芯总成 | Front door lock core assembly, L.H. | 1 |  | C |  |  |
| 13 | O2 | 6105220-2E2 | 右前门锁芯总成 | Front door lock core assembly , R.H. | 1 |  | C |  |  |
| 14 | O1 | CQ32606 | 六角头锁紧螺母 | Nut | 4 |  | D |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY–Front door gemel | SECTION. NO.:06-6200 | PAGE:135 |
| --- | --- | --- |
| BODY–Front door gemel | SECTION. NO-06-6200 | PAGE:136 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 6106105-2E2 | 前门铰链总成 | front door gemel assembly | 4 | Петля передних дверей верхняя,нижняя | D |  |  |
| 2 |  | Q1400820 | 六角头螺栓和平垫圈组合件 | bolt and flat washer complex | 16 |  | D |  |  |
| 3 |  | 6109010-2E2 | 前门限位器总成 | limit machine,front door | 2 | Ограничитель открывания передних дверей | D |  |  |
| 4 |  | Q1800612 | 六角法兰面承面带齿螺栓 | bolt | 2 |  | D |  |  |
| 5 |  | 6102081-2E2 | 前门铰链加强板工艺孔密封片 | sealing piece,reinforce plate,front door gemel | 4 |  | D |  |  |
| 6 |  | 6109101-2E2 | 开口弹性销 | elastic pin | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY-Rear door | SECTION. NO.:06-6200 | PAGE:137 |
| --- | --- | --- |
| BODY-Rear Door | SECTION. NO.:06-6200 | PAGE:138 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 6200015-4E2 | 左后门总成 | left rear door assembly | 1 | Дверь пассажирская левая | D |  |  |
| 2 |  | 6200020-4E2 | 右后门总成 | right rear door assembly | 1 | Дверь пассажирская правая | D |  |  |
| 3 |  | 6206105-4E2 | 后车门上铰链总成 | up gemel assembly,rear door | 1 |  | D |  |  |
| 4 |  | 6206120-4E2 | 后车门下铰链总成 | bottom gemel assembly,rear door | 1 |  | D |  |  |
| 5 |  | Q1460820 | 六角头组合螺栓 | bolt | 16 |  | D |  |  |
| 6 |  | 6202061-4E2 | 左后门密封膜 | left rear door sealing film | 1 |  | B |  |  |
| 7 |  | 6206062-4E2 | 右后门密封膜 | right rear door sealing film | 1 |  | B |  |  |
| 8 |  | 6202015-4E2 | 左后门内饰板总成 | inner decorating plate ,left rear door | 1 | Обшивка пассажирской левой двери | B |  |  |
| 9 |  | 6202020-4E2 | 右后门内饰板总成 | inner decorating plate ,right rear door | 1 | Обшивка пассажирской левой двери | B |  |  |
| 10 |  | 6102105-V01 | 卡扣 | clamp | 20 |  | B |  |  |
| 11 |  | 6207021-4E2 | 后门门口密封条 | rear door sealing strip | 1 | Уплотнитель пасажирской двери | C |  |  |
| 12 |  | 6102071-2E2 | 前门内拉手 | inner handle,rear door | 2 |  | C |  |  |
| 13 |  | Q2206322 | 组合自攻螺钉 | combined screw | 4 |  | D |  |  |
| 14 |  | 6101034-V01 | 塑料螺母 | plastic nut | 4 |  | C |  |  |
|  |  |  |  |  |  |  |  | 1020vr |  |

| BODY–Rear Door Lifter | SECTION. NO.:06-6203 | PAGE:139 |
| --- | --- | --- |
| BODY - Rear Door Lifter | SECTION. NO:06-6203 | PAGE:140 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 6203015-4E2 | 左后门玻璃总成 | left rear door glass assembly | 1 | Стекло пассажирской двери левое | B |  |  |
| 2 |  | 6203020-4E2 | 右后门玻璃总成 | right rear door glass assembly | 1 | Стекло пассажирской двери правое | B |  |  |
| 3 |  | 6203125-4E2 | 左后门玻璃后导槽总成 | rear rail slot,left rear door glass | 1 |  | D |  |  |
| 4 |  | 6203130-4E2 | 右后门玻璃后导槽总成 | rear rail slot,right rear door glass | 1 |  | D |  |  |
| 5 |  | Q1800612 | 六角法兰面带齿螺栓 | bolt | 8 |  | D |  |  |
| 6 |  | 6203175-4E2 | 左后门玻璃前导槽总成 | front rail slot,left rear door glass | 1 |  | D |  |  |
| 7 |  | 6203180-4E2 | 右后门玻璃前导槽总成 | front rail slot,right rear door glass | 1 |  | D |  |  |
| 8 |  | 6104112-V01 | 摇柄防护罩 | protecting cover,rock handle | 2 |  | C |  |  |
| 9 |  | 6104111-V01 | 摇柄卡黄 | clamp spring ,rock handle assembly | 2 |  | C |  |  |
| 10 |  | 6104105-V01 | 玻璃升降器摇柄总成 | rock handle assembly, glass lifter | 2 |  | C |  |  |
| 11 |  | 6204015-4E2 | 左后门玻璃升降器总成 | rear door glass lifter assembly, LH | 1 | Стеклоподъемник пассажирской двери левый | C |  |  |
| 12 |  | 6204020-4E2 | 右后门玻璃升降器总成 | rear door glass lifter assembly, RH | 1 | Стеклоподъемник пассажирской двери левый | C |  |  |
| 13 |  | Q2360616 | 组合螺钉 | combined screw | 8 |  | D |  |  |
| 14 |  | Q2360616 | 组合螺钉 | combined screw | 4 |  | D |  |  |
| 15 |  | 6203053-4E2 | 后车门玻璃托架夹条 | bracket clamp,rear door glass | 2 |  | B |  |  |
| 16 |  | 6203050-4E2 | 后车门玻璃托架总成 | bracket,rear door glass | 2 |  | D |  |  |
| 17 |  | Q2360612 | 组合螺钉 | combined screw | 4 |  | D |  |  |
| 18 |  | 6207045-4E2 | 左后门玻璃外挡水条 | outlet sealing strip,left rear door glass | 1 | Бархотка пасажирской двери внешняя левая | C |  |  |
| 19 |  | 6207050-4E2 | 右后门玻璃外挡水条 | outlet sealing strip,right rear door glass | 1 | Бархотка пасажирской двери внешняя правая | C |  |  |
| 20 |  | 6207061-4E2 | 后门玻璃内挡水条 | sealing strip,rear door glass | 2 |  | C |  |  |
| 21 |  | 6207041-4E2 | 左后门玻璃密封条 | sealing strip,left rear door glass | 1 | Уплотнитель пассажирской двери левый | C |  |  |
| 22 |  | 6207042-4E2 | 右后门玻璃密封条 | sealing strip,right rear door glass | 1 | Уплотнитель пассажирской двери правывй | C |  |  |
|  |  |  |  |  |  |  |  | 1020vr |  |

| BODY–Rear Door Lock Mechanism | SECTION. NO.:06-6300 | PAGE:141 |
| --- | --- | --- |
| BODY–Rear Door Lock Mechanism | SECTION. NO-06-6300 | PAGE:142 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 6205015-4E2 | 左后门锁总成 | left rear door lock assembly | 1 | Замок пассажирской двери левый | C |  |  |
| 2 |  | 6205020-4E2 | 右后门锁总成 | right rear door lock assembly | 1 | Замок пассажирской двери правый | C |  |  |
| 3 |  | Q2420620 | 组合螺钉 | combined screw | 6 |  | D |  |  |
| 4 |  | 6205075-4E2 | 左后门内手柄总成 | inner handle,left rear door | 1 |  | C |  |  |
| 5 |  | 6205080-4E2 | 右后门内手柄总成 | inner handle,right rear door | 1 |  | C |  |  |
| 6 |  | Q2640516 | 自攻螺钉 | screw | 2 |  | D |  |  |
| 7 |  | 6101034-V01 | 塑料螺母 | plastic nut | 2 |  | C |  |  |
| 8 |  | 6105022-V01 | 缓冲块 | cushion | 4 |  | C |  |  |
| 9 |  | 6205035-4E2 | 左后门锁链锁机构总成 | connecting machine,left rear door lock | 1 |  | C |  |  |
| 10 |  | 6205040-4E2 | 右后门锁链锁机构总成 | connecting machine,right rear door lock | 1 |  | C |  |  |
| 11 |  | Q2140612 | 盘头螺钉 | screw | 4 |  | D |  |  |
| 12 |  | CQ23606 | 锁紧螺母 | lock nut | 4 |  | D |  |  |
| 13 |  | 6105021-2E2 | 车门锁止按钮 | door self-lock handle | 2 |  | C |  |  |
| 14 |  | 6105158-V01 | 车门自锁手柄套 | door self-lock handle bushing | 2 |  | C |  |  |
| 15 |  | 6105050-2E2 | 前门锁环总成 | frong door lock ring | 2 |  | D |  |  |
| 16 |  | 5105051-2E2 | 前门锁环调整片 | adjusting piece,front door lock | 0-4 |  | D |  |  |
| 17 |  | Q2420820 | 组合螺钉 | combined screw | 4 |  | D |  |  |
| 18 |  | 6105405-V01 | 左前门外抠手总成 | outside handle assembly, left front door | 1 |  | C |  |  |
| 19 |  | 6105410-V01 | 右前门外抠手总成 | outside handle assembly, right front door | 1 |  | C |  |  |
| 20 |  | 6105411-V01 | 前车门外扣手连接套 | handle connecting bushing,front door | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  | 1020vr |  |

| BODY –Driver’s Seat | SECTION. NO.:06-6800 | PAGE:147 |
| --- | --- | --- |
| BODY - Driver’s Seat | SECTION. NO.:06-6800 | PAGE:148 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 6800010-2E2 | 驾驶员座椅总成 | driver’s seat assy | 1 |  | C |  |  |
| 1-1 |  | 6804015-2E2 | 左调角器总成 | angle-adjusting assembly,Lh | 1 |  | D |  |  |
| 1-2 |  | 6804210-2E2 | 副滑轨总成 | vice sliding rail driver or passenger seat | 1 |  | D |  |  |
| 1-3 |  | 6804110-2E2 | 主滑轨总成-驾驶员座 | Sliding rail assembly,driver seat | 1 |  | C |  |  |
| 2 |  | Q1460820 | 组合螺栓 | Combined bolt | 4 |  | C |  |  |
| 3 |  | 5107015-2E2 | 发动机左盖板总成 | engine left cover assembly | 1 |  | C |  |  |
| 4 |  | 5107131-2E2 | 发动机左盖板隔热垫 | Heat-insulating lining, engine left cover | 1 |  | D |  |  |
| 5 |  | 5107121-2E2 | 发动机左盖板密封条 | Sealing strap,engine left cover | 1 |  | C |  |  |
| 6 |  | 6900010-2E2 | 前座椅总成 | passenger seat assy | 1 |  | D |  |  |
| 6-1 |  | 6904020-2E2 | 右调角器总成 | angle-adjusting assembly,Rh | 1 |  | C |  |  |
| 6-2 |  | 6904110-2E2 | 主滑轨总成-前座 | Sliding rail assembly,passenger seat | 1 |  | D |  |  |
| 7 |  | 5107020-2E2 | 发动机右盖板总成 | engine right cover assembly | 1 |  | D |  |  |
| 8 |  | 5107132-2E2 | 发动机右盖板隔热垫 | Heat-insulating lining, engine right cover | 1 |  | C |  |  |
| 9 |  | Q32006 | 六角法兰面螺母 | Nut | 4 |  | C |  |  |
| 10 |  | 5107122-2E2 | 发动机右盖板密封条 | Sealing strap,engine right cover | 1 |  | D |  |  |
| 11 |  | 5107190-V01 | 发动机盖板锁扣总成 | Engine cover lock assembly | 4 |  | D |  |  |
| 12 |  | CQ1420616 | 组合螺栓 | Combined bolt | 8 |  | D |  |  |
| 13 |  | 8212030-2E2 | 前安全带带扣总成 | Seat belt seat assy, 3 point, front seat | 2 |  | D |  |  |
| 14 |  | 6800901-2E2 | 驾驶员座椅与发动机左盖板合件 | driver’s seat with engine cover assy | 1 |  | D |  |  |
| 15 |  | 6900901-2E2 | 前座椅与发动机右盖板合件 | passenger seat with enine cover assy | 1 |  | D |  |  |
|  |  |  |  |  |  |  |  | 6371 |  |

| BODY –Rear Seat | SECTION. NO.:06-7200 | PAGE:149 |
| --- | --- | --- |
| BODY - Rear Seat | SECTION. NO.:06-7000 | PAGE:150 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | Q2300616 | 螺钉 | screw | 4 |  | C |  |  |
| 2 |  | 7008010-4E2 | 后座头枕总称 | pillow,rear seat | 2 |  | C |  |  |
| 3 |  | 7000010-4E2 | 后座总成 | rear seat assembly | 1 |  | D |  |  |
| 4 |  | Q1460820 | 组合螺钉 | combined screw | 4 |  | C |  |  |
|  |  |  |  |  |  |  |  | 1020vr |  |

| BODY –Driver seat belt | SECTION. NO.:06-8212 | PAGE:151 |
| --- | --- | --- |
| BODY - Driver seat belt | SECTION. NO.:06-8212 | PAGE:152 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 8212015-2E2 | 左前安全带总成 | Front Seat belt, L.H. | 1 |  | C |  |  |
| 2 |  | 8212020-2E2 | 右前安全带总成 | Front Seat belt, R.H. | 1 |  | C |  |  |
| 3 |  | Q2204816 | 组合自攻螺钉 | Combined screw | 2 |  | C |  |  |
| 4 |  | Q2140516 | 十字槽盘头螺钉 | Screw | 2 |  | C |  |  |
| 5 |  | 8212030-2E2 | 前安全带带扣总成 | Seat belt seat assy, 3 point, front seat | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY-Front & Rear Bumper | SECTION. NO.:06-2803 | PAGE:153 |
| --- | --- | --- |
| BODY- Front & Rear Bumper | SECTION. NO.:06-2803 | PAGE:154 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2803010-4E2 | 前保险杠总成 | Front bumper | 1 | Бампер передний | B |  |  |
| 2 |  | Q2300620 | 十字槽盘头螺钉和平垫圈组合件 | Combined screw | 12 |  | D |  |  |
| 3 |  | Q340B06 | 1型六角螺母 | Nut | 2 |  | D |  |  |
| 4 |  | Q40306 | 弹簧垫圈 | Washer | 2 |  | C |  |  |
| 5 |  | 8401010-2E2 | 散热器面罩总成 | Cover assy-radiator | 1 | Решетка радиатора | B |  |  |
| 6 |  | Q1460616 | 六角头组合螺栓合件 | Combined bolt | 2 |  | D |  |  |

| BODY–Heat insulating lining, engine house | SECTION. NO.:06-5107 | PAGE:155 |
| --- | --- | --- |
| BODY- Heat insulating lining, engine house | SECTION. NO.:06-5107 | PAGE:156 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5109061-2E2 | 左前内轮罩护板 | protecting plate ,left inner wheeling cover | 1 |  | C |  |  |
| 2 |  | 5109062-2E2 | 右前内轮罩护板 | protecting plate ,right inner wheeling cover | 1 |  | C |  |  |
| 3 |  | 5107631-2E2 | 前地板防震胶板 | shockproof plate,front floor | 2 |  | C |  |  |
| 4 |  | 5107511-2E2 | 发动机仓前隔热垫 | front heat-insulating lining,engine house | 1 |  | C |  |  |
| 5 |  | 5107513-2E2 | 发动机仓左后隔热垫 | rear left heat-insulating lining,engine house | 1 |  | C |  |  |
| 6 |  | 5107514-2E2 | 发动机仓右后隔热垫 | rear right heat-insulating lining,engine house | 1 |  | C |  |  |
| 7 |  | 5109083-V01 | 后地板防震胶板（左 | left shockproof plate ,rear floor | 1 |  | C |  |  |
| 8 |  | 5109084-V01 | 后地板防震胶板（右） | right shockproof plate ,rear floor | 1 |  | C |  |  |
| 9 |  | 5107231-2E2 | 发动机中盖板隔热垫 | heat-insulating lining,engine middle cover | 1 |  | C |  |  |
| 10 |  | 5107221-2E2 | 发动机中盖板前密封条 | front sealing strap,engine middle cover | 1 |  | C |  |  |
| 11 |  | 5107222-2E2 | 发动机中盖板后密封条 | rear sealing strap,engine middle cover | 1 |  | C |  |  |
| 12 |  | 5107331-2E2 | 发动机后盖板隔热垫 | heat-insulating lining,engine rear cover | 1 |  | C |  |  |
| 13 |  | 5107321-2E2 | 发动机后盖板密封条 | rear sealing strap,engine rear cover | 1 |  | C |  |  |
| 14 |  | CQ2204213 | 十字槽盘头自攻螺钉 | screw | 4 |  | D |  |  |
| 15 |  | Q399B03 | 端封式嵌装塑料螺母 | plastic nut | 4 |  | C |  |  |
| 16 |  | 5109091-2E2 | 前地板隔热垫 | heat-insulating lining,front floor | 1 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY –Battery cover | SECTION. NO.:06-5107 | PAGE:157 |
| --- | --- | --- |
| BODY –Battery cover | SECTION. NO.:06-5107 | PAGE:158 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3703021-4E2 | 蓄电池压板 | press plate,battery | 1 | Скоба крепления АКБ | D |  |  |
| 2 |  | Q2360620 | 十字槽盘头螺钉，弹簧垫圈组合件 | screw and spring washer complex | 2 |  | D |  |  |
| 3 |  | 5101432-4E2 | 蓄电池托板 | battery tray | 1 | Площадка АКБ | D |  |  |

| BODY-Carpet | SECTION. NO.:06-5109 | PAGE:159 |
| --- | --- | --- |
| BODY -Carpet | SECTION. NO.:06-5109 | PAGE:160 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 1 | 5109051-2E2 | 前地毯 | front carpet assembly | 1 |  | CA1020 |  |  |
| 2 | O1 | 5109081-2E2 | 左前门口护板 | left front door protecting plate | 1 |  | CA1020 |  |  |
| 3 | O1 | 5109082-2E2 | 右前门口护板 | right front door protecting plate | 1 |  | CA1020 |  |  |
| 4 | O1 | CQ2204213 | 十字槽盘头自攻螺钉+垫圈 | screw and washer complex | 10 |  | CA1020 |  |  |
| 5 | O1 | Q399B03 | 端封式嵌装塑料螺母 | plastic nut | 10 |  | CA1020 |  |  |
| 6 | O1 | 5109211-4E2 | 后地毯 | rear carpet | 1 |  | CA1020VR |  |  |

| BODY - Front windshield | SECTION. NO.:06-5206 | PAGE:161 |
| --- | --- | --- |
| BODY - Front windshield | SECTION. NO.:06-5206 | PAGE:162 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5206013-6J6 | 前风窗玻璃内装饰条 | front windshield inner decorating strap | 1 | Уплотнитель лобового стекла внутренний6350?? | B |  |  |
| 2 |  | 5206012-6J6 | 前风窗玻璃密封条 | front windshield sealing strap | 1 | Стекло лобовое6350??? | C |  |  |
| 3 |  | 5206011-6J6 | 前风窗玻璃 | front windshield | 1 | Уплотнитель лобового стекла внешний | C |  |  |
| 4 |  | 8204010-6J6 | 遮阳板总成 | sunvoir plate assembly | 2 | Козырек солцезащитный правый,левый | D |  |  |
| 5 |  | Q2140512 | 十字槽平圆头螺钉 | screw | 4 |  | B |  |  |
| 6 |  | 3714010-1J0 | 前室内灯总成 | front chamber light assy | 1 | Плафон освещения кабины 1010??? | B |  |  |
| 7 |  | Q2714813 | 十字槽盘头自攻螺钉 | screw | 2 | Зеркало заднего вида (салонное) 1010???? | B |  |  |
| 8 |  | 8201010-6J6 | 内后视镜总成 | inner review mirror assy | 1 |  | B |  |  |
| 8-1 |  | 8201017-V01 | 弹簧 | spring | 1 |  | C |  |  |
| 8-2 |  | 8201018-V01 | 弹簧座 | spring seat | 1 |  | C |  |  |
| 9 |  | Q2714813 | 十字槽盘头自攻螺钉 | screw | 2 |  | B |  |  |
| 10 |  | 8202020-2E2 | 右外后视镜总成 | Outerside mirror,RH | 1 | Зеркало заднего вида правое | C |  |  |
| 11 |  | 8202015-2E2 | 左外后视镜总成 | Outerside mirror,LH | 1 | Зеркало заднего вида левое | C |  |  |

| BODY –Top cover | SECTION. NO.:06-5702 | PAGE:163 |
| --- | --- | --- |
| BODY - Top cover | SECTION. NO.:06-5702 | PAGE:164 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 | 1 | 5701011-3E2 | 顶盖 | top cover | 1 | D |  | 1020v |  |
|  | 2 | 5701011-4E2 | 顶盖 | top cover | 1 | D |  | 1020vr |  |
| 2 | 1 | 5702011-3E2 | 顶盖内饰 | inner decoration,top cover | 1 | D |  | 1020v |  |
|  | 2 | 5702011-4E2 | 顶盖内饰 | inner decoration,top cover | 1 | D |  | 1020vr |  |
| 3 | 1 | 5702021-3E2 | 顶盖内装饰条 | inner decorating strip,top cover | 1 | D |  | 1020v |  |
|  | 2 | 5702021-4E2 | 顶盖内装饰条 | inner decorating strip,top cover | 1 | D |  | 1020vr |  |

| BODY-Rear chassis Frame-1020V | SECTION. NO.:06-2801 | PAGE:165 |
| --- | --- | --- |
| BODY-Rear Chassis Frame-CA1020V | SECTION. NO.:06-2801 | PAGE:166 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801141-3E2 | 左后纵梁-车架 | left rear rail,frame | 1 | D | 1 | CA1020V |  |
| 2 |  | 2801142-3E2 | 右后纵梁-车架 | right rear rail,frame | 1 | D | 2 | CA1020V |  |
| 3 |  | 2801437-4E2 | 货箱支座Ⅳ | seat IV,truck bed | 2 | D | 3 | CA1020V |  |
| 4 |  | 2801097-4E2 | 定位挡板-加强板Ⅱ | position plate,reinforce plate II | 2 | D | 4 | CA1020V |  |
| 5 |  | 2801420-4E2 | 汽油滤支架总成 | bracket,fuel filter | 1 | D | 5 | CA1020V |  |
| 6 |  | 2801265-4E2 | 手制动拉线支架总称-第四 横梁 | bracket,haddle brake cable,fourth cross beam | 2 | D | 6 | CA1020V |  |
| 7 |  | 2801268-4E2 | 消音器前吊架 | front hanging frame,muffle | 1 | D | 7 | CA1020V |  |
| 8 |  | 2801246-4E2 | 第四横梁 | fourth cross beam | 1 | D | 8 | CA1020V |  |
| 9 |  | 2801260-4E2 | 油箱左后吊架总成-第四横梁 | left rear hanger,fuel tank,fourth cross beam | 1 | D | 9 | CA1020V |  |
| 10 |  | 2801168-4E2 | 撑板-板簧前吊架 | supporting plate,front hanger,leaf spring | 2 | D | 10 | CA1020V |  |
| 11 |  | 2801167-4E2 | 板簧前吊架 | front hanger,leaf spring | 2 | D | 11 | CA1020V |  |
| 12 |  | 2801170-4E2 | 减震器支架总成-车架 | bracket,rear shock absorber-frame | 2 | D | 12 | CA1020V |  |
| 13 |  | 2801155-4E2 | 油箱右后吊架总成-车架 | right rear hanger,fuel tank,frame | 1 | D | 13 | CA1020V |  |
| 14 |  | 2801121-4E2 | 货箱支座Ⅰ | seat I,truck bed | 2 | D | 14 | CA1020V |  |
| 15 |  | 2801158-4E2 | 感载比例阀支架 | bracket,loading level valve | 1 | D | 15 | CA1020V |  |
| 16 |  | 2801186-4E2 | 限位支座-车架 | limit bracket,frame | 2 | D | 16 | CA1020V |  |
| 17 |  | 2801187-4E2 | 油管支架 | bracket,brake tube | 1 | D | 17 | CA1020V |  |
| 18 |  | 2801285-4E2 | 左支架总成-备胎 | left bracket,spare tyre | 1 | D | 18 | CA1020V |  |
| 19 |  | 2801290-4E2 | 右支架总成-备胎 | right bracket,spare tyre | 1 | D | 19 | CA1020V |  |
| 20 |  | 2801281-4E2 | 第六横梁 | sixth cross beam | 1 | D | 20 | CA1020V |  |
| 21 |  | 2801206-4E2 | 板簧后吊耳-车架 | rear hanger,leaf spring | 2 | D | 21 | CA1020V |  |
| 22 |  | 2801207-4E2 | 套管-板簧后吊耳总成 | sleeve,rear hanger,leaf spring | 2 | D | 22 | CA1020V |  |
| 23 |  | 2801300-4E2 | 第七横梁焊接总成 | seventh cross beam welding assembly | 1 | D | 23 | CA1020V |  |
| 24 |  | 2801123-4E2 | 货箱支座Ⅲ | seat III,truck bed | 2 | D | 24 | CA1020V |  |

| BODY-Rear chassis Frame-1020VR | SECTION. NO.:06-2801 | PAGE:167 |
| --- | --- | --- |
| BODY-Rear Chassis Frame-CA1020VR | SECTION. NO.:06-2801 | PAGE:168 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801141-4E2 | 左后纵梁-车架 | left rear rail,frame | 1 |  | D | CA1020VR |  |
| 2 |  | 2801142-4E2 | 右后纵梁-车架 | right rear rail,frame | 1 |  | D | CA1020VR |  |
| 3 |  | 2801437-4E2 | 左第三边梁托架 1020V和1020VR名称不一致 | bracket,left third side beam | 1 |  | D | CA1020VR |  |
| 4 |  | 2801438-4E2 | 右第三边梁托架 | bracket,right third side beam | 1 |  | D | CA1020VR |  |
| 5 |  | 2801097-4E2 | 定位挡板-加强板Ⅱ | position plate,reinforce plate II | 2 |  | D | CA1020VR |  |
| 6 |  | 2801420-4E2 | 汽油滤支架总成 | bracket,fuel filter | 1 |  | D | CA1020VR |  |
| 7 |  | 2801265-4E2 | 手制动拉线支架总成-第四 横梁 | bracket,haddle brake cable,fourth cross beam | 2 |  | D | CA1020VR |  |
| 8 |  | 2801268-4E2 | 消音器前吊架 | front hanger,muffle | 1 |  | D | CA1020VR |  |
| 9 |  | 2801246-4E2 | 第四横梁 | fourth cross beam | 1 |  | D | CA1020VR |  |
| 10 |  | 2801260-4E2 | 油箱左后吊架总成-第四横梁 | left rear hanger,fuel tank,fourth cross beam | 1 |  | D | CA1020VR |  |
| 11 |  | 2801168-4E2 | 撑板-板簧前吊架 | supporting plate,front hanger,leaf spring | 2 |  | D | CA1020VR |  |
| 12 |  | 2801167-4E2 | 板簧前吊架 | front hanger,leaf spring | 2 |  | D | CA1020VR |  |
| 13 |  | 2801171-4E2 | 支架杆-减震器支架 | supporting pole,rear shock absorber supporting bracket | 2 |  | D | CA1020VR |  |
| 14 |  | 2801172-4E2 | 支架板-减震器支架 | supporting plate,rear shock absorber supporting bracket | 2 |  | D | CA1020VR |  |
| 15 |  | 2801155-4E2 | 油箱右后吊架总成-车架 | right rear hanger,fuel tank,frame | 1 |  | D | CA1020VR |  |
| 16 |  | 2801121-4E2 | 货箱支座Ⅰ | seat I,truck bed | 2 |  | D | CA1020VR |  |
| 17 |  | 2801158-4E2 | 感载比例阀支架 | bracket,loading level valve | 1 |  | D | CA1020VR |  |
| 18 |  | 2801186-4E2 | 限位支座-车架 | limit bracket,frame | 2 |  | D | CA1020VR |  |
| 19 |  | 2801187-4E2 | 油管支架 | bracket,brake tube | 1 |  | D | CA1020VR |  |
| 20 |  | 2801285-4E2 | 左支架总成-备胎 | left bracket,spare tyre | 1 |  | D | CA1020VR |  |
| 21 |  | 2801290-4E2 | 右支架总成-备胎 | right bracket,spare tyre | 1 |  | D | CA1020VR |  |
| 22 |  | 2801281-4E2 | 第六横梁 | sixth cross beam | 1 |  | D | CA1020VR |  |
| 23 |  | 2801206-4E2 | 板簧后吊耳-车架 | rear hanger,leaf spring | 2 |  | D | CA1020VR |  |
| 24 |  | 2801207-4E2 | 套管-板簧后吊耳总成 | sleeve,rear hanger,leaf spring | 2 |  | D | CA1020VR |  |
| 25 |  | 2801122-4E2 | 货箱支座Ⅱ | seat II,truck bed | 2 |  | D | CA1020VR |  |
| 26 |  | 2801281-4E2 | 第六横梁 | sixth cross beam | 1 |  | D | CA1020VR |  |
| 27 |  | 2801311-4E2 | 备胎固定架 | fixed bracket,spare tyre | 1 |  | D | CA1020VR |  |
| 28 |  | 2801123-4E2 | 货箱支座Ⅲ | seat III,truck bed | 2 |  | D | CA1020VR |  |

| BODY-Rear chassis Frame-1020VRL | SECTION. NO.:06-2801 | PAGE:169 |
| --- | --- | --- |
| BODY-Rear Chassis Frame-CA1020VRL | SECTION. NO.:06-2801 | PAGE:170 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801141-3E2 | 左后纵梁-车架 | left rear rail,frame | 1 |  | D | CA1020VRl |  |
| 2 |  | 2801142-3E2 | 右后纵梁-车架 | right rear rail,frame | 1 |  | D | CA1020VRl |  |
| 3 |  | 2801437-4E2 | 左第三边梁托架 | bracket,left third side beam | 1 |  | D | CA1020VRl |  |
| 4 |  | 2801438-4E2 | 右第三边梁托架 | bracket,right third side beam | 1 |  | D | CA1020VRl |  |
| 5 |  | 2801097-4E2 | 定位挡板-加强板Ⅱ | position plate,reinforce plate II | 2 |  | D | CA1020VRl |  |
| 6 |  | 2801420-4E2 | 汽油滤支架总成 | bracket,fuel filter | 1 |  | D | CA1020VRl |  |
| 7 |  | 2801265-4E2 | 手制动拉线支架总称-第四横梁 | bracket,haddle brake cable,fourth cross beam | 2 |  | D | CA1020VRl |  |
| 8 |  | 2801268-4E2 | 消音器前吊架 | front hanger,muffle | 1 |  | D | CA1020VRl |  |
| 9 |  | 2801246-4E2 | 第四横梁 | fourth cross beam | 1 |  | D | CA1020VRl |  |
| 10 |  | 2801260-4E2 | 油箱左后吊架总成-第四横梁 | left rear hanger,fuel tank,fourth cross beam | 1 |  | D | CA1020VRl |  |
| 11 |  | 2801123-4E3 | 货箱支座Ⅲ | seat III,truck bed | 2 |  | D | CA1020VRl |  |
| 12 |  | 2801167-4E3 | 板簧前吊架 | front hanger,leaf spring | 2 |  | D | CA1020VRl |  |
| 13 |  | 2801170-4E2 | 减震器支架总成-车架 | bracket,rear shock absorber | 2 |  | D | CA1020VRl |  |
| 14 |  | 2801155-4E2 | 油箱右后吊架总成-车架 | right rear hanger,fuel tank,frame | 1 |  | D | CA1020VRl |  |
| 15 |  | 2801121-4E2 | 货箱支座Ⅰ | seat I,truck bed | 2 |  | D | CA1020VRl |  |
| 16 |  | 2801158-4E2 | 感载比例阀支架 | bracket,loading level valve | 1 |  | D | CA1020VRl |  |
| 17 |  | 2801186-4E3 | 限位支座-车架 | limit bracket,frame | 2 |  | D | CA1020VRl |  |
| 18 |  | 2801187-4E2 | 油管支架 | bracket,brake tube | 1 |  | D | CA1020VRl |  |
| 19 |  | 2801285-4E3 | 左支架总成-备胎 | left bracket,spare tyre | 1 |  | D | CA1020VRl |  |
| 20 |  | 2801290-4E3 | 右支架总成-备胎 | right bracket,spare tyre | 1 |  | D | CA1020VRl |  |
| 21 |  | 2801281-4E2 | 第六横梁 | sixth cross beam | 1 |  | D | CA1020VRl |  |
| 22 |  | 2801205-4E2 | 板簧后吊耳总成-车架 | rear hanger,leaf spring | 2 |  | D | CA1020VRl |  |
| 23 |  | 2801122-4E3 | 货箱支座Ⅱ | seat II,truck bed | 2 |  | D | CA1020VRl |  |
| 24 |  | 2801281-4E2 | 第六横梁 | sixth cross beam | 1 |  | D | CA1020VRl |  |
| 25 |  | 2801311-4E2 | 备胎固定架 | fixed bracket,spare tyre | 1 |  | D | CA1020VRl |  |
| 26 |  | 2801716-4E3 | 后纵梁Ⅱ | rear rail II | 2 |  | D | CA1020VRl |  |

| BODY-Front chassis Frame | SECTION. NO.:06-2801 | PAGE:171 |
| --- | --- | --- |
| BODY-Front Chassis Frame | SECTION. NO.:06-2801 | PAGE:172 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801016-2E2 | 前横梁-车架 | front cross beam,frame | 1 |  | D |  |  |
| 2 |  | 2801096-2E2 | 定位挡板-加强板I | limit plate,reinforce plate I | 2 |  | D |  |  |
| 3 |  | 2806011-2E2 | 前拖钩 | front drag hook | 1 |  | D |  |  |
| 4 |  | 2801063-4E2 | 左前纵梁-车架 | front left rail-frame | 1 |  | D |  |  |
| 5 |  | 2801064-4E2 | 右前纵梁-车架 | front right rail-frame | 1 |  | D |  |  |
| 6 |  | 2801018-2E2 | 散热器支架 | bracket-radiator | 2 |  | D |  |  |
| 7 |  | 2801351-2E2 | 横梁本体 | cross beam | 1 |  | D |  |  |
| 8 |  | 2801077-2E2 | 前悬置螺母板-左前纵梁 | nut plate-front mounting-front left side rail | 1 |  | D |  |  |
| 9 |  | 2801078-2E2 | 前悬置螺母板-右前纵梁 | nut plate-front mounting-front right side rail | 1 |  | D |  |  |
| 10 |  | 2801361-2E2 | 左稳定拉杆固定板 | fixed plate-left stable pulling rod | 1 |  | D |  |  |
| 11 |  | 2801362-2E2 | 右稳定拉杆固定板 | fixed plate-right stable pulling rod | 1 |  | D |  |  |
| 12 |  | 2801375-2E2 | 加强板焊接总成-左稳定拉杆固定板 | reinforce plate welding assembly,fixed plate,left pulling pole | 1 |  | D |  |  |
| 13 |  | 2801380-2E2 | 加强板焊接总成-右稳定拉杆固定板 | reinforce plate welding assembly,fixed plate,right pulling pole | 1 |  | D |  |  |
| 14 |  | 2801067-2E2 | 吊装左支架 | bracket,Lh | 1 |  | D |  |  |
| 15 |  | 2801068-2E2 | 吊装右支架 | bracket,Rh | 1 |  | D |  |  |
| 16 |  | 2801071-2E2 | 左纵梁侧加强件 | reinforce unit-left side rail | 1 |  | D |  |  |
| 17 |  | 2801072-2E2 | 右纵梁侧加强件 | reinforce unit-right side rail | 1 |  | D |  |  |
| 18 |  | 2801386-2E2 | 组合水管支架 | combined water hose bracket | 2 |  | D |  |  |
| 19 |  | 2801081-4E2 | 发动机悬置螺母板-左前纵梁 | nut plate-engine mounting -front left side rail | 1 |  | D |  |  |
| 20 |  | 2801082-4E2 | 发动机悬置螺母板-右前纵梁 | nut plate-engine mounting -front right side rail | 1 |  | D |  |  |

| BODY-Middle chassis Frame-CA1020V | SECTION. NO.:06-2801 | PAGE:173 |
| --- | --- | --- |
| BODY-Middle Chassis Frame-CA1020V | SECTION. NO.:06-2801 | PAGE:174 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801117-4E2 | 左中纵梁-车架 | left middle rail,frame | 1 |  | D | CA1020V |  |
| 2 |  | 2801118-4E2 | 右中纵梁-车架 | right middle rail,frame | 2 |  | D | CA1020V |  |
| 3 |  | 2801411-4E2 | 左第二边梁托架 | supporting bracket,left second side beam | 1 |  | D | CA1020V |  |
| 4 |  | 2801410-4E2 | 右第二边梁托架总成 | supporting bracket,right second side beam | 1 |  | D | CA1020V |  |
| 5 |  | 2801210-4E2 | 第一横梁总成 | first cross beam assembly | 1 |  | D | CA1020V |  |
| 6 |  | 2801481-4E2 | 第二横梁 | second cross beam assembly | 1 |  | D | CA1020V |  |
| 7 |  | 2801225-4E2 | 变速箱吊架总成-第二横梁 | hanger,transmission-second cross beam | 1 |  | D | CA1020V |  |
| 8 |  | 2801263-4E2 | 手制动拉线支架-第三横梁 | bracket,hand brake cable-third cross beam | 1 |  | D | CA1020V |  |
| 9 |  | 2801221-4E2 | 第三横梁 | third cross beam | 1 |  | D | CA1020V |  |
| 10 |  | 2801230-4E2 | 左前油箱吊架总成 | left front hanger,fuel tank | 1 |  | D | CA1020V |  |
| 11 |  | 2801150-3E2 | 油箱右前吊架总成-车架 | right front hanger,fuel tank | 1 |  | D | CA1020V |  |
| 12 |  | 2801621-3E2 | 前连接板-蓄电池托架 | front contecting plate,battery tray | 1 |  | D | CA1020V |  |
| 13 |  | 2801622-3E2 | 后连接板-蓄电池托架 | rear contecting plate,battery tray | 1 |  | D | CA1020V |  |
| 14 |  | 2801625-3E2 | 蓄电池底板总成 | bottom plate,battery | 1 |  | D | CA1020V |  |

| BODY-Middle chassis Frame-CA1020VR | SECTION. NO.:06-2801 | PAGE:175 |
| --- | --- | --- |
| BODY-Middle Chassis Frame-CA1020VR | SECTION. NO.:06-2801 | PAGE:176 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801117-4E2 | 左中纵梁-车架 | left middle rail,frame | 1 |  | D | CA1020VR(L) |  |
| 2 |  | 2801118-4E2 | 右中纵梁-车架 | right middle rail,frame | 2 |  | D | CA1020VR(L) |  |
| 3 |  | 2801411-4E2 | 左第二边梁托架 | supporting bracket,left second side beam | 1 |  | D | CA1020VR(L) |  |
| 4 |  | 2801410-4E2 | 右第二边梁托架总称 | supporting bracket,right second side beam | 1 |  | D | CA1020VR(L) |  |
| 5 |  | 2801210-4E2 | 第一横梁总称 | first cross beam assembly | 1 |  | D | CA1020VR(L) |  |
| 6 |  | 2801481-4E2 | 第二横梁 | second cross beam assembly | 1 |  | D | CA1020VR(L) |  |
| 7 |  | 2801225-4E2 | 变速箱吊架总称-第二横梁 | hanger,transmission-second cross beam | 2 |  | D | CA1020VR(L) |  |
| 8 |  | 2801263-4E2 | 手制动拉线支架-第三横梁 | bracket,hand brake cable-third cross beam | 1 |  | D | CA1020VR(L) |  |
| 9 |  | 2801221-4E2 | 第三横梁 | third cross beam | 1 |  | D | CA1020VR(L) |  |
| 10 |  | 2801230-4E2 | 左前油箱吊架总成 | left front hanger,fuel tank | 1 |  | D | CA1020VR(L) |  |
| 11 |  | 2801150-4E2 | 油箱右前吊架总成-车架 | right front hangert,fuel tank | 1 |  | D | CA1020VR(L) |  |

| BODY- Cover-Frame-CA1020V | SECTION. NO.:06-2801 | PAGE:177 |
| --- | --- | --- |
| BODY- Cover-Frame-CA1020V | SECTION. NO.:06-2801 | PAGE:178 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801455-2E2 | 前盖板总成-左前纵梁 | front cover assembly,left front rail | 1 |  | D | CA1020V |  |
| 2 |  | 2801460-2E2 | 前盖板总成-右前纵梁 | front cover assembly,right front rail | 1 |  | D | CA1020V |  |
| 3 |  | 2801073-2E2 | 加强板Ⅰ | reinforce plate I | 2 |  | D | CA1020V |  |
| 4 |  | 2801107-4E2 | 加强板Ⅱ-左纵梁 | reinforce plate Ⅱ,left rail beam | 1 |  | D | CA1020V |  |
| 5 |  | 2801108-4E2 | 加强板Ⅱ-右纵梁 | reinforce plate Ⅱ,right rail beam | 1 |  | D | CA1020V |  |
| 6 |  | 2801515-2E2 | 后盖板总成-左前纵梁 | rear cover assembly,left front rail | 1 |  | D | CA1020V |  |
| 7 |  | 2801520-2E2 | 后盖板总成-右前纵梁 | rear cover assembly,right front rail | 1 |  | D | CA1020V |  |
| 8 |  | 2801541-4E2 | 加强板Ⅲ-左纵梁 | reinforce plate Ⅲ,left rail beam | 1 |  | D | CA1020V |  |
| 9 |  | 2801541-4E2 | 加强板Ⅲ-右纵梁 | reinforce plate Ⅲ,right rail beam | 1 |  | D | CA1020V |  |
| 10 |  | 2801127-3E2 | 后围板支座 | seat,rear plate | 2 |  | D | CA1020V |  |
| 11 |  | 2801235-3E2 | 后围板支座左加强板总成 | left reinforce plate,rear plate seat | 1 |  | D | CA1020V |  |
| 12 |  | 2801236-3E2 | 后围板支座右加强板总成 | right reinforce plate,rear plate seat | 1 |  | D | CA1020V |  |
| 13 |  | 2801611-3E2 | 左中盖板-纵梁 | left middle cover,rail | 1 |  | D | CA1020V |  |
| 14 |  | 2801612-3E2 | 右中盖板-纵梁 | right middle cover,rail | 1 |  | D | CA1020V |  |
| 15 |  | 2801271-4E2 | 第五横梁 | fifth rail beam | 1 |  | D | CA1020V |  |
| 16 |  | 2801273-4E2 | 消音器中吊架 | middle hanger,muffle | 1 |  | D | CA1020V |  |
| 17 |  | 2801175-3E2 | 盖板总成-左后纵梁 | cover assembly,left rear rail | 1 |  | D | CA1020V |  |
| 18 |  | 2801176-3E2 | 盖板总成-右后纵梁 | cover assembly,right rear rail | 1 |  | D | CA1020V |  |

| BODY- Cover-Frame-CA1020VR(L) | SECTION. NO.:06-2801 | PAGE:179 |
| --- | --- | --- |
| BODY- Cover-Frame-CA1020VR(L) | SECTION. NO.:06-2801 | PAGE:180 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 2801455-2E2 | 前盖板总成-左前纵梁 | front cover,left front rail | 1 |  | D | CA1020VR(L) |  |
| 2 |  | 2801460-2E2 | 前盖板总成-右前纵梁 | front cover,right front rail | 1 |  | D | CA1020VR(L) |  |
| 3 |  | 2801073-2E2 | 加强板Ⅰ | reinforce plate Ⅰ | 2 |  | D | CA1020VR(L) |  |
| 4 |  | 2801177-4E2 | 消音器后吊架 | rear hanger,muffle | 1 |  | D | CA1020VR(L) |  |
| 5 |  | 2801107-4E2 | 加强板Ⅱ-左纵梁 | reinforce plate Ⅱ,left rail | 1 |  | D | CA1020VR(L) |  |
| 6 |  | 2801108-4E2 | 加强板Ⅱ-右纵梁 | reinforce plate Ⅱ,right rail | 1 |  | D | CA1020VR(L) |  |
| 7 |  | 2801515-2E2 | 后盖板总成-左前纵梁 | rear cover assembly,left front rail | 1 |  | D | CA1020VR(L) |  |
| 8 |  | 2801520-2E2 | 后盖板总成-右前纵梁 | rear cover assembly,right front rail | 1 |  | D | CA1020VR(L) |  |
| 9 |  | 2801541-4E2 | 加强板Ⅲ-左纵梁 | reinforce plate Ⅲ,left rail | 1 |  | D | CA1020VR(L) |  |
| 10 |  | 2801541-4E2 | 加强板Ⅲ-右纵梁 | reinforce plate Ⅲ,right rail | 1 |  | D | CA1020VR(L) |  |
| 11 |  | 2801127-4E2 | 左后围板支座Ⅰ | seat I,left rear plate | 1 |  | D | CA1020VR(L) |  |
| 12 |  | 2801128-4E2 | 右后围板支座Ⅰ | seat I,right rear plate | 1 |  | D | CA1020VR(L) |  |
| 13 |  | 2801131-4E2 | 左后围板支座Ⅱ | seat II,left rear plate | 1 |  | D | CA1020VR(L) |  |
| 14 |  | 2801132-4E2 | 右后围板支座Ⅱ | seat II,right rear plate | 1 |  | D | CA1020VR(L) |  |
| 15 |  | 2801136-4E2 | 支座内连接板 | inner contecting plate,seat | 2 |  | D | CA1020VR(L) |  |
| 16 |  | 2801137-4E2 | 支座外连接板 | outlet contecting plate,seat | 2 |  | D | CA1020VR(L) |  |
| 17 |  | 2801270-4E2 | 第五横梁焊接总成 | fifth beam welding assembly | 1 |  | D | CA1020VR(L) |  |
| 18 |  | 2801176-4E2 | 盖板总成-左后纵梁 | cover assembly, left rear rail | 2 |  | D | CA1020VR(L) |  |

| BODY- Rear welding floor –Frame-CA1020V | SECTION. NO.:06-5101 | PAGE:181 |
| --- | --- | --- |
| BODY-Rear welding floor –Frame-CA1020V | SECTION. NO.:06-5101 | PAGE:182 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5101250-3E2 | 后地板下加强梁分总成 | reinforce beam,rear floor | 1 |  | D | CA1020V |  |
| 2 |  | 5101310-3E2 | 后地板分总成 | rear floor assembly | 1 |  | D | CA1020V |  |
| 3 |  | 5101331-3E2 | 地板左裙板 | left apron plate,floor | 1 |  | D | CA1020V |  |
| 4 |  | 5101332-3E2 | 地板右裙板 | right apron plate,floor | 1 |  | D | CA1020V |  |
| 5 |  | 5101355-3E2 | 左安全带下固定点加强板总成 | reinforce plate,left seat belt | 1 |  | D | CA1020V |  |
| 6 |  | 5101360-3E2 | 右安全带下固定点加强板总成 | reinforce plate,right seat belt | 1 |  | D | CA1020V |  |

| BODY- Rear welding floor –Frame-CA1020VR(L) | SECTION. NO.:06-5101 | PAGE:183 |
| --- | --- | --- |
| BODY-Rear welding floor –Frame-CA1020VR(L) | SECTION. NO.:06-5101 | PAGE:184 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5101512-4E2 | 地板左后裙板 | left apron plate,floor | 1 |  | D | CA1020VR(L) |  |
| 2 |  | 5101431-4E2 | 后地板 | rear floor | 1 |  | D | CA1020VR(L) |  |
| 3 |  | 5101432-4E2 | 蓄电池托板 | supporting plate,battery | 1 |  | D | CA1020VR(L) |  |
| 4 |  | 5101522-4E2 | 地板右后裙板 | right apron plate,floor | 1 |  | D | CA1020VR(L) |  |
| 5 |  | 5101421-4E2 | 左后门槛内板 | inner plate,left rear doorsill | 1 |  | D | CA1020VR(L) |  |
| 6 |  | 5101630-4E2 | 后座椅加强板总成 | reinforce plate,rear seat | 4 |  | D | CA1020VR(L) |  |
| 7 |  | 5107294-4E2 | 地板胶堵-下滑道用 | floor glue plug | 2 |  | C | CA1020VR(L) |  |
| 8 |  | N 011 094 4 | 螺母 | nut | 2 |  | C | CA1020VR(L) |  |
| 9 |  | Q36405 | 焊接方形螺母 | nut | 2 |  | C | CA1020VR(L) |  |
| 10 |  | 5101361-4E2 | 左侧安全带螺母板 | nut plate,left seat belt | 1 |  | D | CA1020VR(L) |  |
| 11 |  | 5101361-4E2 | 右侧安全带螺母板 | nut plate,right seat belt | 1 |  | D | CA1020VR(L) |  |
| 12 |  | 5101250-2E2 | 后地板前板总成 | front plate,rear floor | 1 |  | D | CA1020VR(L) |  |
| 13 |  | 5101255-2E2 | 后地板前板加强梁总成 | front plate reinforce beam,rear floor | 1 |  | D | CA1020VR(L) |  |
| 14 |  | 5101315-4E2 | 左中立柱下内板总成 | lower inner plate,left middle pillar | 1 |  | D | CA1020VR(L) |  |
| 15 |  | 5101315-4E2 | 右中立柱下内板总成 | lower inner plate,right middle pillar | 1 |  | D | CA1020VR(L) |  |
| 16 |  | 5101422-4E2 | 右后门槛内板 | inner plate,right rear doorsill | 1 |  | D | CA1020VR(L) |  |

| BODY- Front welded panel parts-Frame | SECTION. NO.:06-5301 | PAGE:185 |
| --- | --- | --- |
| BODY- Front welded panel parts-Frame | SECTION. NO.:06-5301 | PAGE:186 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5701020-V01 | 顶盖前横梁总成 | Beam, cab cover | 1 |  | D |  |  |
| 2 |  | 5702051-V06 | 顶盖前横梁护板 | Protecting panel,cab cover beam | 1 |  | D |  |  |
| 3 |  | 5401210-2E2 | 右前立柱上内板总成 | Welded inner plate assembly,RH | 1 |  | D |  |  |
| 4 |  | 5401205-2E2 | 左前立柱上内板总成 | Welded inner plate assembly,LH | 1 |  | D |  |  |
| 5 |  | 5301031-2E2 | 前风窗下板 | Outer plate, under window | 1 |  | D |  |  |
| 6 |  | 8402147-2E2 | 前盖板撑杆 | Front cover supporting bar | 1 |  | D |  |  |
| 7 |  | 5301040-2E2 | 前壁板分总成 | Front wainscot welded assy | 1 |  | D |  |  |
|  |  | 5301105-2E2 | 刮水器电机支架总成 | Bracket,wiper motor | 1 |  | D |  |  |
|  |  | 5301111-2E2 | 刮水器连杆中支架 | Middle bracket ,connecting rod assembly | 1 |  | D |  |  |
|  |  | 5301115-2E2 | 刮水器连杆侧支架总成 | Side bracket ,connecting rod assembly | 1 |  | D |  |  |
|  |  | 5301120-2E2 | 洗涤器水盒支架总成 | Bracket,washer box | 2 |  | D |  |  |
| 8 |  | 5301180-2E2 | 右侧壁板焊接总成 | Right side wainscot welded assy | 1 | Усилитель переднего крыла правый | D |  |  |
| 9 |  | 5301175-2E2 | 左侧壁板焊接总成 | Left side wainscot welded assy | 1 | Усилитель переднего крыла левый | D |  |  |
| 10 |  | 5301242-2E2 | 右侧壁板连接板 | connect plate, Right side wainscot welded assy | 1 |  | D |  |  |
| 11 |  | 5301241-2E2 | 左侧壁板连接板 | connect plate, Left side wainscot welded assy | 1 |  | D |  |  |
| 12 |  | 8400015-2E2 | 前支撑梁焊接总成 | Front supporting beam welding assy | 1 |  | D |  |  |
| 13 |  | 8402155-2E2 | 盖板锁拉线总成 | Cable assy,front cover lock | 1 |  | C |  |  |
| 14 |  | Q174B0616 | 六角头部带十字槽螺栓 | Bolt | 2 |  | D |  |  |
| 15 |  | 8400081-2E2 | 前大灯支架下连接板 | Connection plate,head lamp bracket | 1 |  | D |  |  |
| 16 |  | 8400050-2E2 | 右前大灯支架焊接总成 | Bracket,right head lamp | 1 |  | D |  |  |
| 17 |  | 8400045-2E2 | 左前大灯支架焊接总成 | Bracket,left head lamp | 1 |  | D |  |  |
| 18 |  | 8402210-2E2 | 锁体总成 | Lock body assy | 1 |  | C |  |  |
| 19 |  | Q1460616 | 六角头螺栓组合件 | Combined bolt | 2 |  | D |  |  |
| 20 |  | 8403031-2E2 | 左前翼子板 | Left Welded Fender Plate | 1 | Крыло переднее левое | C |  |  |
| 21 |  | 8403032-2E2 | 右前翼子板 | Right Welded Fender Plate | 1 | Крыло переднее правое | C |  |  |
| 22 |  | 8402085-2E2 | 前盖板左铰链总成 | Left Hinge Assy.,Front Cover Plate | 1 |  | D |  |  |
| 23 |  | 8402090-2E2 | 前盖板右铰链总成 | Right Hinge Assy.,Front Cover Plate | 1 |  | D |  |  |
| 24 |  | 8402010-2E2 | 前盖板总成 | Front Cover Plate Assy(Hood) | 1 | капот | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY- Side panel welded parts | SECTION. NO.:06-5401-1 | PAGE:187 |
| --- | --- | --- |
| BODY- Side panel welded parts | SECTION. NO:06-5401-1 | PAGE:188 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5401031-4E2 | 左流水槽 | Left Water Slot | 1 |  | D | CA1020V |  |
| 2 |  | 5401032-4E2 | 右流水槽 | Right Water Slot | 1 |  | D | CA1020V |  |
| 3 |  | 5401061-4E2 | 左前立柱外板 | Outlet Plate,Left Front Pillar | 1 |  | D | CA1020V |  |
| 4 |  | 5401062-4E2 | 右前立柱外板 | Outlet Plate,Right Front Pillar | 1 |  | D | CA1020V |  |
| 5 |  | 5401063-2E2 | 左侧壁板加强板 | Reinforce Plate,Left Side Wainscot | 1 |  | D | CA1020V |  |
| 6 |  | 5401064-2E2 | 右侧壁板加强板 | Reinforce Plate,Right Side Wainscot | 1 |  | D | CA1020V |  |
| 7 |  | 5401066-2E2 | 天线螺母板 | Nut Plate,Antenna | 1 |  | D | CA1020V |  |
| 8 |  | 5401075-2E2 | 翼子板支架Ⅰ总成 | BracketⅠ-Welded Fender Plate | 2 |  | D | CA1020V |  |
| 9 |  | 5401080-2E2 | 翼子板支架Ⅱ总成 | Bracket Ⅱ-Welded Fender Plate | 2 |  | D | CA1020V |  |
| 10 |  | 5401101-2E2 | 左前立柱下加强板 | Lower Reinforce Plate,Front Pillar,Lh | 1 |  | D | CA1020V |  |
| 11 |  | 5401102-2E2 | 右前立柱下加强板 | Lower Reinforce Plate,Front Pillar,Rh | 1 |  | D | CA1020V |  |
| 12 |  | 5401103-2E2 | 仪表板横梁固定支架 | Positioning Bracket,Instrument Panel Beam | 2 |  | D | CA1020V |  |
| 13 |  | 5401111-2E2 | 前门限位支架 | Position Fixing Bracket,Front Door,Lh | 2 |  | D | CA1020V |  |
| 14 |  | 5401113-2E2 | 左前门限位支架加强板 | Reinforce Plate-Position Fixing Bracket, Front Door,Lh | 1 |  | D | CA1020V |  |
| 15 |  | 5401114-2E2 | 右前门限位支架加强板 | Reinforce Plate-Position Fixing Bracket, Front Door,Rh | 1 |  | D | CA1020V |  |
| 16 |  | 5401121-3E2 | 左后立柱外板 | Outlet Plate,Left Rear Pillar | 1 | Проем передней двери левый | D | CA1020V |  |
| 17 |  | 5401122-3E2 | 右后立柱外板 | Outlet Plate,Right Rear Pillar | 1 | Проем передней двери правый | D | CA1020V |  |
| 18 |  | 5401136-2E2 | 前门锁环螺母板 | Nut Plate,Front Door Lock Ring | 2 |  | D | CA1020V |  |
| 19 |  | 5401137-2E2 | 前门锁环螺母板盒 | Nut Plate Box,Front Door Lock Ring | 2 |  | D | CA1020V |  |
| 20 |  | 5401141-3E2 | 左前门锁环加强板 | Reinforce Plate,Left Front Door Lock Ring | 1 |  | D | CA1020V |  |

| BODY- Side panel welded parts | SECTION. NO:06-5401-2 | PAGE:189 |
| --- | --- | --- |
| BODY- Side panel welded parts | SECTION. NO:06-5401-2 | PAGE:190 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 21 |  | 5401142-3E2 | 右前门锁环加强板 | Reinforce Plate,Right Front Door Lock Ring | 1 |  | D | CA1020V |  |
| 22 |  | 5401143-V01 | 限位胶块 | Limit Rubber Block | 2 |  | C | CA1020V |  |
| 23 |  | 5401146-2E2 | 加油孔外座 | Outlet Seat,Fuel Filler Neck | 1 |  | D | CA1020V |  |
| 24 |  | 5401150-2E2 | 加油孔盖总成 | Cap,Fuel Filler Neck | 1 |  | D | CA1020V |  |
| 27 |  | 5401267-3E2 | 安全带左上固定点加强板 | Upper Fixing Plate,Left Seat Belt | 1 |  | D | CA1020V |  |
| 28 |  | 5401268-3E2 | 安全带右上固定点加强板 | Upper Fixing Plate,Right Seat Belt | 1 |  | D | CA1020V |  |
| 29 |  | 5401281-3E2 | 安全带左加强板 | Left Reinforce Plate,Seat Belt | 1 |  | D | CA1020V |  |
| 30 |  | 5401282-3E2 | 安全带右加强板 | Right Reinforce Plate,Seat Belt | 1 |  | D | CA1020V |  |
| 31 |  | 5401211-2E2 | 左前立柱上内板 | Upper Inner Plate,Left Front Pillar | 1 |  | D | CA1020V |  |
| 32 |  | 5401212-2E2 | 右前立柱上内板 | Upper Inner Plate,Right Front Pillar | 1 |  | D | CA1020V |  |
| 33 |  | 5401221-2E2 | 左前门框上内板 | Upper Inner Plate -Front Door Frame,Lh | 1 |  | D | CA1020V |  |
| 34 |  | 5401222-2E2 | 右前门框上内板 | Upper Inner Plate-Front Door Frame,Rh | 1 |  | D | CA1020V |  |
| 35 |  | 5401241-3E2 | 左后立柱内板 | Inner Plate,Left Rear Pillar | 1 | Накладка задней стойки проема двери левая(V) | D | CA1020V |  |
| 36 |  | 5401242-3E2 | 右后立柱内板 | Inner Plate,Right Rear Pillar | 1 | Накладка задней стойки проема двери правая (V) | D | CA1020V |  |
| 37 |  | 5401305-3E2 | 左边板锁钩加强板总成 | Reinforce Plate,Left Side Plate Lock Hook | 1 |  | D | CA1020V |  |
| 38 |  | 5401310-3E2 | 右边板锁钩加强板总成 | Reinforce Plate,Right Side Plate Lock Hook | 1 |  | D | CA1020V |  |
| 39 |  | 5402011-3E2 | 边板上缓冲块 | Upper Cushion,Side Plate | 2 |  | D | CA1020V |  |
| 40 |  | 5402036-2E2 | 前门框装饰条 | decorating trap,front door frame | 2 |  | C | CA1020V |  |
| 41 |  | 5402046-V01 | 侧围扶手 | Handle Assy(Plastic), Side Plate | 1 |  | D | CA1020V |  |
| 42 |  | 5402049-2E2 | 前车门下防撞块 | Bumper Block,Front Door | 4 |  | C | CA1020V |  |
| 43 |  | 5402057-2E2 | 线束过孔胶堵 | Rubber Plug | 2 |  | C | CA1020V |  |

| BODY- Side panel welded parts | SECTION. NO:06-5401-3 | PAGE:191 |
| --- | --- | --- |
| BODY- Side panel welded parts | SECTION. NO:06-5401-3 | PAGE:192 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5401031-4E2 | 左流水槽 | Left Water Slot | 1 |  | D | CA1020VR |  |
| 2 |  | 5401032-4E2 | 右流水槽 | Right Water Slot | 1 |  | D | CA1020VR |  |
| 3 |  | 5401061-4E2 | 左前立柱外板 | Outlet Plate,Left Front Pillar | 1 |  | D | CA1020VR |  |
| 4 |  | 5401062-4E2 | 右前立柱外板 | Outlet Plate,Right Front Pillar | 1 |  | D | CA1020VR |  |
| 5 |  | 5401063-2E2 | 左侧壁板加强板 | Reinforce Plate,Left Side Wainscot | 1 |  | D | CA1020VR |  |
| 6 |  | 5401064-2E2 | 右侧壁板加强板 | Reinforce Plate,Right Side Wainscot | 1 |  | D | CA1020VR |  |
| 7 |  | 5401066-2E2 | 天线螺母板 | Nut Plate,Antenna | 1 |  | D | CA1020VR |  |
| 8 |  | 5401075-2E2 | 翼子板支架Ⅰ总成 | BracketⅠ-Welded Fender Plate | 2 |  | D | CA1020VR |  |
| 9 |  | 5401080-2E2 | 翼子板支架Ⅱ总成 | Bracket Ⅱ-Welded Fender Plate | 2 |  | D | CA1020VR |  |
| 10 |  | 5401101-2E2 | 左前立柱下加强板 | Lower Reinforce Plate,Front Pillar,Lh | 1 |  | D | CA1020VR |  |
| 11 |  | 5401102-2E2 | 右前立柱下加强板 | Lower Reinforce Plate,Front Pillar,Rh | 1 |  | D | CA1020VR |  |
| 12 |  | 5401103-2E2 | 仪表板横梁固定支架 | Positioning Bracket,Instrument Panel Beam | 2 |  | D | CA1020VR |  |
| 13 |  | 5401111-2E2 | 前门限位支架 | Position Fixing Bracket,Front Door,Lh | 2 |  | D | CA1020VR |  |
| 14 |  | 5401113-2E2 | 左前门限位支架加强板 | Reinforce Plate-Position Fixing Bracket, Front Door,Lh | 1 |  | D | CA1020VR |  |
| 15 |  | 5401114-2E2 | 右前门限位支架加强板 | Reinforce Plate-Position Fixing Bracket, Front Door,Rh | 1 |  | D | CA1020VR |  |
| 16 |  | 5401121-4E2 | 左后门洞外板 | Outlet Plate,Left Rear Door Frame | 1 |  | D | CA1020VR |  |
| 17 |  | 5401122-4E2 | 右后门洞外板 | Outlet Plate,Right Rear Door Frame | 1 |  | D | CA1020VR |  |
| 18 |  | 5401136-2E2 | 前门锁环螺母板 | Nut Plate,Front Door Lock Ring | 4 |  | D | CA1020VR |  |
| 19 |  | 5401137-2E2 | 前门锁环螺母板盒 | Nut Plate Box,Front Door Lock Ring | 4 |  | D | CA1020VR |  |
| 20 |  | 5401141-4E2 | 左中立柱铰链加强板 | Reinforce Plate,Gemel-Left Middle Pillar | 1 |  | D | CA1020VR |  |
| 21 |  | 5401142-4E2 | 右中立柱铰链加强板 | Reinforce Plate,Gemel-Right Middle Pillar | 1 |  | D | CA1020VR |  |
| 22 |  | 5401171-4E2 | 中立柱铰链螺母板 | Nut Plate,Gemel-Middle Pillar | 4 |  | D | CA1020VR |  |
| 23 |  | 5401143-V01 | 限位胶块 | Limit Rubber Block | 2 |  | C | CA1020VR |  |
| 24 |  | 5401146-2E2 | 加油孔外座 | Outlet Seat,Fuel Filler Neck | 1 |  | D | CA1020VR |  |

| BODY- Side panel welded parts | SECTION. NO:06-5401-4 | PAGE:193 |
| --- | --- | --- |
| BODY- Side panel welded parts | SECTION. NO:06-5401-4 | PAGE:194 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 25 |  | 5401150-2E2 | 加油孔盖总成 | Cap,Fuel Filler Neck | 1 |  | D | CA1020VR |  |
| 28 |  | 5401212-V01 | 顶盖加强梁支架 | Bracket,Top Cover Reinforce Beam | 1 |  | D | CA1020VR |  |
| 29 |  | 5401191-4E2 | 左后立柱琐环加强板 | Reinforce Plate,Lock Ring-Left Rear Pillar | 1 |  | D | CA1020VR |  |
| 30 |  | 5401192-4E2 | 右后立柱琐环加强板 | Reinforce Plate,Lock Ring-Right Rear Pillar | 1 |  | D | CA1020VR |  |
| 31 |  | 5401211-2E2 | 左前立柱上内板 | Upper Inner Plate,Left Front Pillar | 1 |  | D | CA1020VR |  |
| 32 |  | 5401212-2E2 | 右前立柱上内板 | Upper Inner Plate,Right Front Pillar | 1 |  | D | CA1020VR |  |
| 33 |  | 5401221-2E2 | 左前门框上内板 | Upper Inner Plate-Front Door Frame,Lh | 1 |  | D | CA1020VR |  |
| 34 |  | 5401222-2E2 | 右前门框上内板 | Upper Inner Plate,Front Door Frame,Rh | 1 |  | D | CA1020VR |  |
| 35 |  | 5401241-4E2 | 左中立柱上内板 | Upper Inner Plate,Left Middle Pillar | 1 |  | D | CA1020VR |  |
| 36 |  | 5401242-4E2 | 右中立柱上内板 | Upper Inner Plate,Right Middle Pillar | 1 |  | D | CA1020VR |  |
| 37 |  | 5401251-4E2 | 左后门框上内板 | Upper Inner Plate,Left Rear Door Frame | 1 |  | D | CA1020VR |  |
| 38 |  | 5401252-4E2 | 右后门框上内板 | Upper Inner Plate,Right Rear Door Frame | 1 |  | D | CA1020VR |  |
| 39 |  | 5401267-4E2 | 安全带左上固定板 | Left Upper Fixed Plate,Seat Belt | 1 |  | D | CA1020VR |  |
| 40 |  | 5401268-4E2 | 安全带右上固定板 | Right Upper Fixed Plate,Seat Belt | 1 |  | D | CA1020VR |  |
| 41 |  | 5401371-4E2 | 左后立柱内板 | Inner Plate,Left Rear Pillar | 1 |  | D | CA1020VR |  |
| 42 |  | 5401372-4E2 | 右后立柱内板 | Inner Plate,Right Rear Pillar | 1 |  | D | CA1020VR |  |
| 43 |  | 5401383-4E2 | 左边板锁钩加强板 | Reinforce Plate,Left Side Plate Lock Hook | 1 |  | D | CA1020VR |  |
| 44 |  | 5401384-4E2 | 右边板锁钩加强板 | Reinforce Plate,Right Side Plate Lock Hook | 1 |  | D | CA1020VR |  |
| 45 |  | 5402036-2E2 | 前门框装饰条 | Decorating Trap,Front Door Frame | 2 |  | C | CA1020VR |  |
| 46 |  | 5402046-V01 | 侧围扶手 | Handle Assy(Plastic), Side Plate | 3 |  | D | CA1020VR |  |
| 47 |  | 5402049-2E2 | 前车门下防撞块 | Bumper Block,Front Door | 4 |  | D | CA1020VR |  |
| 48 |  | 5402057-2E2 | 线束过孔胶堵 | Rubber Plug | 2 |  | C | CA1020VR |  |

| BODY- Front welded floor parts-Frame | SECTION. NO.:06-5101 | PAGE:195 |
| --- | --- | --- |
| BODY- Front welded floor parts-Frame | SECTION. NO.:06-5101 | PAGE:196 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 5101025-2E2 | 前地板分总成 | Front welded floor assembly | 1 |  | D |  |  |
| 2 |  | 5101065-2E2 | 左前内轮罩焊接总成 | Inner front left wheeling cover assy | 1 | Арка переднего колеса левая(ниша) | D |  |  |
| 3 |  | 5101070-2E2 | 右前内轮罩焊接总成 | Inner front right wheeling cover assy | 1 | Арка переднего колеса правая(ниша) | D |  |  |
| 4 |  | 5101165-2E2 | 发动机仓前板分总成 | Front plate assy,engine house | 1 |  | D |  |  |
| 5 |  | 5101170-2E2 | 前排座椅加强板焊接总成 | Reinforce plate,front seat | 4 |  | D |  |  |
| 6 |  | 5101185-2E2 | 发动机仓左侧板总成 | Left side plate,engine house | 1 |  | D |  |  |
| 7 |  | 5101190-2E2 | 发动机仓右侧板总成 | Right side plate,engine house | 1 | Щит моторного отсека | D |  |  |
| 8 |  | 5107211-2E2 | 发动机中盖板 | Middle engine cover plate | 1 | Панель рычага КПП (жесть металл) | C |  |  |
| 9 |  | 5107311-2E2 | 发动机后盖板 | Rear engine cover plate | 1 |  | C |  |  |
| 10 |  | 5107291-V01 | 地板胶堵1（橡胶件） | Plug I | 2 |  | C |  |  |
|  |  |  |  |  |  |  |  |  | 6371 |

| BODY- Truck bed-CA1020VR | SECTION. NO.:06-8500 | PAGE:197 |
| --- | --- | --- |
| BODY- Truck bed-CA1020VR | SECTION. NO.:06-8500 | PAGE:198 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 8501015-4E2 | 底板总成 | Bottom Plate Assembly,Truck Bed | 1 |  | D | CA1020VR |  |
| 2 |  | Q1461035 | 组合螺栓 | Combined Bolt | 10 |  | D | CA1020VR |  |
| 3 |  | Q1460825 | 组合螺栓 | Combined Bolt | 8 |  | D | CA1020VR |  |
| 4 |  | 8500011-4E2 | 车厢连接板 | Connecting Plate,Truck Bed | 2 |  | D | CA1020VR |  |
| 5 |  | 8500015-4E2 | 车厢焊接总成 | Truck Bed Welding Assembly | 1 |  | D | CA1020VR |  |
| 6 |  | 8503050-4E2 | 锁环总成 | Lock Ring Assembly,Truck Bed | 2 |  | D | CA1020VR |  |
| 7 |  | Q24008 | 十字槽沉头螺钉和锥形锁紧垫圈组合件 | Screw And Washer Complex | 4 |  | D | CA1020VR |  |
| 8 |  | 8503061-4E2 | 限位杆固定螺栓 | Fixed Bolt | 2 |  | D | CA1020VR |  |
| 9 |  | 8503055-4E2 | 后厢板开锁限位杆总成 | Limit Pole,Rear Plate,Truck Bed | 2 |  | D | CA1020VR |  |
| 10 |  | 8503023-4E2 | 后板内罩板 | Inner Cover,Rear Plate,Truck Bed | 1 |  | D | CA1020VR |  |
| 11 |  | Q23006 | 十字槽盘头螺钉和平垫圈组合件 | Screw And Washer Complex | 8 |  | D | CA1020VR |  |
| 12 |  | Q23006 | 十字槽盘头螺钉和平垫圈组合件 | Screw And Washer Complex | 2 |  | D | CA1020VR |  |
| 13 |  | 8503035-4E2 | 后板锁总成 | Rear Plate Lock Assembly | 1 |  | D | CA1020VR |  |
| 14 |  | Q24008 | 十字槽沉头螺钉和锥形锁紧垫圈组合件 | Screw And Washer Complex | 6 |  | D | CA1020VR |  |
| 15 |  | Q1460620 | 组合螺栓 | Combined Bolt | 4 |  | D | CA1020VR |  |
| 16 |  | 8511023-4E2 | 左后轮挡泥板胶板 | Rubber Plate,Left Rear Mudguard | 1 |  | B | CA1020VR |  |
| 17 |  | 8511024-4E2 | 右后轮挡泥板胶板 | Rubber Plate,Right Rear Mudguard | 1 |  | B | CA1020VR |  |

| BODY- Truck bed-CA1020V | SECTION. NO.:06-8500 | PAGE:199 |
| --- | --- | --- |
| BODY- Truck bed-CA1020V | SECTION. NO.:06-8500 | PAGE:200 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | Q1461035 | 组合螺栓 | Combined Bolt | 10 |  | D | CA1020V |  |
| 2 |  | 8500011-3E2 | 边板前锁钩 | Front Lock Hook,Side Plate,Truck Bed | 2 |  | D | CA1020V |  |
| 3 |  | Q1460825 | 组合螺栓 | Combined Bolt | 4 |  | D | CA1020V |  |
| 4 |  | 8502043-3E2 | 前堵盖 | Front Plug Cover | 3 |  | D | CA1020V |  |
| 5 |  | Q340B06 | 螺母 | Nut | 8 |  | D | CA1020V |  |
| 6 |  | 8501015-3E2 | 底板总成 | Bottom Plate,Truck Bed | 1 |  | D | CA1020V |  |
| 7 |  | 8502020-3E2 | 右边板焊接总成 | Right Side Plate Welding Assembly,Truck Bed | 1 | Борт задний правый | D | CA1020V |  |
| 8 |  | 8511024-6J6 | 右后轮挡泥板胶板 | Rubber Plate,Right Rear Mudguard | 1 |  | D | CA1020V |  |
| 9 |  | Q1460620 | 组合螺栓 | Combined Bolt | 2 |  | D | CA1020V |  |
| 10 |  | 8503010-3E2 | 后板焊接总成 | Rear Plate Welding Assembly,Truck Bed | 1 | Борт задний | D | CA1020V |  |
| 11 |  | 8502044-3E2 | 后堵盖 | Rear Plug Cover | 3 |  | D | CA1020V |  |
| 12 |  | Q43660 | 开口挡圈 | Cotter Washer | 3 |  | D | CA1020V |  |
| 13 |  | Q1460620 | 组合螺栓 | Combined Bolt | 2 |  | D | CA1020V |  |
| 14 |  | 8511023-6J6 | 左后轮挡泥板胶板 | Rubber Plate,Left Rear Mudguard | 1 | Брызговик заднего колеса (резина) | D | CA1020V |  |
| 15 |  | 8502015-3E2 | 左边板焊接总成 | Left Side Plate Welding Assembly,Truck Bed | 1 | Борт задний левый | D | CA1020V |  |
| 16 |  | Q340B10 | 螺母 | Nut | 2 |  | D | CA1020V |  |
| 17 |  | 8502110-3E2 | 边板锁总成 | Side Plate Lock Assembly,Truck Bed | 4 | Запор бортов (боковых,заднего) | D | CA1020V |  |
| 18 |  | Q1460616 | 组合螺栓 | Combined Bolt | 8 |  | D | CA1020V |  |
| 19 |  | Q2140630 | 十字槽平圆头螺钉 | Screw | 6 |  | D | CA1020V |  |
| 20 |  | 8500031-6J6 | 缓冲块 | Cushion | 6 |  | D | CA1020V |  |

| BODY- Truck bed-CA1020VRL | SECTION. NO.:06-8500 | PAGE:201 |
| --- | --- | --- |
| BODY- Truck bed-CA1020VRL | SECTION. NO.:06-8500 | PAGE:202 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | Q1461035 | 组合螺栓 | Combined Bolt | 10 |  | D | CA1020VRL |  |
| 2 |  | 8500011-3E2 | 边板前锁钩 | Front Lock Hook,Side Plate,Truck Bed | 2 |  | D | CA1020VRL |  |
| 3 |  | Q1460825 | 组合螺栓 | Combined Bolt | 4 |  | D | CA1020VRL |  |
| 4 |  | 8502043-3E2 | 前堵盖 | Front Plug Cover | 3 |  | D | CA1020VRL |  |
| 5 |  | Q340B06 | 螺母 | Nut | 8 |  | D | CA1020VRL |  |
| 6 |  | 8501015-4E3 | 底板总成 | Bottom Plate,Truck Bed | 1 |  | D | CA1020VRL |  |
| 7 |  | 8502020-4E3 | 右边板焊接总成 | Right Side Plate Welding Assembly,Truck Bed | 1 |  | D | CA1020VRL |  |
| 8 |  | 8511024-6J6 | 右后轮挡泥板胶板 | Rubber Plate,Right Rear Mudguard,Truck Bed | 1 |  | D | CA1020VRL |  |
| 9 |  | Q1460620 | 组合螺栓 | Combined Bolt | 2 |  | D | CA1020VRL |  |
| 10 |  | 8503010-3E2 | 后板焊接总成 | Rear Plate Welding Assembly,Truck Bed | 1 |  | D | CA1020VRL |  |
| 11 |  | 8502044-3E2 | 后堵盖 | Rear Plug Cover | 3 |  | D | CA1020VRL |  |
| 12 |  | Q43660 | 开口挡圈 | Cotter Washer | 3 |  | D | CA1020VRL |  |
| 13 |  | Q1460620 | 组合螺栓 | Combined Bolt | 2 |  | D | CA1020VRL |  |
| 14 |  | 8511023-6J6 | 左后轮挡泥板胶板 | Rubber Plate,Left Rear Mudguard | 1 |  | D | CA1020VRL |  |
| 15 |  | 8502015-4E3 | 左边板焊接总成 | Left Side Plate Welding Assembly | 1 |  | D | CA1020VRL |  |
| 16 |  | Q340B10 | 螺母 | Nut | 2 |  | D | CA1020VRL |  |
| 17 |  | 8502110-3E2 | 边板锁总成 | Side Plate Lock Assembly,Truck Bed | 4 |  | D | CA1020VRL |  |
| 18 |  | Q1460616 | 组合螺栓 | Combined Bolt | 8 |  | D | CA1020VRL |  |
| 19 |  | Q2140630 | 十字槽平圆头螺钉 | Screw | 6 |  | D | CA1020VRL |  |
| 20 |  | 8500031-6J6 | 缓冲块 | Cushion | 6 |  | D | CA1020VRL |  |

| Miscellaneous-Brand & Logo | SECTION. NO:07-3921 | PAGE:203 |
| --- | --- | --- |
| Miscellaneous- Brand & Logo | SECTION. NO:07-3921 | PAGE:204 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3921016-A1 | FAW 商标 | FAW BRAND | 1 |  | D |  | OPTIONAL |
| 2 |  | 8401016-2E2 | 一汽标志 | FAW LOGO | 1 |  | C |  |  |
| 3 |  | 8202020-2E2 | 右外后视镜总成 | Outerside mirror,RH | 1 |  | C |  |  |
| 4 |  | 8202015-2E2 | 左外后视镜总成 | Outerside mirror,LH | 1 |  | C |  |  |

| Miscellaneous- Key Set & Blank Key | SECTION. NO:07-3704 | PAGE:205 |
| --- | --- | --- |
| Miscellaneous- Key Set & Blank Key | SECTION. NO:07-3704 | PAGE:206 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1，2 |  | 3704901-2E2 | 点火开关、全车锁芯工艺合件 | Ignition Switch,all vehicle keys and all door lock core | 1 |  | C | СМ .6371 |  |
| 3 |  | 3704020-00 | 空白钥匙 | Blank Key | 1 |  | C | СМ6371 |  |

| Miscellaneous-Tool Kit | SECTION. NO:07-3919 | PAGE:207 |
| --- | --- | --- |
| Miscellaneous-Tool Kit | SECTION. NO:07-3919 | PAGE:208 |
| Key No. | Part Number | Part description in Chinese | Part description in English | QTY | Unit package | Class | Applied model | remark |
| 1 |  | 3919035-2E2 | 工具装袋总成 | Tool bag with all the tools | 1 |  | D |  |  |
| 2 |  |  | 开口扳手8×10 | Open end wrench 8 X 10 | 1 |  | D |  |  |
| 3 |  |  | 开口扳手12×14 | Open end wrench 12 X 14 | 1 |  | D |  |  |
| 4 |  |  | 开口扳手13×16 | Open end wrench 13 X 16 | 1 |  | D |  |  |
| 5 |  |  | 两用旋具 | Dual purpose screw driver | 1 |  | D |  |  |
| 6 |  |  | 旋具手柄 | Screw driver lever | 1 |  | D |  |  |
| 7 |  |  | 鲤鱼钳 | Slip joint pliers | 1 |  | D |  |  |
| 8 |  |  | 套筒扳手——火花塞用 | Socket wrench--used for spark plug | 1 |  | D |  |  |
| 9 |  |  | 柄——火花塞套筒扳手 | Lever--spark plug socket wrench | 1 |  | D |  |  |
| 10 |  |  | 四方头扳手 | Square wrench | 1 |  | D |  |  |
| 11 |  |  | 车轮扳手 | Wheel wrench | 1 |  | D |  |  |
| 12 |  | 3913030-A1 | 千斤顶 | Jack | 1 |  | D |  |  |
| 13 |  |  | 千斤顶手柄 | Jack lever | 1 |  | D |  |  |
|  |  | SF10W30 | 机油 | engine oil 10W 30 | 3KG |  | B |  |  |

# Text boxes

0

7

7

17，18

| Production name | CA1020V Series FAW MINI TRUCK |
| --- | --- |
| DIMENSIONS |
| Exterior dimensions(L×W×H) mm | 4260×1475×1890 |
| Wheel base mm | 2550 |
| Treads(F/R) mm | 1280/1290 |
| Ground clearance mm | 156(rear axle shaft tube) |
| Seating capacity persons | 2 |
| Max. Speed Km/h | 100(970cc) |
| Max. gradability % | 29 |
| Angles(Approach/Departure) | 27.°/ 29° |
| Brake distance at 80 Km/h m | <57.2 |
| Turning circles semi-meters m | 5 |
| Fuel consumption at L/100Km | 6.0(50Km/h) |
| MODEL | CA1020V |
| WEIGHT |
| Curb vehicle weight Kg | 865 |
| Gross vehicle weight Kg | 1795 |
| Weight distribution(loaded) Kg | 825kg/970kg |
| Weight distribution (unloaded) Kg | 510kg/355Kg |
| ENGINE |  |
| Model,Cylinders | JB465Q-1AE1,L4,OHC EFI |  |
| Displacement ml/fuel | 1051/Gasoline |  |
| Bore×Stroke mm×mm | 65.5×78 |  |
| Compression ratio | 9 |  |
| Max.Power W(r/min) | 38.5（5200） |  |
| Max.torque N.m(r/min) | 83（3000-3500） |  |
| Type | 5MT,synchromesh |  |
| Gear tatio 1st | 3.652 |  |
| 2nd | 1.947 |  |
| 3rd | 1.423 |  |
| 4th | 1 |  |
| 5th | 0.795 |  |
| Reverse | 3.466 |  |
| Final gear ratio | 5.125 |
| Clutch system | Single-plate,Diaphragm spring clutch |
| CHASSIS |
| Steering | Rack & pinion |
| Braking system | Dual hydraulic brake system,Disc brake(F),Drum brake(R) |
| Suspension | Front | Strut & Coil spring |
|  | Rear | Semi-oval leaf spring |
| Drive train | 4×2MR 5.125 |
| Tires size | 165/70 R13 |
| CAPACITY |
| Fuel tank capacity litre |

3

4

2

1

1

2

3

4

5

6

7

9

5

1

4

3

2

9

9

8

9

6

7

15

14

7

8

9

10

11

12

13

5

6

3

4

2

1

15

14

13

12

11

10

9

4

5

3

1、2

3

2

2

1

16

8

7

6

5

3

3

2

1

4

9

6

8

18

13

16

5

17

3

11

15

3

2

1

1

10，11

3

12

10

14

7

1

2

1

2

3

4

5

6

16

15

11

9

1

8

6

6

13

12

7

14

10

9

8

6

6

5

4

3

2

1

1

2

3

4

5

6

7

8

11

10

9

12

15

16

14

13

15

17

1

5

4

3

2

9

8

7

6

11

12

10

17

16

13

15

14

20

19

18

18

19

20

14

15

13

16

17

10

12

11

6

7

8

9

2

3

4

5

1